## Slide 1: Deep Learning of Dynamics Dynamics of Deep Learning
Ján Drgoňa Collaborators: Aaron Tuor, Elliott Skomski, Soumya Vasisht, Draguna Vrabie
Pacific Northwest National Laboratory
DnC2S meeting January 15, 2021

## Slide 2: Physics-based Modeling of Dynamical Systems
Differential equations
Difference equations
Issues:
Hard/expensive to obtain
Some are hard to solve
Discretization methods
Types:
Non-autonomous
Partially observable
Problems:
Initial value problem
Boundary value problem
Parameter/state estimation
Sensitivity analysis
Optimal control
Methods:
Euler discretization
Runge Kutta
Linear multistep
Predictor-corrector
Shooting methods
Notes: Use cases for accurate systems models
    Scientific discovery
    Support strategic decisions in dynamic environments
    Predictive maintenance
    Predictive control
Physics-based modeling infeasible for many critical real-world systems
    Missing information of underlying system dynamics
    Incomplete awareness of model state-space
    Limitations on available operational data
    Sometimes difficult to get real time simulations
Purely data driven approaches are unsuitable
    Poor sampling efficiency due to limited observational data
    Black box models lack operational safety guarantees

## Slide 3: Data-driven Modeling of Dynamical Systems
Time-series data
Difference equations
System identification
State space models
Markov models
NARX models
Recurrent neural nets
Issues:
Data efficiency
Generalization
Accuracy and UQ
Stability and Convergence
Notes: Use cases for accurate systems models
    Scientific discovery
    Support strategic decisions in dynamic environments
    Predictive maintenance
    Predictive control
Physics-based modeling infeasible for many critical real-world systems
    Missing information of underlying system dynamics
    Incomplete awareness of model state-space
    Limitations on available operational data
    Sometimes difficult to get real time simulations
Purely data driven approaches are unsuitable
    Poor sampling efficiency due to limited observational data
    Black box models lack operational safety guarantees

## Slide 4: Constrained Deep Neural State Space Models
  ML models that respect constraints by
    Structured architectures
    Penalties as auxiliary loss function terms
    Structured linear maps
    More structure = improved well-posedness
  Elliott Skomski, Jan Drgona, Aaron Tuor Physics-Informed Neural State Space Models via Learning and Evolution, https://arxiv.org/abs/2011.13497
  Aaron R Tuor, Ján Drgona, Draguna L Vrabie Constrained Neural Ordinary Differential Equations with Stability Guarantees, https://arxiv.org/abs/2004.10883 Code release: https://github.com/pnnl/neural_ODE_ICLR2020
Notes: We present a generalized family of neural state space model architectures constrained block-structured nonlinear neural state space models.
Our approach combines the benefits of classical system identification techniques with the advances in constrained deep learning to learn deep structured models.
In particular, we build modular representations of nonlinear systems with identifiable neuralmodules that may be constrained and influenced by structuralpriors. This allows for inclusion of stability constraints through eigenvalue regularizations of the network weights,state and input constraints, and other boundary conditionconstraints.

## Slide 5: Structured Linear Maps with Eigenvalue Constraints
SVD factorization
Hamiltonian weight
  Jiong Zhang, et al., Stabilizing Gradients for Deep Neural Networks via Efficient SVD Parameterization, 2018. Eldad Haber and Lars Ruthotto, Stable Architectures for Deep Neural Networks 2017 Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics, arXiv:2011.13492

## Slide 6: Constraint Penalties
Output bounds
Input dynamics bounds
Predicted State Smoothing
+

## Slide 7: Multi-objective loss term
N-step prediction MSE
Linear map regularization
State smoothing
Input influence constraints
Output constraints

## Slide 8: Uncertainty Quantification for Deep Neural State Space Models
Preliminary results show correlation between uncertainty estimate and prediction error
Monte-Carlo Dropout
Ensembling
BNN

## Slide 9: Application: Learning Thermal Dynamics of Multi-zone Building
  Jan Drgona, Aaron R. Tuor, Vikas Chandan, Draguna L. Vrabie, Physics-constrained Deep Learning of Multi-zone Building Thermal Dynamics, CCAI Workshop NeurIPS 2020, https://arxiv.org/abs/2011.05987

## Slide 10: Differentiable Predictive Control of Unknown Dynamical Systems
Step 1: System identification
Step 2: Policy optimization by model differentiation
Notes: Use cases for accurate systems models
    Scientific discovery
    Support strategic decisions in dynamic environments
    Predictive maintenance
    Predictive control
Physics-based modeling infeasible for many critical real-world systems
    Missing information of underlying system dynamics
    Incomplete awareness of model state-space
    Limitations on available operational data
    Sometimes difficult to get real time simulations
Purely data driven approaches are unsuitable
    Poor sampling efficiency due to limited observational data
    Black box models lack operational safety guarantees

## Slide 11: Connections of DPC with Model Predictive Control
Formulation of MPC problem as a constrained deep learning model
  Jan Drgona, Aaron Tuor, Draguna Vrabie, Constrained Physics-Informed Deep Learning for Stable System Identification and Control of Linear Systems, Code release: https://github.com/pnnl/deps_arXiv2020

## Slide 12: Physics Informed DPC of Unknown Linear System
Closed loop trajectories. Top: controlled state (orange), internal model predictions (blue), given reference (dashed blue), and constraints (dashed black). Middle: control action (blue) and bounds (dashed black). Bottom: disturbances
Control performance comparison in simulations with parametric and additive uncertainties. Control Strategies: MPC, Robust MPC , Stochastic MPC, LQR, LQI, A2C: Asynchronous, deterministic variant of Advantage Actor Critic, ACKTR: Actor Critic using Kronecker-Factored Trust Region, PPO2: Proximal Policy Optimization
  Jan Drgona, Aaron Tuor, Draguna Vrabie, Constrained Physics-Informed Deep Learning for Stable System Identification and Control of Linear Systems, Code release: https://github.com/pnnl/deps_arXiv2020

## Slide 13: DPC of a Real Unknown Nonlinear System
Energy Data Analytics Symposium
  Jan Drgona, Karol Kis, Aaron Tuor, Draguna Vrabie, Martin Klauco,
  Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, preprint, 2020​ https://arxiv.org/abs/2011.03699​
Solution of optimal control problems for unknown nonlinear systems​
Constrained model-based neural policies with physically plausible outcomes​
Tracking dynamic references and avoiding dynamic constraints
Real-time control application on an embedded hardware​
Favorable control performance and scalability comparison with MPC​

## Slide 14: Dynamical Analysis of Deep Neural Networks

## Slide 15: Dynamical Analysis of Deep Neural Networks
Motivation
  Safety-critical and high-performance systems call for formal verification methods to ensure safe operation.
  Lack of guarantees on global and local behavior of DNNs still remain limiting factors.
  Properties like stability and robustness are crucial for reliable system identification and control.
Goal
  Apply system- and control-theoretic analysis methods on DNNs.
  Provide stability guarantees, identify state space regions and achieve desired dynamical behavior with DNNs.
Notes: The presentation I’m giving today is for a data-driven method for dynamics modeling.
We should care about this because people interact with and depend on complicated systems all the time.
Greater understanding of these systems can lead to outcomes which are
More energy efficient
Cost effective
Conducive to human life
Having an accurate model of a system enables scientific discovery,
Can provide critical information to support high stakes decisions in changing environments
Or to provide necessary information for predictive maintenance of high value equipment, avoiding costly and potentially dangerous equipment
Failures.
One of the most common and lucrative uses of systems models are for predictive control in manufacturing and other large scale enterprises.
I’m presenting a method today which bridges benefits of traditional physics-based modeling with more recent data-driven modeling using deep learning
Traditional physics-based modeling works very well and is widely used in many real world applications. However, it can’t always be applied to every situation.
missing information
incomplete awareness of the model state space.
limitations on the available operational data.
For large scale systems, not only are they difficult to model from first principles, it is also not always possible to simulate the system in real time.
Data-driven approaches for systems modeling are an alternative in these situations but can come with their own disadvantages.
Can take a lot of data to train and may behave unpredictably outside the distribution of training data in unobserved regions of the system state space.
In addition, modern neural network approaches don’t typically provide constraints enforcement within physically realizable and operationally safe bounds,

## Slide 16: Spectral Analysis and Stability of Deep Neural Networks
Novel characterization that views deep neural networks (DNNs) from a dynamical systems perspective.
Jacobians of DNNs as pointwise parameter-varying affine maps.
At every point , the neural network, may be represented as
where represent the weight parameterizations at layer , and is a diagonal matrix that represents the element-wise application of the nonlinear activation function at layer .
  Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics.
Notes: The presentation I’m giving today is for a data-driven method for dynamics modeling.
We should care about this because people interact with and depend on complicated systems all the time.
Greater understanding of these systems can lead to outcomes which are
More energy efficient
Cost effective
Conducive to human life
Having an accurate model of a system enables scientific discovery,
Can provide critical information to support high stakes decisions in changing environments
Or to provide necessary information for predictive maintenance of high value equipment, avoiding costly and potentially dangerous equipment
Failures.
One of the most common and lucrative uses of systems models are for predictive control in manufacturing and other large scale enterprises.
I’m presenting a method today which bridges benefits of traditional physics-based modeling with more recent data-driven modeling using deep learning
Traditional physics-based modeling works very well and is widely used in many real world applications. However, it can’t always be applied to every situation.
missing information
incomplete awareness of the model state space.
limitations on the available operational data.
For large scale systems, not only are they difficult to model from first principles, it is also not always possible to simulate the system in real time.
Data-driven approaches for systems modeling are an alternative in these situations but can come with their own disadvantages.
Can take a lot of data to train and may behave unpredictably outside the distribution of training data in unobserved regions of the system state space.
In addition, modern neural network approaches don’t typically provide constraints enforcement within physically realizable and operationally safe bounds,

## Slide 17: Stability Theorem for Deep Neural Networks
  Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics, arXiv:2011.13492
Notes: The presentation I’m giving today is for a data-driven method for dynamics modeling.
We should care about this because people interact with and depend on complicated systems all the time.
Greater understanding of these systems can lead to outcomes which are
More energy efficient
Cost effective
Conducive to human life
Having an accurate model of a system enables scientific discovery,
Can provide critical information to support high stakes decisions in changing environments
Or to provide necessary information for predictive maintenance of high value equipment, avoiding costly and potentially dangerous equipment
Failures.
One of the most common and lucrative uses of systems models are for predictive control in manufacturing and other large scale enterprises.
I’m presenting a method today which bridges benefits of traditional physics-based modeling with more recent data-driven modeling using deep learning
Traditional physics-based modeling works very well and is widely used in many real world applications. However, it can’t always be applied to every situation.
missing information
incomplete awareness of the model state space.
limitations on the available operational data.
For large scale systems, not only are they difficult to model from first principles, it is also not always possible to simulate the system in real time.
Data-driven approaches for systems modeling are an alternative in these situations but can come with their own disadvantages.
Can take a lot of data to train and may behave unpredictably outside the distribution of training data in unobserved regions of the system state space.
In addition, modern neural network approaches don’t typically provide constraints enforcement within physically realizable and operationally safe bounds,

## Slide 18: Dynamical Effects of Weights
  Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics, arXiv:2011.13492
Notes: The presentation I’m giving today is for a data-driven method for dynamics modeling.
We should care about this because people interact with and depend on complicated systems all the time.
Greater understanding of these systems can lead to outcomes which are
More energy efficient
Cost effective
Conducive to human life
Having an accurate model of a system enables scientific discovery,
Can provide critical information to support high stakes decisions in changing environments
Or to provide necessary information for predictive maintenance of high value equipment, avoiding costly and potentially dangerous equipment
Failures.
One of the most common and lucrative uses of systems models are for predictive control in manufacturing and other large scale enterprises.
I’m presenting a method today which bridges benefits of traditional physics-based modeling with more recent data-driven modeling using deep learning
Traditional physics-based modeling works very well and is widely used in many real world applications. However, it can’t always be applied to every situation.
missing information
incomplete awareness of the model state space.
limitations on the available operational data.
For large scale systems, not only are they difficult to model from first principles, it is also not always possible to simulate the system in real time.
Data-driven approaches for systems modeling are an alternative in these situations but can come with their own disadvantages.
Can take a lot of data to train and may behave unpredictably outside the distribution of training data in unobserved regions of the system state space.
In addition, modern neural network approaches don’t typically provide constraints enforcement within physically realizable and operationally safe bounds,

## Slide 19: Dynamical Effects of Activation Functions
  Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics, arXiv:2011.13492
Notes: The presentation I’m giving today is for a data-driven method for dynamics modeling.
We should care about this because people interact with and depend on complicated systems all the time.
Greater understanding of these systems can lead to outcomes which are
More energy efficient
Cost effective
Conducive to human life
Having an accurate model of a system enables scientific discovery,
Can provide critical information to support high stakes decisions in changing environments
Or to provide necessary information for predictive maintenance of high value equipment, avoiding costly and potentially dangerous equipment
Failures.
One of the most common and lucrative uses of systems models are for predictive control in manufacturing and other large scale enterprises.
I’m presenting a method today which bridges benefits of traditional physics-based modeling with more recent data-driven modeling using deep learning
Traditional physics-based modeling works very well and is widely used in many real world applications. However, it can’t always be applied to every situation.
missing information
incomplete awareness of the model state space.
limitations on the available operational data.
For large scale systems, not only are they difficult to model from first principles, it is also not always possible to simulate the system in real time.
Data-driven approaches for systems modeling are an alternative in these situations but can come with their own disadvantages.
Can take a lot of data to train and may behave unpredictably outside the distribution of training data in unobserved regions of the system state space.
In addition, modern neural network approaches don’t typically provide constraints enforcement within physically realizable and operationally safe bounds,

## Slide 20: Dynamical Effects of Bias Terms
  Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics, arXiv:2011.13492
Bias terms in generic DNNs do not affect the dynamical properties such as eigenvalues, stability, or convergence. Instead, biases uniquely define the centroid of attractors confined in the compact subspace of the state space. Therefore, we posit that dynamical properties are uniquely defined by the network’s weights and activation functions.
Notes: The presentation I’m giving today is for a data-driven method for dynamics modeling.
We should care about this because people interact with and depend on complicated systems all the time.
Greater understanding of these systems can lead to outcomes which are
More energy efficient
Cost effective
Conducive to human life
Having an accurate model of a system enables scientific discovery,
Can provide critical information to support high stakes decisions in changing environments
Or to provide necessary information for predictive maintenance of high value equipment, avoiding costly and potentially dangerous equipment
Failures.
One of the most common and lucrative uses of systems models are for predictive control in manufacturing and other large scale enterprises.
I’m presenting a method today which bridges benefits of traditional physics-based modeling with more recent data-driven modeling using deep learning
Traditional physics-based modeling works very well and is widely used in many real world applications. However, it can’t always be applied to every situation.
missing information
incomplete awareness of the model state space.
limitations on the available operational data.
For large scale systems, not only are they difficult to model from first principles, it is also not always possible to simulate the system in real time.
Data-driven approaches for systems modeling are an alternative in these situations but can come with their own disadvantages.
Can take a lot of data to train and may behave unpredictably outside the distribution of training data in unobserved regions of the system state space.
In addition, modern neural network approaches don’t typically provide constraints enforcement within physically realizable and operationally safe bounds,

## Slide 21: Dynamical Effects of Network Depth
  Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics, arXiv:2011.13492
Unstable layers imply exploding gradient problem
Exponentially stable layers with
small eigenvalues imply
vanishing gradient problem
Network with energy conversion prevents gradient problems
Notes: The presentation I’m giving today is for a data-driven method for dynamics modeling.
We should care about this because people interact with and depend on complicated systems all the time.
Greater understanding of these systems can lead to outcomes which are
More energy efficient
Cost effective
Conducive to human life
Having an accurate model of a system enables scientific discovery,
Can provide critical information to support high stakes decisions in changing environments
Or to provide necessary information for predictive maintenance of high value equipment, avoiding costly and potentially dangerous equipment
Failures.
One of the most common and lucrative uses of systems models are for predictive control in manufacturing and other large scale enterprises.
I’m presenting a method today which bridges benefits of traditional physics-based modeling with more recent data-driven modeling using deep learning
Traditional physics-based modeling works very well and is widely used in many real world applications. However, it can’t always be applied to every situation.
missing information
incomplete awareness of the model state space.
limitations on the available operational data.
For large scale systems, not only are they difficult to model from first principles, it is also not always possible to simulate the system in real time.
Data-driven approaches for systems modeling are an alternative in these situations but can come with their own disadvantages.
Can take a lot of data to train and may behave unpredictably outside the distribution of training data in unobserved regions of the system state space.
In addition, modern neural network approaches don’t typically provide constraints enforcement within physically realizable and operationally safe bounds,

## Slide 22: Attractors of Deep Neural Networks
  Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics, arXiv:2011.13492
Notes: The presentation I’m giving today is for a data-driven method for dynamics modeling.
We should care about this because people interact with and depend on complicated systems all the time.
Greater understanding of these systems can lead to outcomes which are
More energy efficient
Cost effective
Conducive to human life
Having an accurate model of a system enables scientific discovery,
Can provide critical information to support high stakes decisions in changing environments
Or to provide necessary information for predictive maintenance of high value equipment, avoiding costly and potentially dangerous equipment
Failures.
One of the most common and lucrative uses of systems models are for predictive control in manufacturing and other large scale enterprises.
I’m presenting a method today which bridges benefits of traditional physics-based modeling with more recent data-driven modeling using deep learning
Traditional physics-based modeling works very well and is widely used in many real world applications. However, it can’t always be applied to every situation.
missing information
incomplete awareness of the model state space.
limitations on the available operational data.
For large scale systems, not only are they difficult to model from first principles, it is also not always possible to simulate the system in real time.
Data-driven approaches for systems modeling are an alternative in these situations but can come with their own disadvantages.
Can take a lot of data to train and may behave unpredictably outside the distribution of training data in unobserved regions of the system state space.
In addition, modern neural network approaches don’t typically provide constraints enforcement within physically realizable and operationally safe bounds,

## Slide 23: Attractors of Deep Neural Networks
  Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics, arXiv:2011.13492
Notes: The presentation I’m giving today is for a data-driven method for dynamics modeling.
We should care about this because people interact with and depend on complicated systems all the time.
Greater understanding of these systems can lead to outcomes which are
More energy efficient
Cost effective
Conducive to human life
Having an accurate model of a system enables scientific discovery,
Can provide critical information to support high stakes decisions in changing environments
Or to provide necessary information for predictive maintenance of high value equipment, avoiding costly and potentially dangerous equipment
Failures.
One of the most common and lucrative uses of systems models are for predictive control in manufacturing and other large scale enterprises.
I’m presenting a method today which bridges benefits of traditional physics-based modeling with more recent data-driven modeling using deep learning
Traditional physics-based modeling works very well and is widely used in many real world applications. However, it can’t always be applied to every situation.
missing information
incomplete awareness of the model state space.
limitations on the available operational data.
For large scale systems, not only are they difficult to model from first principles, it is also not always possible to simulate the system in real time.
Data-driven approaches for systems modeling are an alternative in these situations but can come with their own disadvantages.
Can take a lot of data to train and may behave unpredictably outside the distribution of training data in unobserved regions of the system state space.
In addition, modern neural network approaches don’t typically provide constraints enforcement within physically realizable and operationally safe bounds,

## Slide 24: Jacobians of Deep Neural Networks
Notes: The presentation I’m giving today is for a data-driven method for dynamics modeling.
We should care about this because people interact with and depend on complicated systems all the time.
Greater understanding of these systems can lead to outcomes which are
More energy efficient
Cost effective
Conducive to human life
Having an accurate model of a system enables scientific discovery,
Can provide critical information to support high stakes decisions in changing environments
Or to provide necessary information for predictive maintenance of high value equipment, avoiding costly and potentially dangerous equipment
Failures.
One of the most common and lucrative uses of systems models are for predictive control in manufacturing and other large scale enterprises.
I’m presenting a method today which bridges benefits of traditional physics-based modeling with more recent data-driven modeling using deep learning
Traditional physics-based modeling works very well and is widely used in many real world applications. However, it can’t always be applied to every situation.
missing information
incomplete awareness of the model state space.
limitations on the available operational data.
For large scale systems, not only are they difficult to model from first principles, it is also not always possible to simulate the system in real time.
Data-driven approaches for systems modeling are an alternative in these situations but can come with their own disadvantages.
Can take a lot of data to train and may behave unpredictably outside the distribution of training data in unobserved regions of the system state space.
In addition, modern neural network approaches don’t typically provide constraints enforcement within physically realizable and operationally safe bounds,

## Slide 25: Nonlinearity of Deep Neural Networks
ReLU
Identity
Sigmoid
SoftExponential
SoftExponential
Sigmoid
Identity
ReLU
Notes: The presentation I’m giving today is for a data-driven method for dynamics modeling.
We should care about this because people interact with and depend on complicated systems all the time.
Greater understanding of these systems can lead to outcomes which are
More energy efficient
Cost effective
Conducive to human life
Having an accurate model of a system enables scientific discovery,
Can provide critical information to support high stakes decisions in changing environments
Or to provide necessary information for predictive maintenance of high value equipment, avoiding costly and potentially dangerous equipment
Failures.
One of the most common and lucrative uses of systems models are for predictive control in manufacturing and other large scale enterprises.
I’m presenting a method today which bridges benefits of traditional physics-based modeling with more recent data-driven modeling using deep learning
Traditional physics-based modeling works very well and is widely used in many real world applications. However, it can’t always be applied to every situation.
missing information
incomplete awareness of the model state space.
limitations on the available operational data.
For large scale systems, not only are they difficult to model from first principles, it is also not always possible to simulate the system in real time.
Data-driven approaches for systems modeling are an alternative in these situations but can come with their own disadvantages.
Can take a lot of data to train and may behave unpredictably outside the distribution of training data in unobserved regions of the system state space.
In addition, modern neural network approaches don’t typically provide constraints enforcement within physically realizable and operationally safe bounds,

## Slide 26: Ongoing Work and Vision

## Slide 27: Ongoing Work and Vision
Open-source code
  PSL: Python Systems Library
    https://github.com/pnnl/psl
  SLiM: Structured Linear Maps in Pytorch
    https://github.com/pnnl/slim
  NeuroMANCER: Neural Modules with Adaptive Nonlinear Constraints and Efficient Regularizations
    https://github.com/pnnl/neuromancer
FY21 ongoing work
  Uncertainty Quantification
  User-friendly software API which follows the idioms of ML and Control
  Comprehensive suite of physics-based priors and constraints
  Theoretical guarantees: convergence, stability, constraints satisfaction

## Slide 28: Research Ideas for DnC2S
T1 Modeling
Stability, invertibility and improved inference via regularizations
  Deep Markov models
  Deep POMDPs
  Graph neural networks
  Deep PGMs
T2 UQ
Robustness of deep neural nets and deep PGMs
  Lipschitz constants
  Reachability analysis
  Sensitivity to perturbations
T3 Control
Probabilistic differentiable predictive control (DPC)
Closed loop stability and constraints satisfaction of POMDPs with neural networks
DPC as a policy optimization step for deep RL
T4 Continual Learning
Adaptive DPC policy updates with constraints and stability guarantees

## Slide 29: Backup slides and references

## Slide 30: Selected Reading: Dynamical Systems and Deep Learning
Differential equation solvers as part of DNN architectures
Ricky T. Q. Chen, et al., Neural Ordinary Differential Equations, 2018.
Eldad Haber and Lars Ruthotto, Deep Neural Networks motivated by Partial Differential Equations, 2018.
M. Raissi, et al., Multistep Neural Networks for Data-driven Discovery of Nonlinear Dynamical Systems, 2018.
Michael Poli, et al., TorchDyn: A Neural Differential Equations Library, 2020.
DiffEqFlux.jl – A Julia Library for Neural Differential Equations https://julialang.org/blog/2019/01/fluxdiffeq/
Using deep neural networks for solving differential equations
M Raissi, et al., Physics Informed Deep Learning: Data-driven Solutions of Nonlinear Partial Differential Equations, 2017.
Batuhan Güler, et al., Towards Robust and Stable Deep Learning Algorithms for Forward Backward Stochastic Differential Equations, 2019.
Deep neural operators for approximating differential equations
Zongyi Li , et al., Fourier Neural Operator for Parametric Partial Differential Equations, 2020.
Lu Lu, et al., DeepONet: Learning nonlinear operators for identifying differential equations based on the universal approximation theorem of operators, 2020
Notes: Use cases for accurate systems models
    Scientific discovery
    Support strategic decisions in dynamic environments
    Predictive maintenance
    Predictive control
Physics-based modeling infeasible for many critical real-world systems
    Missing information of underlying system dynamics
    Incomplete awareness of model state-space
    Limitations on available operational data
    Sometimes difficult to get real time simulations
Purely data driven approaches are unsuitable
    Poor sampling efficiency due to limited observational data
    Black box models lack operational safety guarantees

## Slide 31: Selected Reading: Dynamical Systems and Deep Learning
Deep learning for domain decomposition and Koopman operators
Bethany Lusch, et al., Deep learning for universal linear embeddings of nonlinear dynamics, 2018.
Enoch Yeung, et al., Learning Deep Neural Network Representations for Koopman Operators of Nonlinear Dynamical Systems, 2019.
Kathleen Champion, et al., Data-driven discovery of coordinates and governing equations, 2019.
Combining graph neural nets and physics constraints
Peter W. Battaglia, et al., Interaction Networks for Learning about Objects, Relations and Physics, 2016.
Alvaro Sanchez-Gonzalez, et al., Hamiltonian Graph Networks with ODE Integrators, 2019.
Sungyong Seo, Differentiable Physics-informed Graph Networks, 2019.
Combining deep learning and state space models
Olalekan Ogunmolu, et al., Nonlinear Systems Identification Using Deep Dynamic Neural Networks, 2016.
Rahul G. Krishnan, et al., Structured Inference Networks for Nonlinear State Space Models, 2016.
Syama Sundar Rangapuram, et al., Deep State Space Models for Time Series Forecasting, 2018.
Daniel Gedon, et al., Deep State Space Models for Nonlinear System Identification, 2020.
Notes: Use cases for accurate systems models
    Scientific discovery
    Support strategic decisions in dynamic environments
    Predictive maintenance
    Predictive control
Physics-based modeling infeasible for many critical real-world systems
    Missing information of underlying system dynamics
    Incomplete awareness of model state-space
    Limitations on available operational data
    Sometimes difficult to get real time simulations
Purely data driven approaches are unsuitable
    Poor sampling efficiency due to limited observational data
    Black box models lack operational safety guarantees

## Slide 32: Literature on Stability of Deep Neural Networks
Symmetric Structural Assumptions
  Eldad Haber and Lars Ruthotto, Stable Architectures for Deep Neural Networks 2017.
  Sam Greydanus, et al., Hamiltonian Neural Networks, 2019.
  Miles Cranmer, et al., Lagrangian Neural Networks, 2020.
Lyapunov-based Stability Analysis: contraction towards stationary point
  S. M. Richards, et al., The Lyapunov Neural Network: Adaptive Stability Certification for Safe Learning of Dynamic Systems, 2018.
  Gaurav Manek, and Zico Kolter, Learning Stable Deep Dynamics Models, 2019.
  Ya-Chien Chang, et al., Neural Lyapunov Control, 2019.
Spectral Constraints and Weight Regularizations
  Jiong Zhang, et al., Stabilizing Gradients for Deep Neural Networks via Efficient SVD Parameterization, 2018.
  Shaowu Pan, Karthik Duraisamy, Long-time predictive modeling of nonlinear dynamical systems using neural networks, 2018.
  Eldad Haber, et al., IMEXnet: A Forward Stable Deep Neural Network. 2019
  A. Tuor, J. Drgona, D. Vrabie, Constrained Neural Ordinary Differential Equations with Stability Guarantees, 2020.
Notes: The presentation I’m giving today is for a data-driven method for dynamics modeling.
We should care about this because people interact with and depend on complicated systems all the time.
Greater understanding of these systems can lead to outcomes which are
More energy efficient
Cost effective
Conducive to human life
Having an accurate model of a system enables scientific discovery,
Can provide critical information to support high stakes decisions in changing environments
Or to provide necessary information for predictive maintenance of high value equipment, avoiding costly and potentially dangerous equipment
Failures.
One of the most common and lucrative uses of systems models are for predictive control in manufacturing and other large scale enterprises.
I’m presenting a method today which bridges benefits of traditional physics-based modeling with more recent data-driven modeling using deep learning
Traditional physics-based modeling works very well and is widely used in many real world applications. However, it can’t always be applied to every situation.
missing information
incomplete awareness of the model state space.
limitations on the available operational data.
For large scale systems, not only are they difficult to model from first principles, it is also not always possible to simulate the system in real time.
Data-driven approaches for systems modeling are an alternative in these situations but can come with their own disadvantages.
Can take a lot of data to train and may behave unpredictably outside the distribution of training data in unobserved regions of the system state space.
In addition, modern neural network approaches don’t typically provide constraints enforcement within physically realizable and operationally safe bounds,

## Slide 33: Uncertainty Quantification: Methods
Monte-Carlo Dropout
  Approximate variational inference via repeated sampling of NN predictions with dropout enabled at inference time
  Method from “Dropout as a Bayesian approximation: representing model uncertainty in deep learning” by Gal and Ghahramani.
Graphic: “A frequentist approach to prediction uncertainty” by Yu Ri Tan
Notes: Old:
Deep Gaussian Processes
  Composes Gaussian Process models to represent hidden layers as distributions over functions
Conditional Invertible Neural Networks
  Invertible architecture of cINNs allows for posterior estimation via latent space sampling

## Slide 34: Uncertainty Quantification: Methods
Ensembling
  Train K models with different random weight initializations, then aggregate predictions of all models
  Models trained using Gaussian mixture objective
  Method from “Simple and Scalable Predictive Uncertainty Using Deep Ensembles” by Lakshminarayanan et al.
…
…
Model 1
Model K
Predicted mean, std. deviation
from each model
Aggregated mean, std. deviation
Notes: Old:
Deep Gaussian Processes
  Composes Gaussian Process models to represent hidden layers as distributions over functions
Conditional Invertible Neural Networks
  Invertible architecture of cINNs allows for posterior estimation via latent space sampling

## Slide 35: Uncertainty Quantification: Methods
Bayesian Neural Networks
  Each weight of a NN defined as a distribution whose parameters are learned by variational inference
  Method from “Weight uncertainty in neural networks” by Blundell et al.
Figure from Blundell et al., 2015. A standard neural network (left), a Bayesian neural network (right).
Notes: Old:
Deep Gaussian Processes
  Composes Gaussian Process models to represent hidden layers as distributions over functions
Conditional Invertible Neural Networks
  Invertible architecture of cINNs allows for posterior estimation via latent space sampling