## Slide 1: Deep Learning Explicit Differentiable Predictive Control Laws for Buildings
Ján Drgoňa
Collaborators: Aaron Tuor, Elliott Skomski,
Soumya Vasisht, Draguna Vrabie
IFAC NMPC July 11-14, 2021

## Slide 2: Model Predictive Control
95% of the process control applications are PID loops using trial and error rule-based optimization. The rest is model predictive control (MPC).
Modeling
  Unknown or partially known dynamics
  Physics-based modeling is expensive
  Purely data-driven models lack generalization
Real-time optimization
  Scalability
  Computational limitations of control hardware
  Parallelization, distributed optimization
Assumption:
Reliable and accurate system dynamics model
Drgona J., J. Arroyo, I.C. Figueroa, D. Blum, K. Arendt, D. Kim, and E.P. Olle, J. Oravec, M. Wetter, D. L. Vrabie, L. Helsen. 2020. "All You Need to Know About Model Predictive Control for Buildings." Annual Reviews in Control, September 29, 2020
Successes
Challenges
Notes: Domain awareness, trusted autonomy
PID controller-
A PID controller continuously calculates an error value
the difference between a desired setpoint (SP) a process variable (PV) and
Correction based on proportion of error, integration of accumulated error, and derivative of the error
MPC first developed in the chemical industry to address some of the shortcomings of a PID controller.
Designed to handle MIMO systems
Can handle constraints
Preview capability
MPC uses a model to predict future outcomes of a process.
Online optimization problem at each process interval. Performs first action in the rollout.
requiring large memory and fast processor to operate in real time.
Training and calibration of models- lots of expert time
Optimization: translation to a solver language- lots of expert time
Computational limitations of control hardware depending on the system

## Slide 3: Implementation of MPC in Office Building in Belgium
The field test energy use performance of MPC (green) and RBC (red) during the transient season. Each dot represents one day.
The field test thermal comfort performance of MPC (green) and RBC (red) during the transient season. Each dot represents one day.
Highlights: Heat pump energy savings up to 53%.
Thermal comfort improvement up to 37%.
Drgona J., et al., Cloud-based implementation of white-box model predictive control for a GEOTABS office building: a field test demonstration. Journal of Process Control, 2020.
Notes: To better understand the complexity of the task, lets walk through a complete workflow as implemented for a practical use case to control an office building in Belgium.
This office building is equipped with thermally activated building structures with a geothermal heat pump (GEOTABS). These kinds of buildings are known to be very challenging to control due to the large thermal mass and associated time delays. For optimal operation of this type of systems, predictive control is an absolute must.
First one develops a high-fidelity physics-based model based on the available engineering documentation and measurement data.
Then the control-relevant equations are extracted and used to construct an optimization-based predictive controller.
The optimized controls are computed every 15min based on new weather forecast and new measurement from the building, then the controls are communicated to the building management system for execution.
The whole procedure takes approximately a minute to execute in real time.
After using the MPC in the office building for a couple of months the team measured more than 50% energy savings on the heat pump and improved thermal comfort by approximately 37%. The rigid and delayed behavior of the rule-based controller is replaced by dynamic and anticipatory behavior of MPC, which keeps the zone temperatures closer within comfort bounds and delivers cooling only when it is needed.

## Slide 4: Deep Learning of MPC-based Control Policies
Approximate MPC
  Supervised learning
  Imitation learning of MPC
  Requires original MPC and model
Differentiable Predictive Control
  Differentiable closed-loop model
  Model-based policy optimization
  Theoretical connection with MPC
Drgona J., et al., “Approximate model predictive building control via machine learning,” Applied Energy, 2018
Drgona J., Helsen L., Vrabie D., "Cutting the Deployment Costs of Physics-Based MPC in Buildings by Simulation-Based Imitation Learning.”, proceedings of Dynamic Systems and Control Conference 2020, - Best paper award
Drgona J., et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, preprint 2021. https://arxiv.org/abs/2011.03699

## Slide 5: Formulations of Constrained Optimization Problems
Standard form
Parametric programming
Lagrangian form
Machine learning
“online” optimization
Single solution for
given parameter values
“offline” optimization
Obtains a solution map
for a set of parameters
“offline” optimization
Obtains a model (map)
for a set of datapoints
“online” optimization
Using soft constraints
Instead of hard constraints
Data-driven differentiable parametric optimization (D3PO): Combining principles of
Lagrangian formulation, parametric programming and ML
Notes: There are four main challenges that must be overcome to make MPC cost-effective
The Training and calibration of models – must be automated
The translation of the optimization problems to a solver language – must be automated
To address the computational limitations of embedded hardware - must reduce computing need without trading performance
Acceptance by building operators – complex decisions must be translated to interpretable decision rules

## Slide 6: Data-Driven Differentiable Parametric Optimization (D3PO)
import neuromancer as nm dataset = nm.datasets.Dataset(sequences=data)
components = nm.policies.SolutionMap(**kwargs) objectives = nm.Objective(torch.norm(z, 2)), weight=Q_x) constraints = nm.Objective(torch.norm(F.relu(
torch.mm(A, z.T)-b), 1), weight=Q_con) problem = nm.Problem(objectives, constraints, components)
optimizer = torch.optim.AdamW(model.parameters(), lr)
trainer = nm.Trainer(problem, dataset, optimizer, epochs) best_model = trainer.train()
D3PO problem definition:
D3PO implementation using Neuromancer:
Optimize x, given dataset
by finding a mapping x=h( )
  https://github.com/pnnl/neuromancer
PyTorch-based D3PO framework:

## Slide 7: Learning to Stabilize Known Unstable System with DPC
Problem setup:
DPC formulation:
  Drgona J., Tuor A., Vrabie D., Learning Stable Adaptive Explicit Differentiable Predictive Control for Unknown Linear Systems, under review, 2021

## Slide 8: Economic DPC for Building Control
System model
Explicit control policy
Economic MPC loss function with penalties

## Slide 9: Closed-loop Performance of DPC on Learned Model without Plant-Model Mismatch

## Slide 10: Closed-loop Performance of DPC on System Model with Plant-Model Mismatch and PI Correctors

## Slide 11: Conclusion
Differentiable Predictive Control
  Neural state space models
  Incorporating constraints
  Explicit neural control policies
  Theoretical connection with MPC
Ongoing work
  Uncertainty Quantification
  Plant-model mismatch
  Theoretical guarantees: convergence, stability, constraints satisfaction
Code development
  Neuromancer software package
    https://github.com/pnnl/neuromancer
  Structured linear maps in Pytorch
    https://pnnl.github.io/slim/
Long-Term Vision
  Causal discovery, dynamical coupling
  Solving large-scale non-convex constrained optimization problems
  Applications in energy, manufacturing, cyber

## Slide 12: Differentiable Predictive Control (DPC)
Stage I: System Identification
Stage II: Policy Optimization
[1] Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, preprint 2021
[2] Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Stable Adaptive Explicit Differentiable Predictive Control for Unknown Linear Systems, under review, 2021

## Slide 13: Model Predictive Control vs Differentiable Predictive Control
DPC = Formulation of MPC problem as a constrained deep learning problem
  Drgona J., Tuor A., Vrabie D., Learning Stable Adaptive Explicit Differentiable Predictive Control for Unknown Linear Systems, under review, 2021

## Slide 14: Modeling Thermal Dynamics
Ján Drgona, et al., Physics-constrained deep learning of multi-zone building thermal dynamics, Energy and Buildings, 2021