## Slide 1: Constrained Deep Learning for System Identification and Differentiable Predictive Control of Nonlinear Systems
Jan Drgona
Collaborators: Elliott Skomski, Soumya Vasisht,
Aaron Tuor, Draguna Vrabie
Invited talk: IMT Lucca, 17th of June 2021

## Slide 2: Model Predictive Control
95% of the process control applications are PID loops using trial and error rule-based optimization. The rest is model predictive control (MPC).
Modeling
  Unknown or partially known dynamics
  Physics-based modeling is expensive
  Purely data-driven models lack generalization
Real-time optimization
  Scalability
  Computational limitations of control hardware
  Parallelization, distributed optimization
Assumption:
Reliable and accurate system dynamics model
Drgona J., J. Arroyo, I.C. Figueroa, D. Blum, K. Arendt, D. Kim, and E.P. Olle, J. Oravec, M. Wetter, D. L. Vrabie, L. Helsen. 2020. "All You Need to Know About Model Predictive Control for Buildings." Annual Reviews in Control, September 29, 2020
Successes
Challenges
Notes: Domain awareness, trusted autonomy
PID controller-
A PID controller continuously calculates an error value
the difference between a desired setpoint (SP) a process variable (PV) and
Correction based on proportion of error, integration of accumulated error, and derivative of the error
MPC first developed in the chemical industry to address some of the shortcomings of a PID controller.
Designed to handle MIMO systems
Can handle constraints
Preview capability
MPC uses a model to predict future outcomes of a process.
Online optimization problem at each process interval. Performs first action in the rollout.
requiring large memory and fast processor to operate in real time.
Training and calibration of models- lots of expert time
Optimization: translation to a solver language- lots of expert time
Computational limitations of control hardware depending on the system

## Slide 3: Objective: Integrate Deep Learning with MPC and Physics
Automate learning of the system dynamics and model-based control policy
Streamline the installation process, facilitate explainability
Endow with lifelong learning and offer performance guarantees during the learning process

## Slide 4: Deep Learning of MPC-based Control Policies
Approximate MPC
  Supervised learning
  Imitation learning of MPC
  Requires original MPC
  Requires system model
Differentiable Predictive Control
  Neural state space models
  Differentiable closed-loop model
  Model-based policy optimization
  Theoretical connection with MPC
  Drgona J., et al., “Approximate model predictive building control via machine learning,” Applied Energy, 2018
  Drgona J., Helsen L., Vrabie D., "Cutting the Deployment Costs of Physics-Based MPC in Buildings by Simulation-Based Imitation Learning.”, proceedings of Dynamic Systems and Control Conference 2020, - Best paper award

## Slide 5: Formulations of Constrained Optimization Problems
Standard form
Parametric programming
Lagrangian form
Machine learning
“online” optimization
Single solution for
given parameter values
“offline” optimization
Obtains a solution map
for a set of parameters
“offline” optimization
Obtains a model (map)
for a set of datapoints
“online” optimization
Using soft constraints
Instead of hard constraints

## Slide 6: Formulations of Constrained Optimization Problems
Standard form
Parametric programming
Lagrangian form
Machine learning
“online” optimization
Single solution for
given parameter values
“offline” optimization
Obtains a solution map
for a set of parameters
“offline” optimization
Obtains a model (map)
for a set of datapoints
“online” optimization
Using soft constraints
Instead of hard constraints
Data-driven differentiable parametric optimization (D3PO): Combining principles of
Lagrangian formulation, parametric programming and ML

## Slide 7: Data-Driven Differentiable Parametric Optimization (D3PO)
import neuromancer as nm dataset = nm.datasets.Dataset(sequences=data)
components = nm.policies.SolutionMap(**kwargs) objectives = nm.Objective(torch.norm(z, 2)), weight=Q_x) constraints = nm.Objective(torch.norm(F.relu(torch.mm(A, z.T)-b), 1), weight=Q_con) problem = nm.Problem(objectives, constraints, components)
optimizer = torch.optim.AdamW(model.parameters(), lr)
trainer = nm.Trainer(problem, dataset, optimizer, epochs) best_model = trainer.train()
D3PO problem definition:
D3PO implementation using Neuromancer:
Optimize x, given dataset
D3PO solution of
parametric quadratic program.
by finding a mapping x=h( )
Applications:
Optimization
Modeling
Control
with constraints
Solution of parametric quadratic
program with classical solver.
  https://github.com/pnnl/neuromancer
  https://github.com/pnnl/slim

## Slide 8: Constrained Neural Models in D3PO
Structured linear algebra:
  Eigenvalues, sparsity, rank, positive definiteness
Loss function terms:
  Regularizations
  Penalty methods
  Physics-informed neural networks
Neural models for dynamical systems:
  Neural state space models
  Energy-based models
Constrained optimal control
  Differentiable predictive control
  https://github.com/pnnl/neuromancer
  https://github.com/pnnl/slim

## Slide 9: Differentiable Predictive Control (DPC)
Stage I: System Identification
Stage II: Policy Optimization
Notes: Integrate Deep Learning with Optimization-Based Control
Machine learning models that respect physical laws
Incorporate domain knowledge in their architectures
Incorporate domain knowledge with auxiliary loss functions
Use cases
Optimal control
Predictive maintenance
Surrogates for inverse problems
Forecasting for high level planning
Configurable optimization
Sequential
Joint
Alternating
Online updates
Scalable inference
Fast sampling rates
Limited computational resources
High dimensional state space
Long prediction horizons

## Slide 10: Constrained Neural State Space Models
Machine learning models that respect physical laws and constraints
Structured architectures
Physics-informed loss functions
Constraints enforcing penalties
Learnable activation functions
Structured linear maps
  Elliott Skomski, et al., Constrained Block Nonlinear Neural Dynamical Models, American Control Conference (ACC) 2021.
  A. R. Tuor, J. Drgona, D. L. Vrabie, Constrained Neural Ordinary Differential Equations with Stability Guarantees, ICML workshop 2020.

## Slide 11: Training Constrained Neural State Space Models
Bound influence of input and bound output to physical range
Predicted State Smoothing
Partially observable non-autonomous system
Dataset:
Optimize N-step prediction horizon MSE
Multi-term loss function:
Elliott Skomski, Ján Drgoňa, Aaron Tuor, Automating Discovery of Physics-Informed Neural State Space Models via Learning and Evolution, Proceedings of the 3rd Conference on Learning for Dynamics and Control (L4DC), 2021.

## Slide 12: Modeling Thermal Dynamics with Domain-aware Model Design
Ján Drgona, et al., Physics-constrained deep learning of multi-zone building thermal dynamics, Energy and Buildings, 2021

## Slide 13: Real World Data: Office Building

## Slide 14: Open-loop Trajectories of Linear Dynamics Model
Ján Drgona, et. al, Physics-constrained deep learning of multi-zone building thermal dynamics, Energy and Buildings, 2021

## Slide 15: Open-loop Trajectories of Neural Dynamics Model
Ján Drgona, et. al, Physics-constrained deep learning of multi-zone building thermal dynamics, Energy and Buildings, 2021

## Slide 16: Differentiable Predictive Control (DPC)
Generic method for constrained model-based control
Can be trained end-to-end from time series dataset
Nonlinear constrained optimal control
Explicit neural network-based control policy
Scalability beyond the limitations of explicit MPC
[1] Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning https://arxiv.org/abs/2011.03699
[2] Jan Drgona, Aaron Tuor, Draguna Vrabie, Constrained Physics-Informed Deep Learning for Stable System Identification and Control of Unknown Linear Systems https://arxiv.org/abs/2004.11184

## Slide 17: Model Predictive Control vs Differentiable Predictive Control
DPC = Formulation of MPC problem as a constrained deep learning model
  Jan Drgona, Aaron Tuor, Draguna Vrabie, Constrained Physics-Informed Deep Learning for Stable System Identification and Control of Unknown Linear Systems https://arxiv.org/abs/2004.11184

## Slide 18: Learning to Stabilize Known Unstable System with DPC
Problem setup:
DPC formulation:

## Slide 19: DPC capability: Computationally efficient offline optimization with operational safety constraints
Balancing conflicting objectives
Response to constraint tightening
Reference tracking performance
--- Reference trajectory
--- Constraints
__ Controlled trajectory
Notes: Computationally efficient performance optimization with operational safety constraints

## Slide 20: Comparison of DPC with MPC, LQR, and RL on Unknown Linear System with Disturbances
Closed loop trajectories. Top: controlled state (orange), internal model predictions (green), given reference (dashed blue), and constraints (dashed black). Middle: control action (blue) and bounds (dashed black). Bottom: disturbances
Control performance comparison in simulations with parametric and additive uncertainties. Control Strategies: MPC, Robust MPC , Stochastic MPC, LQR, LQI, A2C: Asynchronous, deterministic variant of Advantage Actor Critic, ACKTR: Actor Critic using Kronecker-Factored Trust Region, PPO2: Proximal Policy Optimization
  Drgona J., Tuor A., Vrabie D., Constrained Physics-Informed Deep Learning for Stable System Identification and Control of Linear Systems, Code release: https://github.com/pnnl/deps_arXiv2020

## Slide 21: Economic DPC for Building Control
  Jan Drgona, Aaron Tuor, Elliott Skomski, Soumya Vasisht, Draguna Vrabie, Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, accepted for IFAC NMPC 2021
model
policy
Economic MPC loss function

## Slide 22: Closed-loop Performance of DPC on Learned Model without Plant-Model Mismatch
  Jan Drgona, Aaron Tuor, Elliott Skomski, Soumya Vasisht, Draguna Vrabie, Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, accepted for IFAC NMPC 2021

## Slide 23: Closed-loop Performance of DPC on Emulator Model with Plant-Model Mismatch
  Jan Drgona, Aaron Tuor, Elliott Skomski, Soumya Vasisht, Draguna Vrabie, Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, accepted for IFAC NMPC 2021

## Slide 24: Embedded Implementation of DPC
Flexy-Air system sketch with Raspberry-Pi controller
Performance comparison: reference (red dashed), position controlled with PI controller (green), explicit model predictive control (purple), constrained differentiable predictive control (blue) and constraints (black-dashed). Bottom figures show the fan speed controls
  Jan Drgona, Karol Kis, Aaron Tuor, Draguna Vrabie, Martin Klauco, Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning; arXiv:2011.03699

## Slide 25: Scalability Analysis of DPC

## Slide 26: Stability Analysis of Neural Dynamics
2D attractors generated by deep neural networks.
Exploring connections between:
Deep neural networks
Piecewise affine (PWA) maps
Contraction of PWA maps
Banach fixed point theorem
Stability of linear switched systems
Stability of neural feedback systems

## Slide 27: Deep Neural Networks as Pointwise Affine Maps
At every point , the neural network, without bias may be represented as
where represent the weight parameterizations at layer , and is a diagonal matrix that represents the element-wise application of the nonlinear activation function at layer .
  Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics, arXiv:2011.13492
Deep feedforward neural network
Notes: The presentation I’m giving today is for a data-driven method for dynamics modeling.
We should care about this because people interact with and depend on complicated systems all the time.
Greater understanding of these systems can lead to outcomes which are
More energy efficient
Cost effective
Conducive to human life
Having an accurate model of a system enables scientific discovery,
Can provide critical information to support high stakes decisions in changing environments
Or to provide necessary information for predictive maintenance of high value equipment, avoiding costly and potentially dangerous equipment
Failures.
One of the most common and lucrative uses of systems models are for predictive control in manufacturing and other large scale enterprises.
I’m presenting a method today which bridges benefits of traditional physics-based modeling with more recent data-driven modeling using deep learning
Traditional physics-based modeling works very well and is widely used in many real world applications. However, it can’t always be applied to every situation.
missing information
incomplete awareness of the model state space.
limitations on the available operational data.
For large scale systems, not only are they difficult to model from first principles, it is also not always possible to simulate the system in real time.
Data-driven approaches for systems modeling are an alternative in these situations but can come with their own disadvantages.
Can take a lot of data to train and may behave unpredictably outside the distribution of training data in unobserved regions of the system state space.
In addition, modern neural network approaches don’t typically provide constraints enforcement within physically realizable and operationally safe bounds,

## Slide 28: Asymptotic Stability of Deep Neural Dynamics
Notes: The presentation I’m giving today is for a data-driven method for dynamics modeling.
We should care about this because people interact with and depend on complicated systems all the time.
Greater understanding of these systems can lead to outcomes which are
More energy efficient
Cost effective
Conducive to human life
Having an accurate model of a system enables scientific discovery,
Can provide critical information to support high stakes decisions in changing environments
Or to provide necessary information for predictive maintenance of high value equipment, avoiding costly and potentially dangerous equipment
Failures.
One of the most common and lucrative uses of systems models are for predictive control in manufacturing and other large scale enterprises.
I’m presenting a method today which bridges benefits of traditional physics-based modeling with more recent data-driven modeling using deep learning
Traditional physics-based modeling works very well and is widely used in many real world applications. However, it can’t always be applied to every situation.
missing information
incomplete awareness of the model state space.
limitations on the available operational data.
For large scale systems, not only are they difficult to model from first principles, it is also not always possible to simulate the system in real time.
Data-driven approaches for systems modeling are an alternative in these situations but can come with their own disadvantages.
Can take a lot of data to train and may behave unpredictably outside the distribution of training data in unobserved regions of the system state space.
In addition, modern neural network approaches don’t typically provide constraints enforcement within physically realizable and operationally safe bounds,

## Slide 29: Dynamical Effects of Weights
  Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics, arXiv:2011.13492

## Slide 30: Dynamical Effects of Biases and Depth
  Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics, arXiv:2011.13492

## Slide 31: Dynamical Effects of Activation Functions
  Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics, arXiv:2011.13492

## Slide 32: Stability Analysis of Neural State Space Models
Two tank system: 2 states x, 2 inputs u
Exothermic stirred tank reactor system: 2 states x, 1 input u

## Slide 33: Stability of Full State Neural Feedback Systems
Closed-loop system with linear system dynamics and neural policy:
Pointwise affine form of the neural control policy:
Pointwise affine form of the closed-loop system with neural policy:
Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Stable Adaptive Explicit Differentiable Predictive Control for Unknown Linear Systems, under review, 2021

## Slide 34: Conclusion
Differentiable Predictive Control
  Neural state space model for system ID
  Incorporating constraints (neural gray-box)
  Theoretical connection with MPC
  Explicit neural control policies
  Embedded implementation with low-cost HW
Ongoing work
  Uncertainty Quantification
  Plant-model mismatch
  Theoretical guarantees: convergence, stability, constraints satisfaction
Code development
  Neuromancer software package
    https://github.com/pnnl/neuromancer
  Structured linear maps in Pytorch
    https://pnnl.github.io/slim/
Long-Term Vision
  Causal discovery, dynamical coupling
  Solving large-scale non-convex constrained optimization problems
  Applications in energy, manufacturing, cyber

## Slide 35: Attractors of Deep Neural Networks
  Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics, arXiv:2011.13492

## Slide 36: Attractors of Deep Neural Networks
  Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics, arXiv:2011.13492