## Slide 1: Constrained Deep Learning for Modeling and Control of Buildings
Jan Drgona
Collaborators: Elliott Skomski, Soumya Vasisht,
Aaron Tuor, Vikas Chandan, Draguna Vrabie

## Slide 2: Model Predictive Control Challenges
Modeling
  Physics-based modeling is expensive and time-consuming, uncertainties are unavoidable
  Purely data-driven models lack operational safety guarantees, and do not generalize well
Optimization: translation to a solver language
  Multiple customized methods for dealing with constraints (soft, hard)
  Multi-objective, convexification, regularization, convergence issues
Computational limitations of control hardware
  Online optimization computational requirements
  Cloud deployment vs embedded optimization
Acceptance by operators
  Installation: data mapping, sensor discovery, tuning
  Interpretability, interaction, trust
  Performance Measurement & Verification
Drgona J., J. Arroyo, I.C. Figueroa, D. Blum, K. Arendt, D. Kim, and E.P. Olle, J. Oravec, M.Wetter, D.L.Vrabie, L. Helsen. 2020. "All You Need to Know About Model Predictive Control for Buildings." Annual Reviews in Control, September 29, 2020
Notes: There are four main challenges that must be overcome to make MPC cost-effective
The Training and calibration of models – must be automated
The translation of the optimization problems to a solver language – must be automated
To address the computational limitations of embedded hardware - must reduce computing need without trading performance
Acceptance by building operators – complex decisions must be translated to interpretable decision rules

## Slide 3: Formulations of Constrained Optimization Problems
Standard form
Parametric programming
Lagrangian form
Machine learning
“online” optimization
Single solution for
given parameter values
“offline” optimization
Obtains a solution map
for a set of parameters
“offline” optimization
Obtains a model (map)
for a set of datapoints
“online” optimization
Using soft constraints
Instead of hard constraints
Notes: There are four main challenges that must be overcome to make MPC cost-effective
The Training and calibration of models – must be automated
The translation of the optimization problems to a solver language – must be automated
To address the computational limitations of embedded hardware - must reduce computing need without trading performance
Acceptance by building operators – complex decisions must be translated to interpretable decision rules

## Slide 4: Formulations of Constrained Optimization Problems
Standard form
Parametric programming
Lagrangian form
Machine learning
“online” optimization
Single solution for
given parameter values
“offline” optimization
Obtains a solution map
for a set of parameters
“offline” optimization
Obtains a model (map)
for a set of datapoints
“online” optimization
Using soft constraints
Instead of hard constraints
Data-driven differentiable parametric optimization: Combining principles of
Lagrangian formulation, parametric programming and ML
Notes: There are four main challenges that must be overcome to make MPC cost-effective
The Training and calibration of models – must be automated
The translation of the optimization problems to a solver language – must be automated
To address the computational limitations of embedded hardware - must reduce computing need without trading performance
Acceptance by building operators – complex decisions must be translated to interpretable decision rules

## Slide 5: Method: Differentiable Predictive Control (DPC)
Dataset of perturbed system measurements
Synthetic random dataset of references and system states
Stage I: System Identification
Stage II: Policy Optimization
Fixed SSM Parameters
System ID
Loss
Reference
Tracking
Loss
Notes: Integrate Deep Learning with Optimization-Based Control
Machine learning models that respect physical laws
Incorporate domain knowledge in their architectures
Incorporate domain knowledge with auxiliary loss functions
Use cases
Optimal control
Predictive maintenance
Surrogates for inverse problems
Forecasting for high level planning
Configurable optimization
Sequential
Joint
Alternating
Online updates
Scalable inference
Fast sampling rates
Limited computational resources
High dimensional state space
Long prediction horizons

## Slide 6: Stage I: Constrained Neural State Space Models
Machine learning models that respect physical laws and constraints
Nonlinear system identification
Incorporate domain knowledge in their architectures
Incorporate domain knowledge with auxiliary loss functions
Block-structured neural state-space model
Neural state estimator
Learnable activation functions
Structured linear maps
Constraints enforcing penalties
  Aaron R Tuor, Ján Drgona, Draguna L Vrabie Constrained Neural Ordinary Differential Equations with Stability Guarantees, Code release: https://github.com/pnnl/neural_ODE_ICLR2020

## Slide 7: Neural Network Block Structure and Components
Multi-layer perceptron
  Function approximator
  Composed linear maps and nonlinear activation functions
  Model complicated functions
    adding depth (more layers)
    and/or width (more nodes)
Residual Neural Network
  Adds shortcut connections
  Easier to optimize
  Mitigates vanishing gradient
Recurrent Neural Network
  Adds recurrences from previous inputs
  Sequential modeling
  Can model time delay
f

## Slide 8: Structured Linear Maps with Eigenvalue Constraints
SVD factorization
Hamiltonian weight
  Jiong Zhang, et al., Stabilizing Gradients for Deep Neural Networks via Efficient SVD Parameterization, 2018. Eldad Haber and Lars Ruthotto, Stable Architectures for Deep Neural Networks 2017 Jan Drgona, Aaron Tuor, Soumya Vasisht, Elliott Skomski, Draguna Vrabie, Spectral Analysis and Stability of Deep Neural Dynamics, arXiv:2011.13492 Code: https://github.com/pnnl/slim

## Slide 9: Training Loss Includes System Knowledge
Bound influence of input and bound output to physical range
Predicted State Smoothing
Partially observable non-autonomous system
Data needs:
Optimize N-step prediction horizon MSE

## Slide 10: Modeling Thermal Dynamics
Ján Drgona, Aaron R. Tuor, Vikas Chandan, Draguna L. Vrabie, Physics-constrained Deep Recurrent Neural Models of Building Thermal Dynamics, NeurIPS Climate Change AI Workshop, 2020
Implementation in PyTorch https://github.com/pnnl/neuromancer/tree/NeurIPS2020

## Slide 11: Real World Data: Office Building

## Slide 12: Open-loop Trajectories of Linear Dynamics Model

## Slide 13: Open-loop Trajectories of Neural Dynamics Model

## Slide 14: Deep Learning of Model-based Control Policies
Objectives
  Cut the development and deployment cost of model-based control
  Learn safe and robust control policies with adaptive updates
  Embedded hardware implementation
Approaches
  Approximate MPC
    Imitation learning of supervisory MPC
  Differentiable Predictive Control
    Supervised policy learning in closed loop guided by learned model

## Slide 15: Stage II: Differentiable Predictive Control (DPC)
Generic method for constrained model-based control
Can be trained end-to-end from time series dataset
Nonlinear constrained optimal control
  Neural system dynamics model
  Predictive reference tracking
  Constraints satisfaction
  Balancing conflicting objectives
  Economic objectives
Scalability beyond the limitations of explicit MPC
  Explicit neural network-based control policy
  Linear scalability w.r.t. memory footprint, number of policy parameters, and required construction time
  Potential for wide adoption in large-scale control systems with limited computational resources and fast sampling rates
Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning https://arxiv.org/abs/2011.03699
Jan Drgona, Aaron Tuor, Draguna Vrabie, Constrained Physics-Informed Deep Learning for Stable System Identification and Control of Unknown Linear Systems https://arxiv.org/abs/2004.11184

## Slide 16: Capability: Computationally efficient performance optimization with constraints
Balancing conflicting objectives
Response to constraint tightening
Reference tracking performance
--- Reference trajectory
--- Constraints
__ Controlled trajectory
Notes: Computationally efficient performance optimization with operational safety constraints

## Slide 17: Model Predictive Control vs Differentiable Predictive Control
DPC = Formulation of MPC problem as a constrained deep learning model
  Drgona J., Tuor A., Vrabie D., Constrained Physics-Informed Deep Learning for Stable System Identification and Control of Linear Systems, Code release: https://github.com/pnnl/deps_arXiv2020

## Slide 18: Comparison of DPC with MPC, LQR, and RL
Closed loop trajectories. Top: controlled state (orange), internal model predictions (green), given reference (dashed blue), and constraints (dashed black). Middle: control action (blue) and bounds (dashed black). Bottom: disturbances
Control performance comparison in simulations with parametric and additive uncertainties. Control Strategies: MPC, Robust MPC , Stochastic MPC, LQR, LQI, A2C: Asynchronous, deterministic variant of Advantage Actor Critic, ACKTR: Actor Critic using Kronecker-Factored Trust Region, PPO2: Proximal Policy Optimization
  Drgona J., Tuor A., Vrabie D., Constrained Physics-Informed Deep Learning for Stable System Identification and Control of Linear Systems, Code release: https://github.com/pnnl/deps_arXiv2020

## Slide 19: Embedded Implementation of DPC
Flexy-Air system sketch with Raspberry-Pi controller
Performance comparison: reference (red dashed), position controlled with PI controller (green), explicit model predictive control (purple), constrained differentiable predictive control (blue) and constraints (black-dashed). Bottom figures show the fan speed controls
  Jan Drgona, Karol Kis, Aaron Tuor, Draguna Vrabie, Martin Klauco, Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning; arXiv:2011.03699

## Slide 20: DPC for Building Control
  Jan Drgona, Aaron Tuor, Elliott Skomski, Soumya Vasisht, Draguna Vrabie, Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, under review IFAC NMPC 2021
model
policy
Economic MPC loss function

## Slide 21: Closed-loop Performance of DPC on Learned Model without Plant-Model Mismatch
  Jan Drgona, Aaron Tuor, Elliott Skomski, Soumya Vasisht, Draguna Vrabie, Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, under review IFAC NMPC 2021

## Slide 22: Closed-loop Performance of DPC on Emulator Model with Plant-Model Mismatch
  Jan Drgona, Aaron Tuor, Elliott Skomski, Soumya Vasisht, Draguna Vrabie, Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, under review IFAC NMPC 2021

## Slide 23: Conclusion
Differentiable Predictive Control
  Neural state space model for system ID
  Physics-informed priors (neural gray-box)
  Incorporating operational constraints
  Theoretical connection with MPC
  Explicit neural control policies
  Embedded implementation with low-cost HW
  Learning from small datasets
Ongoing work
  Uncertainty Quantification
  User-friendly software package
    Pytorch-based will be released soon: https://github.com/pnnl/neuromancer
  Comprehensive suite of physics-based priors and constraints
    Structured linear maps in Pytorch: https://pnnl.github.io/slim/
  Theoretical guarantees: convergence, stability, constraints satisfaction
Long-Term Vision
  Causal discovery, dynamical coupling
  Solving large-scale non-convex constrained optimization problems
  Real world applications in energy, manufacturing, cyber