## Slide 1: Neural Lyapunov Differentiable Predictive Control
Sayak Mukherjee, Jan Drgona, Aaron Tuor,
Mahantesh Halappanavar, Draguna Vrabie
jan.drgona@pnnl.gov
IEEE Conference on Decision and Control 2022

## Slide 2: Model Predictive Control (MPC)
2
95% of the industrial control applications are PID loops & expert driven rule-based control (RBC).
The rest is model predictive control (MPC).
Modeling
  Unknown or partially known dynamics
  Physics-based modeling is expensive
  Purely data-driven models lack generalization
Real-time optimization
  Scalability
  Computational limitations of control hardware
  Parallelization, distributed optimization
Assumption:
Reliable and accurate system dynamics model
Drgona J., J. Arroyo, I.C. Figueroa, D. Blum, K. Arendt, D. Kim, and E.P. Olle, J. Oravec, M. Wetter, D. L. Vrabie, L. Helsen. 2020. "All You Need to Know About Model Predictive Control for Buildings." Annual Reviews in Control, September 29, 2020
Successes
Challenges

## Slide 3: Deep Reinforcement Learning (DRL)
Dealing with constraints, and stability guarantees. Learning on real system with low data and low compute regimes. Offline learning. High-dimensional continuous state and action systems. Partial observability, time delays. Task generalization and intrinsic rewards.
Challenges
Successes
Everywhere where you have reliable simulation model, mostly discrete action space, and you can use massive offline compute power to solve the problem.
G. Dulac-Arnold, D. J. Mankowitz, and T. Hester, “Challenges of real-world reinforcement learning,”, 2019.
http://arxiv.org/abs/1904.12901

## Slide 4: Optimization Methods for Control
Online MPC
Explicit MPC
Imitation Learning
“online” optimization
single solution for
given parameter values
implicit policy
“offline” optimization obtains a solution map
for a set of parameters
classical methods lead to exponential complexity!
“offline” optimization
obtains a model (map)
for a set of data points
scalable but requires expert controller
Reinforcement Learning
“offline” optimization
obtains a policy map
for a set of data points
poor convergence and
can’t handle constraints

## Slide 5: Optimization Methods for Control
Online MPC
Explicit MPC
Imitation Learning
“online” optimization
single solution for
given parameter values
implicit policy
“offline” optimization obtains a solution map
for a set of parameters
classical methods lead to exponential complexity!
“offline” optimization
obtains a model (map)
for a set of data points
scalable but requires expert controller
Reinforcement Learning
“offline” optimization
obtains a policy map
for a set of data points
poor convergence and
can’t handle constraints
Today’s talk: differentiable programming and policy optimization for explicit MPC

## Slide 6: Differentiable Predictive Control (DPC)
From data to optimized explicit predictive control policy
  Online optimization
  Optimize for control actions
  Implicit solver-based control policy
  Offline optimization
  Optimize for control policy parameters
  Explicit neural control policy
MPC
DPC
Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022
Cost:
Model:
Constraints:

## Slide 7: Differentiable Computational Graphs and Model-based Policy Gradients
https://github.com/pnnl/neuromancer
Constructing differentiable computational graph: implementing parametric MPC problem in Pytorch.
https://pytorch.org/

## Slide 8: Differentiable Computational Graphs and Model-based Policy Gradients
https://github.com/pnnl/neuromancer
Forward pass: evaluate graph components (policy, model, constraints, objective terms) to compute structured learning loss function.

## Slide 9: Differentiable Computational Graphs and Model-based Policy Gradients
https://github.com/pnnl/neuromancer
Forward pass: evaluate graph components (policy, model, constraints, objective terms) to compute structured learning loss function.

## Slide 10: Differentiable Computational Graphs and Model-based Policy Gradients
https://github.com/pnnl/neuromancer
Forward pass: evaluate graph components (policy, model, constraints, objective terms) to compute structured learning loss function.

## Slide 11: Differentiable Computational Graphs and Model-based Policy Gradients
https://github.com/pnnl/neuromancer
Forward pass: evaluate graph components (policy, model, constraints, objective terms) to compute structured learning loss function.

## Slide 12: Differentiable Computational Graphs and Model-based Policy Gradients
https://github.com/pnnl/neuromancer
Forward pass: evaluate graph components (policy, model, constraints, objective terms) to compute structured learning loss function.

## Slide 13: Differentiable Computational Graphs and Model-based Policy Gradients
https://github.com/pnnl/neuromancer
Forward pass: evaluate graph components (policy, model, constraints, objective terms) to compute structured learning loss function.

## Slide 14: Differentiable Computational Graphs and Model-based Policy Gradients
Backward pass: Differentiate the computational graph to train the policies using state-of-the-art deep learning tools.
https://github.com/pnnl/neuromancer

## Slide 15: Differentiable Predictive Control (DPC) Recap
From data to explicit constrained control policy via differentiable optimization
  Theoretical connection with MPC
  Structured offline learning
  Parametric solution of the MPC problem
  Handling state and input constraints
  Handling of arbitrary differentiable models
  Lack of stability guarantees
  Lack of constraints satisfaction guarantees
  Lack of convergence guarantees
  Can’t handle integer variables
  Sampling-based
Pros:
Cons:
Notes: The conceptual methodology of DPC is illustrated here.
Assuming time series dataset obtained from the measurements of the system dynamics, in the first step, we perform system identification using a neural state-space model (SSM).
In the second step, we close the loop by combining the neural SSM with neural control law obtaining a differentiable closed-loop dynamics model fully parametrized by neural networks.
This allows us to leverage standard tools in deep learning to optimize the neural control laws by backpropagating the MPC loss function through the closed-loop dynamics.
Essentially this is a data-driven solution to multiparametric programming problems emerging from explicit nonlinear MPC.
Contrary to approximate MPC (aka imitation learning), DPC does not require supervision by an expert controller. Instead, a dynamics model is learned from a small dataset of system measurements, and the control law is then optimized offline by differentiating the learned system model.

## Slide 16: Differentiable Predictive Control (DPC) Recap
From data to explicit constrained control policy via differentiable optimization
  Theoretical connection with MPC
  Structured offline learning
  Parametric solution of the MPC problem
  Handling state and input constraints
  Handling of arbitrary differentiable models
  Lack of stability guarantees
  Lack of constraints satisfaction guarantees
  Lack of convergence guarantees
  Can’t handle integer variables
  Sampling-based
Pros:
Cons:
Notes: The conceptual methodology of DPC is illustrated here.
Assuming time series dataset obtained from the measurements of the system dynamics, in the first step, we perform system identification using a neural state-space model (SSM).
In the second step, we close the loop by combining the neural SSM with neural control law obtaining a differentiable closed-loop dynamics model fully parametrized by neural networks.
This allows us to leverage standard tools in deep learning to optimize the neural control laws by backpropagating the MPC loss function through the closed-loop dynamics.
Essentially this is a data-driven solution to multiparametric programming problems emerging from explicit nonlinear MPC.
Contrary to approximate MPC (aka imitation learning), DPC does not require supervision by an expert controller. Instead, a dynamics model is learned from a small dataset of system measurements, and the control law is then optimized offline by differentiating the learned system model.

## Slide 17: Joint DPC with Neural Lyapunov Functions
Sayak Mukherjee, Ján Drgoňa, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Neural Lyapunov Differentiable Predictive Control, CDC, 2022
17

## Slide 18: Mathematical framework
Objective function
Dynamics
Constraints
Predictive policy
Lower-level
Soft state, and control constraints
Neural control policy
MPC objective function
DPC Formulation with Neural Lyapunov Functions

## Slide 19: Mathematical framework
Objective function
Dynamics
Constraints
Predictive policy
Lower-level
Input Convex Neural networks (ICNN)
Lyapunov condition:
Soft state, control, and Lyapunov constraints
Neural control policy
MPC objective function
DPC Formulation with Neural Lyapunov Functions
Gaurav Manek, J. Zico Kolter, Learning Stable Deep Dynamics Models, NeurIPS 2019

## Slide 20: Mathematical framework and learning algorithm
Gradient flows:
Joint Offline Learning of Policy and Lyapunov Function
Policy Gradients
Learning Algorithm
NLDPC
Problem
  For probabilistic stability guarantees see the paper Neural Lyapunov Differentiable Predictive Control.

## Slide 21: Experiments: Stabilizing Unstable Double Integrator
Phase portrait with overlaid Lyapunov contours
Learned Lyapunov
function
Stability regions via discrete-time Lyapunov conditions
Closed-loop state and control trajectories

## Slide 22: Experiments: Controlling Unstable PVTOL Aircraft
Phase portrait with overlaid Lyapunov contours
Slice of the learned Lyapunov
function
Stability regions via discrete-time Lyapunov conditions
Closed-loop state and control trajectories

## Slide 23: Conclusion and Future Directions
Learning explicit predictive control policies via differentiable predictive control (DPC) algorithm
Learning neural Lyapunov functions for probabilistic closed-loop stability guarantees
Open-source code
Summary
Next steps
jan.drgona@pnnl.gov
Online safety filters based on learned Lyapunov functions
Dealing with time-varying nonlinear objectives and constraints
Dealing with economic objectives via Dissipativity
https://github.com/pnnl/neuromancer/tree/Lyapunov_DPC

## Slide 24: Acknowledgements
James Koch
Zhao Chen
Stefan Dernbach
Draguna Vrabie
Aaron Tuor
Ethan King
Christian M. Legaard
Soumya Vasisht
Wenceslao Shaw Cortez
Sayak Mukherjee
Mahantesh Halappanavar
Shrirang Abhyankar

## Slide 25: Differentiable Predictive Control (DPC)
From data to optimized explicit control policy
  Step 1: obtain system dynamics model or train the model using given time series data
  Step 2: sample problem parameters and differentiate MPC computational graph to obtain gradients for training the policy offline
Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022

## Slide 26: Motivation: Safety-Critical Control and Learning
Increased automation in human environments
  Robots
  Automated vehicles
Prevent system damage
Task specifications (not just stability)
Empirically shown to perform well
Implemented with low computational burden
Perforance highly dependent on:
  Training set
  Expert `behind-the-curtain’
Learning-based Control
Safety

## Slide 27: Dynamics of DPC Control Policy Learning
1341 learning parameters, 48.2 seconds offline training time on a CPU with 200 epochs.