## Slide 1: Differentiable Programming for Control
From data to explicit constrained control policy via differentiable optimization
  Theoretical connection with MPC
  Neural dynamical system models
  Differentiable closed-loop model
  Model-based policy optimization
Notes: The conceptual methodology of DPC is illustrated here.
Assuming time series dataset obtained from the measurements of the system dynamics, in the first step, we perform system identification using a neural state-space model (SSM).
In the second step, we close the loop by combining the neural SSM with neural control law obtaining a differentiable closed-loop dynamics model fully parametrized by neural networks.
This allows us to leverage standard tools in deep learning to optimize the neural control laws by backpropagating the MPC loss function through the closed-loop dynamics.
Essentially this is a data-driven solution to multiparametric programming problems emerging from explicit nonlinear MPC.
Contrary to approximate MPC (aka imitation learning), DPC does not require supervision by an expert controller. Instead, a dynamics model is learned from a small dataset of system measurements, and the control law is then optimized offline by differentiating the learned system model.

## Slide 2: Differentiable Predictive Control
Problem setup
Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Constrained Adaptive Differentiable Predictive Control Policies With Guarantees https://arxiv.org/abs/2004.11184
DPC formulation
DPC policy gradient

## Slide 3: Dynamics of DPC Control Policy Learning
1341 learning parameters, 48.2 seconds offline training time on a CPU with 200 epochs.

## Slide 4: Model-based Policy Gradients of DPC
Reward function
Policy
Constraints
penalties
Direct policy gradients

## Slide 5: Stochastic Differentiable Predictive Control
  Jan Drgona, Sayak Mukherjee, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Learning Stochastic Parametric Differentiable Predictive Control Policies, arXiv:2203.01447, to appear at IFAC ROCOND 2022
Stochastic
formulation
Robustness
to state noise
Stochastic obstacle avoidance

## Slide 6: Learning Stable Policies via Neural Lyapunov Differentiable Predictive Control
Sayak Mukherjee, Ján Drgoňa, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Neural Lyapunov Differentiable Predictive Control, arXiv:2205.10728, 2022

## Slide 7: Learning Stable via Neural Lyapunov Differentiable Predictive Control
Gaurav Manek, J. Zico Kolter, Learning Stable Deep Dynamics Models, NeurIPS 2019.
Lyapunov stability condition
Trivial null-space via coordinate shift
Neural Lyapunov Functions
Lyapunov regularization
Neural Lyapunov DPC
Input-convex neural network
Sayak Mukherjee, Ján Drgoňa, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Neural Lyapunov Differentiable Predictive Control, arXiv:2205.10728, 2022

## Slide 8: Economic DPC for Building Control
  Jan Drgona, Aaron Tuor, Elliott Skomski, Soumya Vasisht, Draguna Vrabie, Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, IFAC NMPC 2021
Neural state space dynamics model
MLP control policy architecture
Results
Handling multi-input multi-output nonlinear dynamics
Dynamic economic control objective
Parametric constraints

## Slide 9: Koopman-based DPC for Dynamics-Aware Economic Dispatch
Results
5 orders of magnitude speed-up
Minimal loss in solution quality
Ethan King, Ján Drgoňa, Aaron Tuor, Shrirang Abhyankar, Craig Bakker, Arnab Bhattacharya, Draguna Vrabie, Koopman-based Differentiable Predictive Control for the Dynamics-Aware Economic Dispatch Problem, The 2022 American Control Conference
Problem: Current redispatch processes do not incorporate system stability concerns. Incorporating stability in redispatch is too complex and/or time-consuming
Solution: Machine-learning based dynamics-aware redispatch. Learn system dynamics for faster assessment.
KO dynamics model
CNN control policy framework
Notes: Add waveform figure as a result – copy from previous slide replace discretize linearize with one block as iterative method

## Slide 10: DPC Wrap Up
Differentiable Predictive Control
  Differentiable system models
  Explicit control policies
  State and input constraints
  Embedded implementation
  Theoretical connection with MPC
Open-source Code
  Neuromancer software package
    https://github.com/pnnl/neuromancer
  Structured linear maps in Pytorch
    https://pnnl.github.io/slim/
Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning https://arxiv.org/abs/2011.03699
Jan Drgona, Aaron Tuor, Draguna Vrabie, Constrained Physics-Informed Deep Learning for Stable System Identification and Control of Unknown Linear Systems https://arxiv.org/abs/2004.11184