## Slide 1: Differentiable programming for modeling and control of dynamical systems
Ján Drgoňa Collaborators: Aaron Tuor, Shrirang Abhyankar, Ethan King, James Koch, Zhao Chen, Soumya Vasisht, Vikas Chandan, Wenceslao Shaw Cortez, Sayak Mukherjee, Mahantesh Halappanavar, Draguna Vrabie
Invited Talk at COEP Tech University, Pune

## Slide 2: Challenge 1: Systems Modeling
Simulations are crucial for many areas of decision-making and scientific discovery
Need: Improve computational efficiency and scalability for heterogenous scientific simulations
Approach: Integration of machine learning with physics-based models
Applications: building energy systems, power systems, molecular dynamics, unmanned vehicles

## Slide 3: Challenge 2: Systems Control
Model Predictive Control
Reinforcement Learning
Everywhere where you have reliable digital environment model, mostly discrete action space, and you can use massive compute to solve the problem.
Drgona J., J. Arroyo, I.C. Figueroa, D. Blum, K. Arendt, D. Kim, and E.P. Olle, J. Oravec, M. Wetter, D. L. Vrabie, L. Helsen. 2020. "All You Need to Know About Model Predictive Control for Buildings." Annual Reviews in Control, September 29, 2020
G. Dulac-Arnold, D. J. Mankowitz, and T. Hester, “Challenges of real-world reinforcement learning,”, 2019. http://arxiv.org/abs/1904.12901
95% of the industrial control applications are PID loops & expert driven rule-based control (RBC).
The rest is model predictive control (MPC).

## Slide 4: Landscape of Optimization Methods
Online optimization
Parametric programming
Imitation Learning
“online” solution for given parameter values
computationally demanding in real-time
“offline” optimization obtains a solution map
classical methods lead to exponential complexity!
“offline” optimization
obtains a model (map)
scalable but requires expert controller
Reinforcement Learning
“offline” optimization
obtains a policy map
classically can’t handle constraints

## Slide 5: Landscape of Optimization Methods
Online optimization
Parametric programming
Imitation Learning
“online” solution for given parameter values
computationally demanding in real-time
“offline” optimization obtains a solution map
classical methods lead to exponential complexity!
“offline” optimization
obtains a model (map)
scalable but requires expert controller
Reinforcement Learning
“offline” optimization
obtains a policy map
classically can’t handle constraints
Differentiable programming (DP): a unifying approach for data-driven parametric optimization with solutions based on automatic differentiation (AD)

## Slide 6: Differentiable Programming for Scientific Machine Learning
Differentiable Programming
  A Differentiable Programming System to Bridge Machine Learning and Scientific Computing, 2019
Physics-informed Neural Networks
  Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations, 2019
Neural Differential Equations
  Neural Ordinary Differential Equations, 2019
  Universal Differential Equations for Scientific Machine Learning, 2021
Differentiable Optimization
  Differentiable Convex Optimization Layers, 2019
  DC3: A learning method for optimization with hard constraints, 2021
  Deep Declarative Networks: A New Hope, 2020
  End-to-End Constrained Optimization Learning: A Survey, 2021
Differentiable Control
  Differentiable MPC for End-to-end Planning and Control, 2019
  Infinite-Horizon Differentiable Model Predictive Control, 2020

## Slide 7: Parametric Optimization via Differentiable Programming: Generalization of PINNs
Problem formulation:

## Slide 8: Parametric Optimization via Differentiable Programming: Generalization of PINNs
Objective function
Constraints
Scenarios
Parameters
Solution map
Primal optimizers
Problem formulation:

## Slide 9: Parametric Optimization via Differentiable Programming: Generalization of PINNs
Objective function
Constraints
Scenarios
Parameters
Solution map
Primal optimizers
Problem formulation:
Lagrangian form:
Constraints penalties
Gradient-based optimization based on AD

## Slide 10: Differentiable Parametric Programming: NeuroMANCER toolbox
train_data, dev_data, test_data = get_dataloaders(samples)
p = Variable(‘p’) # sampled parameter
x = Variable(‘x’) # decision variable
y = Variable('y’) # decision variable
map = nm.MLP(input_keys=['p’], output_keys=[‘x’,‘y’], name='map’)
# parametric solution map
f = x ** 2 + y ** 2 obj = f.minimize(weight=Q, name='obj’) # objective function con_1 = Q_con*(-x - y + p <= 0) # constraint
con_2 = Q_con*(-x + y + p <= 0) # constraint
objectives = [obj]
constraints = [con_1, con_2] components = [map]
loss = PenaltyLoss(objectives, constraints, train_data) problem = Problem(components, loss) # differentiable optimization optimizer = torch.optim.AdamW(problem.parameters(), lr=args.lr) trainer = Trainer(problem,train_data,dev_data,test_data,optimizer)
best_model = trainer.train()
  https://github.com/pnnl/neuromancer
Neural Modules with Adaptive Nonlinear Constraints and Efficient Regularizations

## Slide 11: Differentiable Parametric Programming: Computational Graphs
Parametric nonlinear programs
Orders of magnitude faster online solution compared to online optimization solvers (IPOPT).

## Slide 12: Universal Differential Equations
Methods:
Learning flow maps (MLPs and RNNs) for neural ODE implicit layers
ODE solution techniques: RK45, hierarchical, higher-order, implicit, multi-step
Physically-informed models: blend expert knowledge with neural ODE construction
Graph structured neural ODEs
White-box:
Gray-box:
Black Box:
  Christopher Rackauckas, et al., Neural Ordinary Differential Equations, arXiv:2001.04385, 2019 James Koch, et al., Structural Inference of Networked Dynamical Systems with Universal Differential Equations, arXiv:2207.04962, 2022

## Slide 13: Networked Dynamical Systems via Universal Differential Equations
  Christopher Rackauckas, et al., Neural Ordinary Differential Equations, arXiv:2001.04385, 2019 James Koch, et al., Structural Inference of Networked Dynamical Systems with Universal Differential Equations, arXiv:2207.04962, 2022
Network of unknown oscillators
Coupling adjacency
Ground truth Kuramoto system:
Qualitative generalization of learned dynamics on never-seen network topology.

## Slide 14: Neural State Space Models
fx
fu
fy
+
Linear
fx
fu
fy
+
Hammerstein
fx
fu
fy
+
Hammerstein-Weiner
fx
fu
fy
+
Block-Nonlinear
fxu
Unstructured
Linear map
Non-Linear map
yt+1
x0
xt
ut
ut
xt
xt+1
xt+1
yt+1
fy
fx
fu
fy
Koopman
fu o fy = I

## Slide 15: Structured Linear Maps (SLiM)
Factorizations and regularizations of linear maps with predetermined structure
Can be used to enforce sparsity or spectral properties
Spectral map
Perron-Frobenius map
  https://github.com/pnnl/slim

## Slide 16: Application: Modeling Thermal Dynamics
Ján Drgona, et al., Physics-constrained deep learning of multi-zone building thermal dynamics, Energy and Buildings, 2021

## Slide 17: Modeling Thermal Dynamics
Ján Drgona, et al., Physics-constrained deep learning of multi-zone building thermal dynamics, Energy and Buildings, 2021

## Slide 18: Open-loop Trajectories of Linear Model

## Slide 19: Open-loop Trajectories of Neural Model

## Slide 20: Differentiable Predictive Control
Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Constrained Adaptive Differentiable Predictive Control Policies With Guarantees, 2021,
https://arxiv.org/abs/2004.11184
Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022, https://arxiv.org/abs/2011.03699
Constrained Model-based Policy Optimization for Parametric Optimal Control

## Slide 21: Differentiable Computational Graphs and Model-based Policy Gradients
Differentiate the computational graph to train the policies using state-of-the-art deep learning practice.

## Slide 22: Differentiable Predictive Control (DPC)
From data to optimized explicit predictive control policy
  Online optimization
  Optimize for control actions
  Implicit solver-based control policy
  Offline optimization
  Optimize for control policy parameters
  Explicit neural control policy
MPC
DPC
Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022
Cost:
Model:
Constraints:

## Slide 23: Differentiable Computational Graphs and Model-based Policy Gradients
https://github.com/pnnl/neuromancer
Constructing differentiable computational graph: implementing parametric MPC problem in Pytorch.
https://pytorch.org/

## Slide 24: Differentiable Computational Graphs and Model-based Policy Gradients
https://github.com/pnnl/neuromancer
Forward pass: evaluate graph components (policy, model, constraints, objective terms) to compute structured learning loss function.

## Slide 25: Differentiable Computational Graphs and Model-based Policy Gradients
https://github.com/pnnl/neuromancer
Forward pass: evaluate graph components (policy, model, constraints, objective terms) to compute structured learning loss function.

## Slide 26: Differentiable Computational Graphs and Model-based Policy Gradients
https://github.com/pnnl/neuromancer
Forward pass: evaluate graph components (policy, model, constraints, objective terms) to compute structured learning loss function.

## Slide 27: Differentiable Computational Graphs and Model-based Policy Gradients
https://github.com/pnnl/neuromancer
Forward pass: evaluate graph components (policy, model, constraints, objective terms) to compute structured learning loss function.

## Slide 28: Differentiable Computational Graphs and Model-based Policy Gradients
https://github.com/pnnl/neuromancer
Forward pass: evaluate graph components (policy, model, constraints, objective terms) to compute structured learning loss function.

## Slide 29: Differentiable Computational Graphs and Model-based Policy Gradients
https://github.com/pnnl/neuromancer
Forward pass: evaluate graph components (policy, model, constraints, objective terms) to compute structured learning loss function.

## Slide 30: Differentiable Computational Graphs and Model-based Policy Gradients
Backward pass: Differentiate the computational graph to train the policies using state-of-the-art deep learning tools.
https://github.com/pnnl/neuromancer

## Slide 31: Learning to Stabilize Unstable System
Problem setup:
Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Constrained Adaptive Differentiable Predictive Control Policies With Guarantees, https://arxiv.org/abs/2004.11184
DPC formulation:

## Slide 32: Dynamics of DPC Control Policy Learning
1341 learning parameters, 48.2 seconds offline training time on a CPU with 200 epochs.
Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Constrained Adaptive Differentiable Predictive Control Policies With Guarantees, https://arxiv.org/abs/2004.11184

## Slide 33: Stochastic Differentiable Predictive Control
  Jan Drgona, Sayak Mukherjee, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Learning Stochastic Parametric Differentiable Predictive Control Policies, arXiv:2203.01447, to appear at IFAC ROCOND 2022
Stochastic
formulation
Robustness
to state noise
Stochastic obstacle avoidance
Parameters
Uncertainties

## Slide 34: Learning Stable Policies via Neural Lyapunov Differentiable Predictive Control
Sayak Mukherjee, Ján Drgoňa, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Neural Lyapunov Differentiable Predictive Control, arXiv:2205.10728, 2022

## Slide 35: Learning Safe Policies via Differentiable Predictive Control with Control Barrier Functions
Wenceslao Shaw Cortez, et al., Differentiable Predictive Control with Safety Guarantees: A Control Barrier Function Approach, arXiv:2208.02319, 2022

## Slide 36: Economic Differentiable Predictive Control of Building Energy System
  Jan Drgona, Aaron Tuor, Elliott Skomski, Soumya Vasisht, Draguna Vrabie, Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, IFAC NMPC 2021
Architectures
Neural state space dynamics model
MLP control policy architecture
Domain-aware constraints
Results
Multi-input multi-output system dynamics
Dynamic economic control objective
Parametric constraints

## Slide 37: Dynamics-Aware Economic Redispatch via Differentiable Predictive Control
Results
5 orders of magnitude speed-up
Minimal loss in solution quality
Ethan King, Ján Drgoňa, Aaron Tuor, Shrirang Abhyankar, Craig Bakker, Arnab Bhattacharya, Draguna Vrabie, Koopman-based Differentiable Predictive Control for the Dynamics-Aware Economic Dispatch Problem, The 2022 American Control Conference
Problem: Current redispatch processes do not incorporate system dynamics concerns. Incorporating dynamics in redispatch is too complex and/or time-consuming
Solution: Machine-learning based dynamics-aware redispatch. Learn system dynamics for faster assessment.
Architectures
Koopman dynamics model
CNN control policy

## Slide 38: Embedded Implementation of DPC
Flexy-Air system sketch with Raspberry-Pi controller
Performance comparison: reference (red dashed), position controlled with PI controller (green), explicit model predictive control (purple), constrained differentiable predictive control (blue) and constraints (black-dashed). Bottom figures show the fan speed controls
  Jan Drgona, Karol Kis, Aaron Tuor, Draguna Vrabie, Martin Klauco, Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning; Journal of Process Control, 2022

## Slide 39: Conclusion
SciML Methods
  Differentiable programming
  Parametric programming
  Constrained optimization
  Dynamical modeling and control
Ongoing work
  Constrained optimization solvers
  Graph neural networks (GNNs)
  Uncertainty Quantification (UQ)
Long-Term Vision
  Causal discovery, dynamical coupling, sensitivity, structure, and stability analysis, machine reasoning
  Solving large-scale parametric constrained optimization problems
  https://github.com/pnnl/neuromancer
  https://github.com/pnnl/slim

## Slide 40: Acknowledgements
James Koch
Zhao Chen
Stefan Dernbach
Draguna Vrabie
Aaron Tuor
Ethan King
Christian M. Legaard
Soumya Vasisht
Wenceslao Shaw Cortez
Sayak Mukherjee
Mahantesh Halappanavar
Shrirang Abhyankar