## Slide 1: Differentiable Programming for Modeling and Control of Dynamical Systems
PNNL-SA-#####
Ján Drgoňa
Aaron Tuor
Shrirang Abhyankar
Ethan King
Andrew August
Mia Skomski
James Koch
Zhao Chen
Soumya Vasisht
Sayak Mukherjee
Mahantesh Halappanavar
Draguna Vrabie
Notes: Image: Visualization of one years of Grid operation data with Gephi Graph Analytics

## Slide 2: Model Predictive Control
2
95% of the industrial control applications are PID loops & expert driven rule-based control (RBC).
The rest is model predictive control (MPC).
Modeling
  Unknown or partially known dynamics
  Physics-based modeling is expensive
  Purely data-driven models lack generalization
Real-time optimization
  Scalability
  Computational limitations of control hardware
  Parallelization, distributed optimization
Assumption:
Reliable and accurate system dynamics model
Drgona J., J. Arroyo, I.C. Figueroa, D. Blum, K. Arendt, D. Kim, and E.P. Olle, J. Oravec, M. Wetter, D. L. Vrabie, L. Helsen. 2020. "All You Need to Know About Model Predictive Control for Buildings." Annual Reviews in Control, September 29, 2020
Successes
Challenges

## Slide 3: Deep Reinforcement Learning
Everywhere where you are dealing with constraints, and stability guarantees. Learning on real system with low data and low compute regimes. Offline learning. High-dimensional continuous state and action systems. Partial observability, time delays. Task generalization and intrinsic rewards.
Challenges
Successes
Everywhere where you have reliable environment model, mostly discrete action space, and you can use massive compute to solve the problem.
G. Dulac-Arnold, D. J. Mankowitz, and T. Hester, “Challenges of real-world reinforcement learning,”, 2019.
http://arxiv.org/abs/1904.12901

## Slide 4: MPC vs RL
MPC - Requires system model
RL - Requires system environment
MPC – parametrized value functions
RL – unknown value functions
MPC – solves constrained optimization via solvers
RL – solves unconstrained optimization via backprop and gradient descent
MPC – implicit policy
RL – explicit neural policy
https://arxiv.org/abs/2005.01643
https://www.do-mpc.com/en/latest/
https://openocl.github.io/
https://www.argmin.net/2020/06/29/tour-revisited/

## Slide 5: MPC vs RL
https://arxiv.org/abs/2005.01643
https://www.argmin.net/2020/06/29/tour-revisited/

## Slide 6: Differentiable Predictive Control
From data to explicit constrained control policy via differentiable optimization
  Theoretical connection with MPC
  Neural dynamical system models
  Differentiable closed-loop model
  Model-based policy optimization
Notes: The conceptual methodology of DPC is illustrated here.
Assuming time series dataset obtained from the measurements of the system dynamics, in the first step, we perform system identification using a neural state-space model (SSM).
In the second step, we close the loop by combining the neural SSM with neural control law obtaining a differentiable closed-loop dynamics model fully parametrized by neural networks.
This allows us to leverage standard tools in deep learning to optimize the neural control laws by backpropagating the MPC loss function through the closed-loop dynamics.
Essentially this is a data-driven solution to multiparametric programming problems emerging from explicit nonlinear MPC.
Contrary to approximate MPC (aka imitation learning), DPC does not require supervision by an expert controller. Instead, a dynamics model is learned from a small dataset of system measurements, and the control law is then optimized offline by differentiating the learned system model.

## Slide 7: Differentiable Optimization as Lingua Franca for Scientific Computing
Standard form
Parametric programming
Lagrangian form
Machine learning
“online” optimization
single solution for
given parameter values
“offline” optimization
obtains a solution map
for a set of parameters classical methods lead to
exponential complexity!
“offline” optimization
obtains a model (map)
for a set of datapoints
scalable but classically
can’t handle constraints
“online” optimization
using soft constraints
instead of hard constraints
Differentiable parametric programming (DPP): a unifying approach for data-driven parametric programming problems with solutions based on automatic differentiation (AD)

## Slide 8: Differentiable Parametric Programming
Data-driven solution of
parametric quadratic program
train_data,dev_data,test_data = get_dataloaders(samples)
map = nm.map(input_keys=['p’], output_keys=[‘x’,‘y’], name='map')
x = Variable(‘x')
y = Variable('y')
p1 = Variable('p') f = x ** 2 + y ** 2 obj = f.minimize(weight=Q, name='obj’) g1 = -x - y + p1 con_1 = Q_con*(g1 <= 0)
objectives = [obj]
Constraints = [con_1] components = [map] model = Problem(objectives, constraints, components) optimizer = torch.optim.AdamW(model.parameters(), lr=args.lr) trainer = Trainer(model,train_data,dev_data,test_data,optimizer)
best_model = trainer.train()
  https://github.com/pnnl/neuromancer

## Slide 9: Differentiable Parametric Programming Computational Graphs in NeuroMANCER
Multi-parametric quadratic program (mpQP)
Differentiable predictive control (DPC)
  https://github.com/pnnl/neuromancer

## Slide 10: Neural State Space Models
fx
fu
fy
+
Linear
fx
fu
fy
+
Hammerstein
fx
fu
fy
+
Hammerstein-Weiner
fx
fu
fy
+
Block-Nonlinear
fxu
Unstructured
Linear map
Non-Linear map
yt+1
x0
xt
ut
ut
xt
xt+1
xt+1
yt+1
fy
fx
fu
fy
Koopman
fu o fy = I

## Slide 11: Structured Linear Maps (SLiM)
Factorizations and regularizations of linear maps with predetermined structure
Can be used to enforce sparsity or spectral properties
Spectral map
Perron-Frobenius map
  https://github.com/pnnl/slim

## Slide 12: Neural Ordinary Differential Equations
Goal: provide a suite of robust methods for interpretable, data-driven time-stepping
Methods:
Learning flow maps (MLPs and RNNs) for neural ODE implicit layers
ODE solution techniques: RK45, hierarchical, higher-order, implicit, multi-step
Physically-informed models: blend expert knowledge with neural ODE construction (ongoing)
PDEs
White-box:
Gray-box:
Black Box:
Applications: Grid infrastructure, molecular dynamics, damped-driven systems, seismic responses, building thermal dynamics, UAVs, etc.

## Slide 13: Neural ODE with Runge-Kutta Integration
Black-box neural ODE*:
Data: Brusselator oscillator
Ground-truth limit cycle
Red: model limit cycle
*NODE architecture is 2x10 MLP with Leaky ReLU activation.

## Slide 14: Learning to Stabilize Unstable System with Differentiable Predictive Control
Problem setup:
Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Constrained Adaptive Differentiable Predictive Control Policies With Guarantees
https://arxiv.org/abs/2004.11184
DPC formulation:

## Slide 15: DPC Policy Gradients and Optimization
Reward function
Policy
Constraints
penalties
Direct policy gradients

## Slide 16: Dynamics of DPC Control Policy Learning
1341 learning parameters, 48.2 seconds offline training time on a CPU with 200 epochs.

## Slide 17: Stochastic Parametric Differentiable Predictive Control
  Jan Drgona, Sayak Mukherjee, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Learning Stochastic Parametric Differentiable Predictive Control Policies, under review for IFAC ROCOND 2022

## Slide 18: Stochastic Parametric Differentiable Predictive Control
  Jan Drgona, Sayak Mukherjee, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Learning Stochastic Parametric Differentiable Predictive Control Policies, under review for IFAC ROCOND 2022

## Slide 19: Economic Differentiable Predictive Control of Building Energy System
  Jan Drgona, Aaron Tuor, Elliott Skomski, Soumya Vasisht, Draguna Vrabie, Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, IFAC NMPC 2021
Neural state space dynamics model
MLP control policy architecture
Results
Handling multi-input multi-output nonlinear dynamics
Dynamic economic control objective
Parametric constraints

## Slide 20: Dynamics-Aware Economic Redispatch via Differentiable Predictive Control
Results
5 orders of magnitude speed-up
Minimal loss in solution quality
Ethan King, Ján Drgoňa, Aaron Tuor, Shrirang Abhyankar, Craig Bakker, Arnab Bhattacharya, Draguna Vrabie, Koopman-based Differentiable Predictive Control for the Dynamics-Aware Economic Dispatch Problem, The 2022 American Control Conference (accepted)
Problem: Current redispatch processes do not incorporate system stability concerns. Incorporating stability in redispatch is too complex and/or time-consuming
Solution: Machine-learning based dynamics-aware redispatch. Learn system dynamics for faster assessment.
KO dynamics model
CNN control policy framework
Notes: Add waveform figure as a result – copy from previous slide replace discretize linearize with one block as iterative method

## Slide 21: DPC Wrap Up
Differentiable Predictive Control
  Differentiable system models
  Explicit control policies
  State and input constraints
  Embedded implementation
  Theoretical connection with MPC
Open-source Code
  Neuromancer software package
    https://github.com/pnnl/neuromancer
  Structured linear maps in Pytorch
    https://pnnl.github.io/slim/
Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning https://arxiv.org/abs/2011.03699
Jan Drgona, Aaron Tuor, Draguna Vrabie, Constrained Physics-Informed Deep Learning for Stable System Identification and Control of Unknown Linear Systems https://arxiv.org/abs/2004.11184

## Slide 22: Research Opportunities via Differentiable Optimization
Safe model-based control via neural Lyapunov functions (ongoing)
Nonlinear system identification via neural state space models, neural ODEs
Control for partially observable systems via model-based state estimation
UQ for system identification and model-based control by leveraging robust and stochastic MPC ideas
Inverse RL
Systematic review and empirical comparison of MPC and RL on benchmarks

## Slide 23: NeuroMANCER Motivation and Aims
Simulations are crucial for many areas of decision-making and scientific discovery
Need: Improve computational efficiency and scalability for heterogenous scientific simulations
Objectives:
  Domain-agnostic software package and new modeling paradigm
  Scientific computing frameworks enhanced by data science
  Algorithmic speedups enhanced with HPC
Applications: Simulation, optimization, and control of dynamical systems (ODE, PDE, DAE, Hybrid systems)

## Slide 24: NeuroMANCER framework
What
  Open-source scientific machine learning (SciML) framework in Python for integrating deep learning, constrained optimization, and physics-based modeling
Current applications
  Power systems (DMC initiative)
  Molecular dynamics (DMC initiative)
  Building control (CRADA BTO)
  Underwater autonomous vehicle (MARS initiative)
Approaches
  Physics-informed, data-driven modeling and control
  Parametric programming (Sensitivity Analysis)
  Differentiable programming (Automatic Differentiation)
https://github.com/pnnl/neuromancer

## Slide 25: NeuroMANCER Supported Problems
Differentiable parametric programming (DPP)
  Linear, Quadratic, Nonlinear programs (LP, QP, NLP)
  Mixed integer nonlinear programming (MINLP) (ongoing)
Physics-informed system identification
  Neural state space models (NSSM)
  Neural ordinary differential equations (NODE)
Differentiable predictive control (DPC)
  Constrained parametric optimal control problems
Constrained ML
  Classical deep learning (RNN, MLP, ResNet)
  Graph neural nets (GNNs)
https://github.com/pnnl/neuromancer/tree/master/examples

## Slide 26: Conclusion
NeuroMANCER
  Differentiable programming
  Parametric programming
  Constrained optimization
  Dynamical modeling and control
Ongoing work
  Parametric solvers (pIPOPT, etc.)
  Graph neural networks (GNNs)
  Mixed-integer programs (MIP)
  Uncertainty Quantification (UQ)
Long-Term Vision
  Causal discovery, dynamical coupling, sensitivity, structure, and stability analysis, machine reasoning
  Solving large-scale non-convex parametric constrained optimization problems
  https://github.com/pnnl/neuromancer
  https://github.com/pnnl/slim