## Slide 1: Differentiable programming for modeling and control of energy systems
Ján Drgoňa Collaborators: Aaron Tuor, Shrirang Abhyankar, Ethan King, James Koch, Zhao Chen, Soumya Vasisht, Vikas Chandan, Draguna Vrabie
Dealer talk at PARC

## Slide 2: Challenge 1: Systems Modeling
Simulations are crucial for many areas of decision-making and scientific discovery
Need: Improve computational efficiency and scalability for heterogenous scientific simulations
Objectives:
  Domain-agnostic software and algorithmic framework
  Scientific computing enhanced by data science
  Algorithmic speedups enhanced with HPC
Applications: Optimization, modeling and control of dynamical systems (ODE, PDE, DAE, Hybrid systems)

## Slide 3: Challenge 2: Systems Control
Model Predictive Control
Reinforcement Learning
Everywhere where you have reliable digital environment model, mostly discrete action space, and you can use massive compute to solve the problem.
Drgona J., J. Arroyo, I.C. Figueroa, D. Blum, K. Arendt, D. Kim, and E.P. Olle, J. Oravec, M. Wetter, D. L. Vrabie, L. Helsen. 2020. "All You Need to Know About Model Predictive Control for Buildings." Annual Reviews in Control, September 29, 2020
G. Dulac-Arnold, D. J. Mankowitz, and T. Hester, “Challenges of real-world reinforcement learning,”, 2019. http://arxiv.org/abs/1904.12901
95% of the industrial control applications are PID loops & expert driven rule-based control (RBC).
The rest is model predictive control (MPC).

## Slide 4: Landscape of Optimization Methods
Online optimization
Parametric programming
Imitation Learning
“online” solution for given parameter values
computationally demanding in real-time
“offline” optimization obtains a solution map
classical methods lead to exponential complexity!
“offline” optimization
obtains a model (map)
scalable but requires expert controller
Reinforcement Learning
“offline” optimization
obtains a policy map
classically can’t handle constraints

## Slide 5: Landscape of Optimization Methods
Online optimization
Parametric programming
Imitation Learning
“online” solution for given parameter values
computationally demanding in real-time
“offline” optimization obtains a solution map
classical methods lead to exponential complexity!
“offline” optimization
obtains a model (map)
scalable but requires expert controller
Reinforcement Learning
“offline” optimization
obtains a policy map
classically can’t handle constraints
Differentiable parametric programming (DPP): a unifying approach for data-driven parametric programming optimization with solutions based on automatic differentiation (AD)

## Slide 6: Differentiable Parametric Programming: Generalization of PINNs
Problem formulation:

## Slide 7: Differentiable Parametric Programming: Generalization of PINNs
Objective function
Constraints
Scenarios
Parameters
Solution map
Primal optimizers
Problem formulation:

## Slide 8: Differentiable Parametric Programming: Generalization of PINNs
Objective function
Constraints
Scenarios
Parameters
Solution map
Primal optimizers
Problem formulation:
Lagrangian form:
Constraints penalties
Gradient-based optimization based on AD

## Slide 9: Differentiable Parametric Programming: NeuroMANCER toolbox
train_data, dev_data, test_data = get_dataloaders(samples)
p = Variable(‘p’) # sampled parameter
x = Variable(‘x’) # decision variable
y = Variable('y’) # decision variable
map = nm.MLP(input_keys=['p’], output_keys=[‘x’,‘y’], name='map’)
# parametric solution map
f = x ** 2 + y ** 2 obj = f.minimize(weight=Q, name='obj’) # objective function con_1 = Q_con*(-x - y + p <= 0) # constraint
con_2 = Q_con*(-x + y + p <= 0) # constraint
objectives = [obj]
constraints = [con_1, con_2] components = [map]
loss = PenaltyLoss(objectives, constraints, train_data) problem = Problem(components, loss) # differentiable optimization optimizer = torch.optim.AdamW(problem.parameters(), lr=args.lr) trainer = Trainer(problem,train_data,dev_data,test_data,optimizer)
best_model = trainer.train()
  https://github.com/pnnl/neuromancer
Neural Modules with Adaptive Nonlinear Constraints and Efficient Regularizations

## Slide 10: Differentiable Parametric Programming: Computational Graphs
Parametric nonlinear programs
Orders of magnitude faster online solution compared to online optimization solvers (IPOPT).

## Slide 11: Neural State Space Models
fx
fu
fy
+
Linear
fx
fu
fy
+
Hammerstein
fx
fu
fy
+
Hammerstein-Weiner
fx
fu
fy
+
Block-Nonlinear
fxu
Unstructured
Linear map
Non-Linear map
yt+1
x0
xt
ut
ut
xt
xt+1
xt+1
yt+1
fy
fx
fu
fy
Koopman
fu o fy = I

## Slide 12: Bottom-Up Approach: Structured Linear Maps (SLiM)
Factorizations and regularizations of linear maps with predetermined structure
Can be used to enforce sparsity or spectral properties
Spectral map
Perron-Frobenius map
  https://github.com/pnnl/slim

## Slide 13: Modeling Thermal Dynamics
Ján Drgona, et al., Physics-constrained deep learning of multi-zone building thermal dynamics, Energy and Buildings, 2021

## Slide 14: Open-loop Trajectories of Linear Model

## Slide 15: Open-loop Trajectories of Neural Model

## Slide 16: Differentiable Predictive Control
Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Constrained Adaptive Differentiable Predictive Control Policies With Guarantees, 2021,
https://arxiv.org/abs/2004.11184
Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022, https://arxiv.org/abs/2011.03699
Constrained Model-based Policy Optimization for Parametric Optimal Control

## Slide 17: Learning to Stabilize Unstable System
Problem setup:
Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Constrained Adaptive Differentiable Predictive Control Policies With Guarantees, https://arxiv.org/abs/2004.11184
DPC formulation:

## Slide 18: Differentiable Computational Graphs and Model-based Policy Gradients
Differentiate the computational graph to train the policies using state-of-the-art deep learning practice.

## Slide 19: Dynamics of DPC Control Policy Learning
1341 learning parameters, 48.2 seconds offline training time on a CPU with 200 epochs.
Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Constrained Adaptive Differentiable Predictive Control Policies With Guarantees, https://arxiv.org/abs/2004.11184

## Slide 20: Stochastic Differentiable Predictive Control
  Jan Drgona, Sayak Mukherjee, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Learning Stochastic Parametric Differentiable Predictive Control Policies, arXiv:2203.01447, to appear at IFAC ROCOND 2022
Stochastic
formulation
Robustness
to state noise
Stochastic obstacle avoidance
Parameters
Uncertainties

## Slide 21: Economic Differentiable Predictive Control of Building Energy System
  Jan Drgona, Aaron Tuor, Elliott Skomski, Soumya Vasisht, Draguna Vrabie, Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, IFAC NMPC 2021
Architectures
Neural state space dynamics model
MLP control policy architecture
Domain-aware constraints
Results
Multi-input multi-output system dynamics
Dynamic economic control objective
Parametric constraints

## Slide 22: Dynamics-Aware Economic Redispatch via Differentiable Predictive Control
Results
5 orders of magnitude speed-up
Minimal loss in solution quality
Ethan King, Ján Drgoňa, Aaron Tuor, Shrirang Abhyankar, Craig Bakker, Arnab Bhattacharya, Draguna Vrabie, Koopman-based Differentiable Predictive Control for the Dynamics-Aware Economic Dispatch Problem, The 2022 American Control Conference
Problem: Current redispatch processes do not incorporate system dynamics concerns. Incorporating dynamics in redispatch is too complex and/or time-consuming
Solution: Machine-learning based dynamics-aware redispatch. Learn system dynamics for faster assessment.
Architectures
Koopman dynamics model
CNN control policy

## Slide 23: Embedded Implementation of DPC
Flexy-Air system sketch with Raspberry-Pi controller
Performance comparison: reference (red dashed), position controlled with PI controller (green), explicit model predictive control (purple), constrained differentiable predictive control (blue) and constraints (black-dashed). Bottom figures show the fan speed controls
  Jan Drgona, Karol Kis, Aaron Tuor, Draguna Vrabie, Martin Klauco, Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning; Journal of Process Control, 2022

## Slide 24: Conclusion
SciML Methods
  Differentiable programming
  Parametric programming
  Constrained optimization
  Dynamical modeling and control
Ongoing work
  Constrained optimization solvers
  Graph neural networks (GNNs)
  Uncertainty Quantification (UQ)
Long-Term Vision
  Causal discovery, dynamical coupling, sensitivity, structure, and stability analysis, machine reasoning
  Solving large-scale parametric constrained optimization problems
  https://github.com/pnnl/neuromancer
  https://github.com/pnnl/slim

## Slide 25: NeuroMANCER
Open-source scientific machine learning (SciML) toolbox in Python for integrating deep learning, constrained optimization, and physics-based modeling
Differentiable constrained optimization
  Parametric nonlinear programs (pNLP)
Constrained machine learning
  Classical deep learning (RNN, MLP, ResNet)
  Graph neural nets (GNNs)
Physics-informed modeling of dynamic systems
  Neural state space models (NSSM)
  Neural ordinary differential equations (NODE)
Constrained control of dynamic systems
  Differentiable predictive control (DPC)
https://github.com/pnnl/neuromancer/tree/master/examples

## Slide 26: Additional details on Neuromancer Technology

## Slide 27: Learning Stable Policies via Neural Lyapunov Differentiable Predictive Control
Sayak Mukherjee, Ján Drgoňa, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Neural Lyapunov Differentiable Predictive Control, arXiv:2205.10728, 2022

## Slide 28: Learning Stable via Neural Lyapunov Differentiable Predictive Control
Gaurav Manek, J. Zico Kolter, Learning Stable Deep Dynamics Models, NeurIPS 2019.
Lyapunov stability condition
Trivial null-space via coordinate shift
Neural Lyapunov Functions
Lyapunov regularization
Neural Lyapunov DPC
Input-convex neural network
Sayak Mukherjee, Ján Drgoňa, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Neural Lyapunov Differentiable Predictive Control, arXiv:2205.10728, 2022