## Slide 1: Differentiable Optimization as Lingua Franca for Scientific Machine Learning
Ján Drgoňa Collaborators: Aaron Tuor, Ethan King, Shrirang Abhyankar, Sayak Mukherjee, Mahantesh Halappanavar, Draguna Vrabie
2022 Sandia Machine Learning and Deep Learning (MLDL) Workshop

## Slide 2: SciML Motivation and Aims
Simulations are crucial for many areas of decision-making and scientific discovery
Need: Improve computational efficiency and scalability for heterogenous scientific simulations
Objectives:
  Domain-agnostic software and algorithmic framework
  Scientific computing enhanced by data science
  Algorithmic speedups enhanced with HPC
Applications: Optimization, modeling and control of dynamical systems (ODE, PDE, DAE, Hybrid systems)

## Slide 3: Landscape of Optimization Methods
Online optimization
Parametric programming
Imitation Learning
“online” solution for given parameter values
computationally demanding in real-time
“offline” optimization obtains a solution map
classical methods lead to exponential complexity!
“offline” optimization
obtains a model (map)
scalable but requires expert controller
Reinforcement Learning
“offline” optimization
obtains a policy map
classically can’t handle constraints

## Slide 4: Landscape of Optimization Methods
Online optimization
Parametric programming
Imitation Learning
“online” solution for given parameter values
computationally demanding in real-time
“offline” optimization obtains a solution map
classical methods lead to exponential complexity!
“offline” optimization
obtains a model (map)
scalable but requires expert controller
Reinforcement Learning
“offline” optimization
obtains a policy map
classically can’t handle constraints
Differentiable parametric programming (DPP): a unifying approach for data-driven parametric programming optimization with solutions based on automatic differentiation (AD)

## Slide 5: Differentiable Parametric Programming: Generalization of PINNs
Objective function
Constraints
Scenarios
Parameters
Solution map
Primal optimizers
Problem formulation:

## Slide 6: Differentiable Parametric Programming: Generalization of PINNs
Objective function
Constraints
Scenarios
Parameters
Solution map
Primal optimizers
Problem formulation:
Lagrangian form:
Constraints penalties
Gradient-based optimization based on AD

## Slide 7: Differentiable Parametric Programming: NeuroMANCER toolbox
train_data, dev_data, test_data = get_dataloaders(samples)
p = Variable(‘p’) # sampled parameter
x = Variable(‘x’) # decision variable
y = Variable('y’) # decision variable
map = nm.MLP(input_keys=['p’], output_keys=[‘x’,‘y’], name='map’)
# parametric solution map
f = x ** 2 + y ** 2 obj = f.minimize(weight=Q, name='obj’) # objective function con_1 = Q_con*(-x - y + p <= 0) # constraint
con_2 = Q_con*(-x + y + p <= 0) # constraint
objectives = [obj]
constraints = [con_1, con_2] components = [map]
loss = PenaltyLoss(objectives, constraints, train_data) problem = Problem(components, loss) # differentiable optimization optimizer = torch.optim.AdamW(problem.parameters(), lr=args.lr) trainer = Trainer(problem,train_data,dev_data,test_data,optimizer)
best_model = trainer.train()
  https://github.com/pnnl/neuromancer
Neural Modules with Adaptive Nonlinear Constraints and Efficient Regularizations

## Slide 8: Differentiable Parametric Programming: Computational Graphs
Parametric nonlinear programs
Orders of magnitude faster online solution compared to online optimization solvers (IPOPT).

## Slide 9: Differentiable Predictive Control
Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Constrained Adaptive Differentiable Predictive Control Policies With Guarantees
https://arxiv.org/abs/2004.11184
Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning https://arxiv.org/abs/2011.03699
Constrained Model-based Policy Optimization for Parametric Optimal Control

## Slide 10: Learning to Stabilize Unstable System
Problem setup:
Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Constrained Adaptive Differentiable Predictive Control Policies With Guarantees, https://arxiv.org/abs/2004.11184
DPC formulation:

## Slide 11: Dynamics of DPC Control Policy Learning
1341 learning parameters, 48.2 seconds offline training time on a CPU with 200 epochs.
Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Constrained Adaptive Differentiable Predictive Control Policies With Guarantees, https://arxiv.org/abs/2004.11184

## Slide 12: Stochastic Differentiable Predictive Control
  Jan Drgona, Sayak Mukherjee, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Learning Stochastic Parametric Differentiable Predictive Control Policies, arXiv:2203.01447, to appear at IFAC ROCOND 2022
Stochastic
formulation
Robustness
to state noise
Stochastic obstacle avoidance
Parameters
Uncertainties

## Slide 13: Dynamics-Aware Economic Redispatch via Differentiable Predictive Control
Results
5 orders of magnitude speed-up
Minimal loss in solution quality
Ethan King, Ján Drgoňa, Aaron Tuor, Shrirang Abhyankar, Craig Bakker, Arnab Bhattacharya, Draguna Vrabie, Koopman-based Differentiable Predictive Control for the Dynamics-Aware Economic Dispatch Problem, The 2022 American Control Conference (ACC)
Problem: Current redispatch processes do not incorporate system dynamics concerns. Incorporating dynamics in redispatch is too complex and/or time-consuming
Solution: Machine-learning based dynamics-aware redispatch. Learn system dynamics for faster assessment.
Architectures
Koopman dynamics model
CNN control policy

## Slide 14: Conclusion
NeuroMANCER
  Differentiable programming
  Parametric programming
  Constrained optimization
  Dynamical modeling and control
Ongoing work
  Constrained optimization solvers
  Graph neural networks (GNNs)
  Mixed-integer programs (MIP)
  Uncertainty Quantification (UQ)
Long-Term Vision
  Causal discovery, dynamical coupling, sensitivity, structure, and stability analysis, machine reasoning
  Solving large-scale non-convex parametric constrained optimization problems
  https://github.com/pnnl/neuromancer
  https://github.com/pnnl/slim

## Slide 15: Learning Stable Policies via Neural Lyapunov Differentiable Predictive Control
Sayak Mukherjee, Ján Drgoňa, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Neural Lyapunov Differentiable Predictive Control, arXiv:2205.10728, accepted to IEEE Conference on Decision and Control, 2022

## Slide 16: Model Predictive Control vs Deep Reinforcement Learning
MPC
RL
Everywhere where you have reliable digital environment model, mostly discrete action space, and you can use massive compute to solve the problem.
Drgona J., J. Arroyo, I.C. Figueroa, D. Blum, K. Arendt, D. Kim, and E.P. Olle, J. Oravec, M. Wetter, D. L. Vrabie, L. Helsen. 2020. "All You Need to Know About Model Predictive Control for Buildings." Annual Reviews in Control, September 29, 2020
G. Dulac-Arnold, D. J. Mankowitz, and T. Hester, “Challenges of real-world reinforcement learning,”, 2019.
http://arxiv.org/abs/1904.12901
95% of the industrial control applications are PID loops & expert driven rule-based control (RBC).
The rest is model predictive control (MPC).