## Slide 1: Differentiable programming for modeling and control of energy systems
Ján Drgoňa Collaborators: Aaron Tuor, Shrirang Abhyankar, Ethan King, James Koch, Zhao Chen, Soumya Vasisht, Vikas Chandan, Wenceslao Shaw Cortez, Sayak Mukherjee, Mahantesh Halappanavar, Draguna Vrabie
IEEE 8th World Forum on Internet of Things Yokohama, Japan

## Slide 2: Challenge 1: Systems Modeling
Simulations are crucial for many areas of decision-making and scientific discovery
Need: Improve computational efficiency and scalability for heterogenous scientific simulations
Approach: Integration of machine learning with physics-based models
Applications: building energy systems, power systems, molecular dynamics, unmanned vehicles

## Slide 3: Universal Differential Equations
Methods:
Learning flow maps (MLPs and RNNs) for neural ODE implicit layers
ODE solution techniques: RK45, hierarchical, higher-order, implicit, multi-step
Physically-informed models: blend expert knowledge with neural ODE construction
Graph structured neural ODEs
White-box:
Gray-box:
Black Box:
  Christopher Rackauckas, et al., Neural Ordinary Differential Equations, arXiv:2001.04385, 2019 James Koch, et al., Structural Inference of Networked Dynamical Systems with Universal Differential Equations, arXiv:2207.04962, 2022

## Slide 4: Networked Dynamical Systems via Universal Differential Equations
  Christopher Rackauckas, et al., Neural Ordinary Differential Equations, arXiv:2001.04385, 2019 James Koch, et al., Structural Inference of Networked Dynamical Systems with Universal Differential Equations, arXiv:2207.04962, 2022
Network of unknown oscillators
Coupling adjacency
Ground truth Kuramoto system:
Qualitative generalization of learned dynamics on never-seen network topology.

## Slide 5: Application: Modeling Thermal Dynamics
Ján Drgona, et al., Physics-constrained deep learning of multi-zone building thermal dynamics, Energy and Buildings, 2021

## Slide 6: Modeling Thermal Dynamics
Ján Drgona, et al., Physics-constrained deep learning of multi-zone building thermal dynamics, Energy and Buildings, 2021

## Slide 7: Open-loop Trajectories of Neural Model

## Slide 8: Challenge 2: Systems Control
Model Predictive Control
Reinforcement Learning
Everywhere where you have reliable digital environment model, mostly discrete action space, and you can use massive compute to solve the problem.
Drgona J., J. Arroyo, I.C. Figueroa, D. Blum, K. Arendt, D. Kim, and E.P. Olle, J. Oravec, M. Wetter, D. L. Vrabie, L. Helsen. 2020. "All You Need to Know About Model Predictive Control for Buildings." Annual Reviews in Control, September 29, 2020
G. Dulac-Arnold, D. J. Mankowitz, and T. Hester, “Challenges of real-world reinforcement learning,”, 2019. http://arxiv.org/abs/1904.12901
95% of the industrial control applications are PID loops & expert driven rule-based control (RBC).
The rest is model predictive control (MPC).

## Slide 9: Landscape of Optimization Methods
Online optimization
Parametric programming
Imitation Learning
“online” solution for given parameter values
computationally demanding in real-time
“offline” optimization obtains a solution map
classical methods lead to exponential complexity!
“offline” optimization
obtains a model (map)
scalable but requires expert controller
Reinforcement Learning
“offline” optimization
obtains a policy map
classically can’t handle constraints
Differentiable programming (DP): a unifying approach for data-driven parametric optimization with solutions based on automatic differentiation (AD)

## Slide 10: Differentiable Predictive Control
Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Constrained Adaptive Differentiable Predictive Control Policies With Guarantees, 2021,
https://arxiv.org/abs/2004.11184
Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022, https://arxiv.org/abs/2011.03699
Constrained Model-based Policy Optimization for Parametric Optimal Control

## Slide 11: Learning to Stabilize Unstable System
Problem setup:
Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Constrained Adaptive Differentiable Predictive Control Policies With Guarantees, https://arxiv.org/abs/2004.11184
DPC formulation:

## Slide 12: Differentiable Computational Graphs and Model-based Policy Gradients
Differentiate the computational graph to train the policies using state-of-the-art deep learning practice.

## Slide 13: Dynamics of DPC Control Policy Learning
1341 learning parameters, 48.2 seconds offline training time on a CPU with 200 epochs.
Jan Drgona, Aaron Tuor, Draguna Vrabie, Learning Constrained Adaptive Differentiable Predictive Control Policies With Guarantees, https://arxiv.org/abs/2004.11184

## Slide 14: Stochastic Differentiable Predictive Control
  Jan Drgona, Sayak Mukherjee, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Learning Stochastic Parametric Differentiable Predictive Control Policies, arXiv:2203.01447, IFAC ROCOND 2022
Stochastic
formulation
Robustness
to state noise
Stochastic obstacle avoidance
Parameters
Uncertainties

## Slide 15: Learning Stable Policies via Neural Lyapunov Differentiable Predictive Control
Sayak Mukherjee, Ján Drgoňa, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Neural Lyapunov Differentiable Predictive Control, arXiv:2205.10728, IEEE CDC, 2022

## Slide 16: Learning Safe Policies via Differentiable Predictive Control with Control Barrier Functions
Wenceslao Shaw Cortez, et al., Differentiable Predictive Control with Safety Guarantees: A Control Barrier Function Approach, arXiv:2208.02319, IEEE CDC, 2022

## Slide 17: Economic Differentiable Predictive Control of Building Energy System
  Jan Drgona, Aaron Tuor, Elliott Skomski, Soumya Vasisht, Draguna Vrabie, Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, IFAC NMPC 2021
Architectures
Neural state space dynamics model
MLP control policy architecture
Domain-aware constraints
Results
Multi-input multi-output system dynamics
Dynamic economic control objective
Parametric constraints

## Slide 18: Dynamics-Aware Economic Redispatch via Differentiable Predictive Control
Results
5 orders of magnitude speed-up
Minimal loss in solution quality
Ethan King, Ján Drgoňa, Aaron Tuor, Shrirang Abhyankar, Craig Bakker, Arnab Bhattacharya, Draguna Vrabie, Koopman-based Differentiable Predictive Control for the Dynamics-Aware Economic Dispatch Problem, The 2022 American Control Conference
Problem: Current redispatch processes do not incorporate system dynamics concerns. Incorporating dynamics in redispatch is too complex and/or time-consuming
Solution: Machine-learning based dynamics-aware redispatch. Learn system dynamics and parametric control policy offline for faster assessment.
Architectures
Koopman dynamics model
CNN control policy

## Slide 19: Embedded Implementation of DPC
Flexy-Air system sketch with Raspberry-Pi controller
Performance comparison: reference (red dashed), position controlled with PI controller (green), explicit model predictive control (purple), constrained differentiable predictive control (blue) and constraints (black-dashed). Bottom figures show the fan speed controls
  Jan Drgona, Karol Kis, Aaron Tuor, Draguna Vrabie, Martin Klauco, Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning; Journal of Process Control, 2022

## Slide 20: Differentiable Parametric Programming: NeuroMANCER toolbox
train_data, dev_data, test_data = get_dataloaders(samples)
p = Variable(‘p’) # sampled parameter
x = Variable(‘x’) # decision variable
y = Variable('y’) # decision variable
map = nm.MLP(input_keys=['p’], output_keys=[‘x’,‘y’], name='map’)
# parametric solution map
f = x ** 2 + y ** 2 obj = f.minimize(weight=Q, name='obj’) # objective function con_1 = Q_con*(-x - y + p <= 0) # constraint
con_2 = Q_con*(-x + y + p <= 0) # constraint
objectives = [obj]
constraints = [con_1, con_2] components = [map]
loss = PenaltyLoss(objectives, constraints, train_data) problem = Problem(components, loss) # differentiable optimization optimizer = torch.optim.AdamW(problem.parameters(), lr=args.lr) trainer = Trainer(problem,train_data,dev_data,test_data,optimizer)
best_model = trainer.train()
  https://github.com/pnnl/neuromancer
Neural Modules with Adaptive Nonlinear Constraints and Efficient Regularizations

## Slide 21: Conclusion
SciML Methods
  Differentiable programming
  Parametric programming
  Constrained optimization
  Dynamical modeling and control
Long-Term Vision
  Causal discovery, dynamical coupling, sensitivity, structure, and stability analysis, machine reasoning
  Solving large-scale parametric constrained optimization problems
Open-source code
  https://github.com/pnnl/neuromancer
  https://github.com/pnnl/slim

## Slide 22: Climate Change AI Catalyzing impactful work at the intersection of climate change & ML
Reports with opportunities for researchers, practitioners, and policymakers
New community-driven Wiki w/ datasets & additional resources
Digital resources
Webinars & happy hours
Newsletter, blog, & community
Calls for Submissions Funding Projects & Courses
Readings Jobs
Learn more & join in:
www.climatechange.ai
@ClimateChangeAI
Webinar series (monthly)
Virtual happy hours (biweekly)
Global research funding
for impactful projects
Funding programs
Workshop series
Submit or attend @ NeurIPS '22
Mentorship programs
www.climatechange.ai/papers
Summer school (multiple tracks)
Conferences & events

## Slide 23: Structured Linear Maps (SLiM)
Factorizations and regularizations of linear maps with predetermined structure
Can be used to enforce sparsity or spectral properties
Spectral map
Perron-Frobenius map
  https://github.com/pnnl/slim

## Slide 24: Parametric Optimization via Differentiable Programming: Generalization of PINNs
Objective function
Constraints
Scenarios
Parameters
Solution map
Primal optimizers
Problem formulation:
Lagrangian form:
Constraints penalties
Gradient-based optimization based on AD

## Slide 25: Differentiable Parametric Programming: Computational Graphs
Parametric nonlinear programs
Orders of magnitude faster online solution compared to online optimization solvers (IPOPT).