## Slide 1: Scientific Machine Learning for Modeling, Optimization, and Control
Ján Drgoňa
Associate Professor Civil and Systems Engineering Department The Ralph O'Connor Sustainable Energy Institute

## Slide 2: Optimizing Complex Energy Systems is Hard
Simulations are crucial for optimal decision-making in complex energy systems
Need: Improve computational efficiency and scalability of digital twins and optimization-based decision-making
Challenges:
  Modeling and simulation of complex systems is hard
  Closed-loop decision-making for complex systems is hard-er
  Scientific computing and machine learning tools are fragmented and not easily composable

## Slide 3: Challenge 1: Heterogenous Modeling Methods
Data-driven
Physics-based
More domain knowledge
Less domain knowledge
White-box models
Gray-box models
Black-box models

## Slide 4: Challenge 2: Heterogenous Solution Methods
Constrained Optimization
Differential Equations
Supervised Learning
Requires prior knowledge of objective function and constraints
Requires prior knowledge of the physics to be modeled
Requires large labeled datasets
Reinforcement Learning
Requires environment model to sample
More domain knowledge
Less domain knowledge

## Slide 5: Challenge 3: Heterogenous Solution Tools
Constrained Optimization
Differential Equations
Supervised Learning
Reinforcement Learning
More domain knowledge
Less domain knowledge

## Slide 6: Scientific Machine Learning (SciML)
What?
SciML systematically integrates ML methods with mathematical models and algorithms developed in various scientific and engineering domains
Why?
Scientific applications are governed by fundamental principles and physical constraints
Purely data-driven “black box” ML methods cannot satisfy underlying physics
How?
Leverage automatic differentiation used in learning for modeling, optimization, and control
Image source: https://sciml.wur.nl/reviews/sciml/sciml.html
Karniadakis, G.E., Kevrekidis, I.G., Lu, L. et al. Physics-informed machine learning. Nat Rev Phys 3, 422–440, 2021.

## Slide 7: Automatic Differentiation (AD) in Machine Learning
Baydin, Atilim Gunes et al. Automatic differentiation in machine learning: a survey. Journal of Machine Learning Research, 2015
Animation source: wikipedia
Gradient Descent Algorithm
Backpropagation Algorithm
AD enables efficient and accurate gradient computation, which is fundamental for training complex ML models using GPUs.
SW and HW Innovations

## Slide 8: Selected Scientific Machine Learning Literature
Differentiable Programming
  M. Innes, et al., A Differentiable Programming System to Bridge Machine Learning and Scientific Computing, 2019
Learning to Solve (L2S)
  M. Raissi, et al., Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations, 2019
Learning to Optimize (L2O)
  A. Agrawal, et al., Differentiable Convex Optimization Layers, 2019
  P. Donti, et al., DC3: A learning method for optimization with hard constraints, 2021
  J. Kotary, et al., End-to-End Constrained Optimization Learning: A Survey, 2021
Learning to Model (L2M)
  B. Lusch, et al., Deep learning for universal linear embeddings of nonlinear dynamics, 2018
  R. T. Q. Chen, et al., Neural Ordinary Differential Equations, 2019
  C. Rackauckas, et al., Universal Differential Equations for Scientific Machine Learning, 2021
Learning to Control (L2C)
  B. Amos, et al., Differentiable MPC for End-to-end Planning and Control, 2019
  S. East, et al., Infinite-Horizon Differentiable Model Predictive Control, 2020
  Y Qiao, et al., Scalable Differentiable Physics for Learning and Control, 2020

## Slide 9: Components of Scientific Machine Learning
Karniadakis, G.E., Kevrekidis, I.G., Lu, L. et al. Physics-informed machine learning. Nat Rev Phys 3, 2021.
Thiyagalingam, J., Shankar, M., Fox, G. et al. Scientific machine learning benchmarks. Nature Reviews Physics 4, 413–420, 2022.
Nghiem T., Drgona J., et al. Physics-Informed Machine Learning for Modeling and Control of Dynamical Systems, ACC, 2023.

## Slide 10: Learning to Solve Differential Equations with Physics-Informed Neural Networks (PINNs)
Training neural networks as PDE solutions
Application: Parameter estimation from data
  M. Raissi, et al., Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations, Journal of Computational Physics, 2019
  Images: NVIDIA Modulus

## Slide 11: Learning to Solve Differential Equations with Physics-Informed Neural Networks (PINNs)
  M. Raissi, et al., Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations, Journal of Computational Physics, 2019
Dataset: collocation points in the spatio-temporal coordinates.
https://github.com/pnnl/neuromancer/blob/master/examples/PDEs/Part_2_PINN_BurgersEquation.ipynb
Architecture: PDE equations solved with neural network via automatic differentiation.
Loss function: minimizing PDE equation, initial and boundary condition residuals.

## Slide 12: Learning to Optimize (L2O) with Constraints
Training neural networks as optimization solutions
Application: solving optimal power flow
  James Kotary, et al., End-to-End Constrained Optimization Learning: A Survey, IJCAI, 2021

## Slide 13: Learning to Optimize (L2O) with Constraints
  A. Agrawal, et al., Differentiable Convex Optimization Layers, 2019
  P. Donti, et al., DC3: A learning method for optimization with hard constraints, 2021
Dataset: collocation points in the parametric space.
https://github.com/pnnl/neuromancer/blob/master/examples/parametric_programming/Part_1_basics.ipynb
Loss function: minimizing objective function and constraints penalties.
Architecture: differentiable optimization solver with neural network surrogate.

## Slide 14: Learning to Model (L2M) Dynamical Systems
Neural models for nonlinear system identification
Application: climate modeling
  R. T. Q. Chen, et al., Neural ordinary differential equations. NeurIPS, 2018
  C. Rackauckas, et al., Universal Differential Equations for Scientific Machine Learning, 2021
  Image: NVIDIA FourCastNet

## Slide 15: Learning to Model (L2M) Dynamical Systems
  R. T. Q. Chen, et al., Neural Ordinary Differential Equations, 2019
  B. Lusch, et al., Deep learning for universal linear embeddings of nonlinear dynamics, 2018
Dataset: time-series of states, inputs, and disturbances tuples.
Loss function: trajectory matching, regularizations, and constraints penalties.
Architecture: differentiable ODE solver with neural network model.
https://github.com/pnnl/neuromancer/blob/master/examples/ODEs/Part_1_NODE.ipynb
Architecture: Koopman operator with neural network basis functions.

## Slide 16: Learning to Control (L2C) via Differentiable Predictive Control (DPC)
Trajectory optimization for dynamical systems
Application: autonomous systems
J. Drgoňa, A. Tuor and D. Vrabie, "Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees," in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024

## Slide 17: Learning to Control (L2C) via Differentiable Predictive Control (DPC)
Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022
Dataset: collocation points in the control parametric space.
Loss function: reference tracking, constraints and terminal penalties.
Architecture: differentiable model with neural network control policy.
https://github.com/pnnl/neuromancer/blob/master/examples/control/Part_3_ref_tracking_ODE.ipynb

## Slide 18: Learning to Control (L2C) via Differentiable Predictive Control (DPC)
Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022
Dataset: collocation points in the control parametric space.
Loss function: reference tracking, constraints and terminal penalties.
Architecture: differentiable model with neural network control policy.
https://github.com/pnnl/neuromancer/blob/master/examples/control/Part_3_ref_tracking_ODE.ipynb
Follow up TuC04: 16:10-16:35

## Slide 19: Learning to Control Building Energy System
  J. Drgona, et al., Physics-constrained deep learning of multi-zone building thermal dynamics, Energy and Buildings, 2021
  J. Drgona, et al., Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, IFAC NMPC 2021
Benefits of Scientific Machine Learning
Modeling and optimal control design is roughly 10-times faster and requires less expertise.
Real-time decisions are made orders of magnitude faster than traditional model-based approaches.

## Slide 20: Learning to Control Power System
Ethan King, et al., Koopman-based Differentiable Predictive Control for the Dynamics-Aware Economic Dispatch Problem, American Control Conference 2022
Benefits of Scientific Machine Learning
Fast prototyping by re-using code template from building control project.
Real-time decisions are made orders of magnitude faster than traditional model-based approaches.

## Slide 21: Can We Use Scientific Machine Learning for Solving Mixed-Integer Nonlinear Programming (MINLP) Problems?

## Slide 22: Authors of Learning to Optimize for Mixed-Integer Non-Linear Programming
Ján Drgoňa
Associate Professor
Department of Civil and Systems Engineering and the Ralph S. O’Connor Sustainable Energy Institute
Johns Hopkins University
Bo Tang
PhD Candidate
Department of Mechanical & Industrial Engineering
University of Toronto
Elias B. Khalil
Assistant Professor
Department of Mechanical & Industrial Engineering
University of Toronto
SCALE AI Research Chair
Data-Driven Algorithms for Modern Supply Chains

## Slide 23: Challenges of Existing Learning to Optimize Methods
1. Collecting Solutions as Training Labels for Supervised Learning is Very Expensive
2. Neural Networks Cannot Directly Output Integer Values
Our Solution: Self-Supervised Learning Approach without requiring solutions for training.
Our Solution: Differentiable Integer Correction Layers to ensure integer feasibility.
Our Solution: Gradient-based Feasibility Projection to guarantee feasible integer solutions.
3. It is Difficult to Ensure Feasibility, Especially in Integers
  Selected Existing L2O methods Ferdinando Fioretto, et al., Predicting ac optimal power flows: Combining deep learning and lagrangian dual methods. AAAI conference on AI, 2020.
  Priya Donti, et al., DC3: A learning method for optimization with hard constraints, ICLR, 2021
  James Kotary, et al., End-to-end constrained optimization learning: A survey. arXiv preprint arXiv:2103.16378, 2021.
  He He, et al., Learning to search in branch and bound algorithms. NeurIPS, 2014.
  Elias Khalil, et al., Learning to branch in mixed integer programming. AAAI Conference on AI, 2016.
  Maxime Gasse, et al., Exact combinatorial optimization with graph convolutional neural networks. NeruIPS, 2019.
  Timo Berthold , et al., Learning to scale mixed-integer programs. AAAI Conference on AI, 2021.
  Yoshua Bengio, et al., Machine learning for combinatorial optimization: a methodological tour d’horizon. European Journal of Operational Research, 2021.
  Dimitris Bertsimas and Bartolomeo Stellato. Online mixed-integer optimization in milliseconds. INFORMS Journal on Computing, 2022.

## Slide 24: Learning to Optimize for Mixed-Integer Nonlinear Programming
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning problem formulation:
Penalty loss function reformulation:
Amortized optimization allows scaling to some of the largest MINLPs.
Could also be used as primal heuristics.

## Slide 25: Learning to Optimize for Mixed-Integer Nonlinear Programming
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning problem formulation:
Penalty loss function reformulation:
Parameters influence the objective and constraints of the optimization problem. We sample a set of problems from a distribution.

## Slide 26: Learning to Optimize for Mixed-Integer Nonlinear Programming
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning problem formulation:
Penalty loss function reformulation:
We aim to predict the solution with machine learning model with inputs and weights

## Slide 27: Learning to Optimize for Mixed-Integer Nonlinear Programming
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning problem formulation:
Penalty loss function reformulation:
Until now this is standard self-supervised L2O for continuous problems.

## Slide 28: Learning to Optimize for Mixed-Integer Nonlinear Programming
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning problem formulation:
Penalty loss function reformulation:
Main innovation of the paper: Integer correction layers and integer feasibility projection

## Slide 29: Differentiable Integer Correction Layers
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learnable end-to-end extension of the Relaxation Enforced Neighborhood Search (RENS).

## Slide 30: Differentiable Integer Correction Layers: RC Example
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 31: Integer Feasibility Projection
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning-based alternative to Feasibility Pump which also alternates between rounding and projection.

## Slide 32: Asymptotic Guarantees of Integer Feasibility Projection
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 33: L2O for MINLP: Comparison with SOTA Solvers
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Exact solvers such as Gurobi and SCIP can find better solutions over time but are slow. In contrast, our methods achieve high-quality feasible solutions within milliseconds. Our methods provide up to 5 orders of magnitude speedup.
https://github.com/pnnl/L2O-pMINLP

## Slide 34: Effect of Penalty Weight
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Our approach achieves comparable or better objective values compared to exact solvers.
https://github.com/pnnl/L2O-pMINLP

## Slide 35: Summary
Scientific machine learning (SciML) methods integrating deep learning, constrained optimization, physics-based modeling, and control
  Learning to solve (L2S)
  Learning to optimize (L2O)
  Learning to model (L2M)
  Learning to control (L2C)
Challenges
  Mixed-integer decisions
  Vanishing and exploding gradients
  Offline pre-training vs online adaptation
  Computational cost of uncertainty quantification and guarantees
Opportunities
  Sampling efficiency via active sampling strategies
  Control of high-dimensional PDEs
  Applications in large-scale safety-critical systems
  Development of new software tools

## Slide 36: Follow Up
Safe Physics-Informed Learning in Dynamics and Control
  TuB03 Tutorial Session, Plaza CF,13:30-15:00
Learning Interpretable Control Policies: Unifying Reinforcement Learning, Differentiable Programming and Bayesian Optimization
  TuC04 Tutorial Session, Governor's Sq. 15, 15:30-17:00,
NeuroMANCER Library tutorial – in 5 min
  github.com/pnnl/neuromancer
drgona.github.io jdrgona1@jh.edu

## Slide 37: NeuroMANCER Scientific Machine Learning Library
github.com/pnnl/neuromancer
Open-source library in PyTorch
Physics-informed Neural Networks
Learning to optimize
Neural differential equations
Learning to control

## Slide 38: NeuroMANCER Scientific Machine Learning Library
import neuromancer as nm
p = nm.variable(‘p’)
x = nm.variable(‘x’)
y = nm.variable('y’)
obj = ((1-x)**2 + p*(y-x**2)**2).minimize(weight=1.0, name='obj’) c1 = (p/2)**2 <= x**2 + y**2
c2 = x**2 + y**2 <= p**2
c3 = x >= y net = nm.MLP(insize=2, outsize=2, hsizes=[80]*4) map = nm.Node(net, input_keys=['p’], output_keys=[‘x’,‘y’])
loss = nm.PenaltyLoss([obj], [c1, c2, c3]) problem = nm.Problem([map], loss)
optimizer = torch.optim.AdamW(problem.parameters()) trainer = nm.Trainer(problem,data,optimizer)
best_model = trainer.train()
2. Python code interface
1. Mathematical formulation
4. Results
3. Problem graph
map

## Slide 39: NeuroMANCER Team
Aaron Tuor
Draguna
Vrabie
James Koch
Madelyn Shapiro
Rahul
Birmiwal
Bruno
Jacob

## Slide 40: Non-Asymptotic Guarantees of Integer Feasibility Projection
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 41: Benchmark Methods
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Method | Description
EX (Exact Solver) | Solves problems exactly using traditional solver with 1000-sec time-limit as a benchmark.
N1 (Root Node Solution) | Finds the first feasible solution from the root node of the solver, combining various heuristics.
RC (Rounding Classification) | A neural network-based correction layer that learns a classification to determine how to round each integer variable.
LT (Learnable Thresholding) | A neural network-based correction layer that learns a threshold value to decide to round up or down for each integer variable.
RC-P (RC + Feasibility Projection) | RC combined with feasibility projection, which corrects infeasibilities while preserving integer constraints.
LT-P (LT + Feasibility Projection) | LT combined with feasibility projection, which corrects infeasibilities while preserving integer constraints.

## Slide 42: L2O for MINLP: Empirical Evaluation
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Method | RC |  |  |  | RC-P |  |  |  | LT |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
100×100 | -13.54 | -13.6 | 96% | 0.0022 | -13.54 | -13.57 | 100% | 0.005 | -13.65 | -13.77 | 93% | 0.0023
200×200 | -31.62 | -31.71 | 97% | 0.0021 | -31.62 | -31.71 | 100% | 0.005 | -31.34 | -31.61 | 95% | 0.0022
500×500 | -73.31 | -73.38 | 86% | 0.0025 | -73.31 | -73.38 | 100% | 0.0065 | -72.36 | -72.48 | 94% | 0.0026
1000×1000 | -142.7 | -142.7 | 82% | 0.0042 | -142.7 | -142.7 | 100% | 0.009 | -142.6 | -142.6 | 100% | 0.0047
Method | LT-P |  |  |  | EX |  |  |  | N1 |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
100×100 | -13.65 | -13.77 | 100% | 0.01 | -20.79 | -20.78 | 100% | 1237 | 1.5E+18 | 1.4E+18 | 100% | 104.2
200×200 | -31.34 | -31.61 | 100% | 0.0064 | - | - | - | - | - | - | - | -
500×500 | -72.36 | -72.48 | 100% | 0.0063 | - | - | - | - | - | - | - | -
1000×1000 | -142.6 | -142.6 | 100% | 0.0086 | - | - | - | - | - | - | - | -
Integer Quadratic Problems (IQPs). Each problem size is evaluated on a test set of 100 instance.

## Slide 43: L2O for MINLP: Empirical Evaluation
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Integer Non-convex Problems (INPs). Each problem size is evaluated on a test set of 100 instance.
Method | RC |  |  |  | RC-P |  |  |  | LT |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
100×100 | 1.664 | 1.594 | 100% | 0.0022 | 1.664 | 1.594 | 100% | 0.0060 | 0.669 | 0.649 | 96% | 0.0021
200×200 | 1.472 | 1.436 | 99% | 0.0022 | 1.471 | 1.436 | 100% | 0.0054 | -0.356 | -0.373 | 100% | 0.0023
500×500 | 0.526 | 0.526 | 96% | 0.0029 | 0.524 | 0.526 | 100% | 0.0061 | -1.374 | -1.594 | 98% | 0.0029
1000×1000 | 1.423 | 0.809 | 97% | 0.0040 | 1.423 | 0.809 | 100% | 0.0115 | -3.744 | -3.716 | 99% | 0.0050
Method | LT-P |  |  |  | EX |  |  |  | N1 |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
100×100 | 0.669 | 0.649 | 100% | 0.0058 | 256.93 | 134.62 | 14% | 1001 | 4411 | 155.2 | 14% | 940.4
200×200 | -0.356 | -0.373 | 100% | 0.0056 | - | - | - | - | - | - | - | -
500×500 | -1.374 | -1.594 | 100% | 0.0072 | - | - | - | - | - | - | - | -
1000×1000 | -3.744 | -3.716 | 100% | 0.0117 | - | - | - | - | - | - | - | -

## Slide 44: L2O for MINLP: Empirical Evaluation
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Mixed-integer Rosenbrock Problems (MIRBs). Each problem size is evaluated on a test set of 100 instance.
Method | RC |  |  |  | RC-P |  |  |  | LT |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
20×4 | 59.39 | 48.86 | 100% | 0.0019 | 59.39 | 48.86 | 100% | 0.0048 | 62.51 | 63.40 | 100% | 0.0020
200×4 | 503.5 | 461.7 | 99% | 0.0021 | 504.2 | 461.7 | 100% | 0.0052 | 622.8 | 626.0 | 100% | 0.0026
50×4 | 5938 | 5792 | 99% | 0.0033 | 5942 | 5792 | 100% | 0.0070 | 5612 | 5558 | 97% | 0.0030
1000×4 | 6.7E+4 | 6.7E+4 | 76% | 0.0121 | 9.8E+4 | 7.3E+4 | 100% | 0.0824 | 4.8E+4 | 3.5E+4 | 66% | 0.0127
Method | LT-P |  |  |  | EX |  |  |  | N1 |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
20×4 | 62.51 | 63.40 | 100% | 0.0055 | 64.67 | 59.16 | 100% | 1005 | 87.83 | 77.34 | 100% | 0.0813
200×4 | 622.8 | 626.0 | 100% | 0.0062 | 8.4E+5 | 908.8 | 100% | 1002 | 3.7E+8 | 957.4 | 100% | 0.2608
2000×4 | 5615 | 5558 | 100% | 0.0071 | 4.7E+10 | 9262 | 96% | 1002 | 8.3E+12 | 9379 | 95% | 71.91
20000×4 | 8.0E+4 | 4.5E+4 | 100% | 0.0639 | 1.1E+15 | 1.0E5 | 78% | 1040 | 1.2E+15 | 1.0E5 | 78% | 782.1

## Slide 45: Effect of Penalty Weight
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Integer feasibility projection (RC-P and LT-P), improves feasibility even with smaller penalty weights. Without projection there is a trade-off between feasibility and objective values (RC and LT).