## Slide 1: Scientific Machine Learning for Modeling, Optimization, and Control with Safety Guarantees
Ján Drgoňa
Associate Professor Civil and Systems Engineering Department Electrical and Computer Engineering Department (secondary) The Ralph O'Connor Sustainable Energy Institute (ROSEI)
Data Science and AI Institute (DSAI)

## Slide 2
Why Safety Matters
Nominal conditions → system stable and constraints satisfied.
Notes: Paragliding is a beautiful sport — it lets you soar with the birds. This was me yesterday, enjoying a perfectly stable, nominal flight over Rio. But things can change quickly: an unexpected disturbance plus a bit of plant–model mismatch… and suddenly we have a constraint violation. A few moments later, this was me hanging in a tree while firefighters tried to figure out how to get me down. Don’t worry — nobody was hurt, except my ego. Today’s talk is about how to prevent that kind of thing from happening in our control systems.

## Slide 3
Why Safety Matters
Nominal conditions → system stable and constraints satisfied.
Plant-model mismatch + disturbance → constraints violation.
Few moments later

## Slide 4: Optimizing Complex Systems with Safety Guarantees is Hard
Simulations are crucial for optimal decision-making in complex energy systems
Need: Improve computational efficiency and scalability of digital twins and optimization-based decision-making
Challenges:
  Modeling and simulation of complex systems is hard
  Closed-loop decision-making for complex systems is hard-er
  Scientific computing and machine learning tools are fragmented and not easily composable
  Safety guarantees are critical

## Slide 5: Challenge 1: Heterogenous Modeling Methods
Data-driven
Physics-based
More domain knowledge
Less domain knowledge
White-box models
Gray-box models
Black-box models

## Slide 6: Challenge 2: Heterogenous Solution Methods
Constrained Optimization
Differential Equations
Supervised Learning
Requires prior knowledge of objective function and constraints
Requires prior knowledge of the physics to be modeled
Requires large labeled datasets
Reinforcement Learning
Requires environment model to sample
Less domain knowledge
More domain knowledge

## Slide 7: Challenge 3: Heterogenous Solution Tools
Constrained Optimization
Differential Equations
Supervised Learning
Reinforcement Learning
More domain knowledge
Less domain knowledge

## Slide 8: Automatic Differentiation (AD) in Machine Learning
Baydin, Atilim Gunes et al. Automatic differentiation in machine learning: a survey. Journal of Machine Learning Research, 2015
Animation source: wikipedia
Gradient Descent Algorithm
Backpropagation Algorithm
AD enables efficient and accurate gradient computation, which is fundamental for training complex ML models using GPUs.
SW and HW Innovations

## Slide 9
What?
SciML systematically integrates ML methods with mathematical models and algorithms developed in various scientific and engineering domains
Why?
Scientific applications are governed by fundamental principles and physical constraints
Purely data-driven “black box” ML methods cannot satisfy underlying physics
How?
Leverage automatic differentiation used in learning for modeling, optimization, and control
Image source: https://sciml.wur.nl/reviews/sciml/sciml.html
Karniadakis, G.E., Kevrekidis, I.G., Lu, L. et al. Physics-informed machine learning. Nat Rev Phys 3, 422–440, 2021.
Scientific Machine Learning (SciML)

## Slide 10: Selected Scientific Machine Learning Literature
Differentiable Programming
  M. Innes, et al., A Differentiable Programming System to Bridge Machine Learning and Scientific Computing, 2019
  A. Baydin, B. Pearlmutter, A. Radul, and J. Siskind, Automatic differentiation in machine learning: a survey. JMLR, 2017
Learning to Solve (L2S)
  M. Raissi, P. Perdikaris, G. E. Karniadakis, Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations, 2019
  S. Goswami, A. Bora, Y Yu, G. E. Karniadakis, Physics-informed deep neural operator networks, 2023
Learning to Optimize (L2O)
  A. Agrawal, et al., Differentiable Convex Optimization Layers, 2019
  P. Donti, et al., DC3: A learning method for optimization with hard constraints, 2021
  J. Kotary, et al., End-to-End Constrained Optimization Learning: A Survey, 2021
Learning to Model (L2M)
  B. Lusch, et al., Deep learning for universal linear embeddings of nonlinear dynamics, 2018
  R. T. Q. Chen, et al., Neural Ordinary Differential Equations, 2019
  C. Rackauckas, et al., Universal Differential Equations for Scientific Machine Learning, 2021
Learning to Control (L2C)
  B. Amos, et al., Differentiable MPC for End-to-end Planning and Control, 2019
  S. East, et al., Infinite-Horizon Differentiable Model Predictive Control, 2020
  Y Qiao, et al., Scalable Differentiable Physics for Learning and Control, 2020

## Slide 11: Components of Scientific Machine Learning
Karniadakis, G.E., Kevrekidis, I.G., Lu, L. et al. Physics-informed machine learning. Nat Rev Phys 3, 2021.
Thiyagalingam, J., Shankar, M., Fox, G. et al. Scientific machine learning benchmarks. Nature Reviews Physics 4, 413–420, 2022.
Nghiem T., Drgona J., et al. Physics-Informed Machine Learning for Modeling and Control of Dynamical Systems, ACC, 2023.

## Slide 12: Learning to Solve Differential Equations with Physics-Informed Neural Networks (PINNs)
Training neural networks as PDE solutions
Application: Parameter estimation from data
  M. Raissi, et al., Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations, Journal of Computational Physics, 2019
  Images: NVIDIA Modulus

## Slide 13: Learning to Solve Differential Equations with Physics-Informed Neural Networks (PINNs)
  M. Raissi, et al., Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations, Journal of Computational Physics, 2019
Dataset: collocation points in the spatio-temporal coordinates.
https://github.com/pnnl/neuromancer/blob/master/examples/PDEs/Part_2_PINN_BurgersEquation.ipynb
Architecture: PDE equations solved with neural network via automatic differentiation.
Loss function: minimizing PDE equation, initial and boundary condition residuals.

## Slide 14: Learning to Optimize (L2O) with Constraints
Training neural networks as optimization solutions
Application: solving optimal power flow
  James Kotary, et al., End-to-End Constrained Optimization Learning: A Survey, IJCAI, 2021

## Slide 15: Learning to Optimize (L2O) with Constraints
  A. Agrawal, et al., Differentiable Convex Optimization Layers, 2019
  P. Donti, et al., DC3: A learning method for optimization with hard constraints, 2021
Dataset: collocation points in the parametric space.
https://github.com/pnnl/neuromancer/blob/master/examples/parametric_programming/Part_1_basics.ipynb
Loss function: minimizing objective function and constraints penalties.
Architecture: differentiable optimization solver with neural network surrogate.

## Slide 16
Nonlinear system identification
  R. T. Q. Chen, et al., Neural ordinary differential equations. NeurIPS, 2018
  C. Rackauckas, et al., Universal Differential Equations for Scientific Machine Learning, 2021
  James Koch, et al., Learning Neural Differential Algebraic Equations via Operator Splitting, CDC, 2025
Applications: modeling process dynamics
Learning to Model (L2M) Dynamical Systems

## Slide 17
  R. T. Q. Chen, et al., Neural Ordinary Differential Equations, 2019
  B. Lusch, et al., Deep learning for universal linear embeddings of nonlinear dynamics, 2018
Dataset: time-series of states, inputs, and disturbances tuples.
Loss function: trajectory matching, regularizations, and constraints penalties.
Architecture: differentiable ODE solver with neural network model.
https://github.com/pnnl/neuromancer/blob/master/examples/ODEs/Part_1_NODE.ipynb
Architecture: Koopman operator with neural network basis functions.
Learning to Model (L2M) Dynamical Systems

## Slide 18: Learning to Control (L2C) Methodologies
Supervised L2C: Approximate Model Predictive Control
Self-Supervised L2C: Differentiable Predictive Control (DPC)
J. Drgoňa, A. Tuor and D. Vrabie, "Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees," in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024
Ján Drgoňa, et al, Differentiable predictive control: Deep learning alternative to explicit model predictive control for unknown nonlinear systems, Journal of Process Control, 2022
M. Hertneck, et al., "Learning an Approximate Model Predictive Controller With Guarantees," in IEEE Control Systems Letters, 2018
B. Karg and S. Lucia, "Efficient Representation and Approximation of Model Predictive Control Laws via Deep Learning," in IEEE Transactions on Cybernetics, 2020

## Slide 19: Supervised L2C: Approximate MPC
Step 1: solve set of MPC problems to generate labeled training data
Step 2: supervised imitation learning to learn approximate MPC policy
M. Hertneck, et al., "Learning an Approximate Model Predictive Controller With Guarantees," in IEEE Control Systems Letters, 2018

## Slide 20: Supervised L2C: Approximate MPC
Step 1: solve set of MPC problems to generate labeled training data
Step 2: supervised imitation learning to learn approximate MPC policy
M. Hertneck, et al., "Learning an Approximate Model Predictive Controller With Guarantees," in IEEE Control Systems Letters, 2018
Problem 1: data generation is expensive!
Problem 2: hard to integrate constraints into supervised learning.

## Slide 21: Self-Supervised L2C: Differentiable Predictive Control (DPC)
J. Drgoňa, A. Tuor and D. Vrabie, "Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees," in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024
Dataset: collocation points in the control parametric space.
Loss function: reference tracking, constraints and terminal penalties.
Architecture: differentiable model with neural network control policy.
https://github.com/pnnl/neuromancer/blob/master/examples/control/Part_3_ref_tracking_ODE.ipynb

## Slide 22: Differentiable Closed-Loop System

## Slide 23: Differentiable Closed-Loop System

## Slide 24: DPC Policy Optimization Algorithm

## Slide 25: DPC vs Model-based Reinforcement Learning
J. Drgoňa, A. Tuor and D. Vrabie, Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees, in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024
J. Drgoňa, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022
DPC is closely related to MBRL in that both leverage model of dynamics, but DPC utilizes differentiable closed-loop models and cost functions, allowing direct policy gradients without requiring a learned critic.
Empirical risk minimization problem:
Policy gradient via automatic differentiation:
Critic parametrized by differentiable MPC loss function:

## Slide 26: DPC vs Model Predictive Control
J. Drgoňa, A. Tuor and D. Vrabie, Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees, in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024
J. Drgoňa, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022
DPC is also related to explicit MPC, as it solves a parametric optimal control problem via gradient-based policy optimization.
There is a structural equivalence between single shooting formulation of MPC problem and the unrolled closed-loop system dynamics in DPC.
DPC is also closely related to MPC, but instead of single instance online optimization, the DPC learns parametric explicit policy offline, over distribution of parametric instances in batched setting.

## Slide 27: DPC vs Model Predictive Control
J. Drgoňa, A. Tuor and D. Vrabie, Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees, in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024
J. Drgoňa, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022
DPC is also related to explicit MPC, as it solves a parametric optimal control problem via gradient-based policy optimization.
There is a structural equivalence between single shooting formulation of MPC problem and the unrolled closed-loop system dynamics in DPC.
DPC is also closely related to MPC, but instead of single instance online optimization, the DPC learns parametric explicit policy offline, over distribution of parametric instances in batched setting.
So, what about safety?

## Slide 28: Learning Stable DPC Policies with Neural Lyapunov Functions
Sayak Mukherjee, Ján Drgoňa, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Neural Lyapunov Differentiable Predictive Control, Conference on Decision and Control (CDC), 2022
https://github.com/SOLARIS-JHU/Differentiable-CBDs/blob/main/example_2.py

## Slide 29: Learning Safe DPC Policies with Control Barrier Functions
Wenceslao Shaw Cortez, Ján Drgoňa, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Differentiable Predictive Control with Safety Guarantees: A Control Barrier Function Approach, Conference on Decision and Control (CDC), 2022

## Slide 30: Co-Authors of Differentiable Predictive Control with Neural Lyapunov Functions and Control Barrier Functions
Aaron Tuor
Draguna
Vrabie
Ján Drgoňa
Wenceslao Shaw Cortez
Sayak Mukherjee
Mahantesh Halappanavar

## Slide 31: Some Open Challenges
Mixed-Integer Decision Space
Modeling of Differential
Algebraic Equations (DAEs)
Control of Partial Differential Equations (PDEs)
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," under review, 2025
J. Koch, M. Shapiro, H. Sharma, D. Vrabie, J. Drgoňa, Learning Neural Differential Algebraic Equations via Operator Splitting, CDC, 2025.
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 32: Some Open Challenges
Mixed-Integer Decision Space
Modeling of Differential
Algebraic Equations (DAEs)
Control of Partial Differential Equations (PDEs)
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," under review, 2025
J. Koch, M. Shapiro, H. Sharma, D. Vrabie, J. Drgoňa, Learning Neural Differential Algebraic Equations via Operator Splitting, CDC, 2025.
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Session WeC04: Physics-Aware Learning for Planning and Control
16:30-18:30 Oceania IV

## Slide 33: Some Open Challenges
Mixed-Integer Decision Space
Modeling of Differential
Algebraic Equations (DAEs)
Control of Partial Differential Equations (PDEs)
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," under review, 2025
J. Koch, M. Shapiro, H. Sharma, D. Vrabie, J. Drgoňa, Learning Neural Differential Algebraic Equations via Operator Splitting, CDC, 2025.
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 34
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," arXiv:2511.08992, 2025
Learning to Control PDEs with DPC and Neural Operators

## Slide 35
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," arXiv:2511.08992, 2025
Time-Integrated Neural Operator (TI-DeepOnet)
⊙ denotes element-wise multiplication
is a state branch net encoding the solution field
is a control branch net encoding the control function
is a trunk net encoding the solution at the collocation points

## Slide 36
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," arXiv:2511.08992, 2025
Formulation of DPC with TI-DeepOnet

## Slide 37
Learning to Control PDEs with DPC and Neural Operators
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," arXiv:2511.08992, 2025

## Slide 38: Co-Authors of Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators
Dibakar Roy Sharkar
Somdatta Goswami
Ján Drgoňa

## Slide 39: Some Open Challenges
Mixed-Integer Decision Space
Modeling of Differential
Algebraic Equations (DAEs)
Control of Partial Differential Equations (PDEs)
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," under review, 2025
J. Koch, M. Shapiro, H. Sharma, D. Vrabie, J. Drgoňa, Learning Neural Differential Algebraic Equations via Operator Splitting, CDC, 2025.
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 40: Challenges of Existing Learning to Optimize Methods
1. Collecting Solutions as Training Labels for Supervised Learning is Very Expensive
2. Neural Networks Cannot Directly Output Integer Values
Our Solution: Self-Supervised Learning Approach without requiring solutions for training.
Our Solution: Differentiable Integer Correction Layers to ensure integer feasibility.
Our Solution: Gradient-based Feasibility Projection to guarantee feasible integer solutions.
3. It is Difficult to Ensure Feasibility, Especially in Integers
  Selected Existing L2O methods Ferdinando Fioretto, et al., Predicting ac optimal power flows: Combining deep learning and lagrangian dual methods. AAAI conference on AI, 2020.
  Priya Donti, et al., DC3: A learning method for optimization with hard constraints, ICLR, 2021
  James Kotary, et al., End-to-end constrained optimization learning: A survey. arXiv preprint arXiv:2103.16378, 2021.
  He He, et al., Learning to search in branch and bound algorithms. NeurIPS, 2014.
  Elias Khalil, et al., Learning to branch in mixed integer programming. AAAI Conference on AI, 2016.
  Maxime Gasse, et al., Exact combinatorial optimization with graph convolutional neural networks. NeruIPS, 2019.
  Timo Berthold , et al., Learning to scale mixed-integer programs. AAAI Conference on AI, 2021.
  Yoshua Bengio, et al., Machine learning for combinatorial optimization: a methodological tour d’horizon. European Journal of Operational Research, 2021.
  Dimitris Bertsimas and Bartolomeo Stellato. Online mixed-integer optimization in milliseconds. INFORMS Journal on Computing, 2022.

## Slide 41: Learning to Optimize for Mixed-Integer Nonlinear Programming
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning problem formulation:
Penalty loss function reformulation:
Amortized optimization allows scaling to some of the largest MINLPs.
Could also be used as primal heuristics.

## Slide 42: Learning to Optimize for Mixed-Integer Nonlinear Programming
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning problem formulation:
Penalty loss function reformulation:
Parameters influence the objective and constraints of the optimization problem. We sample a set of problems from a distribution.

## Slide 43: Learning to Optimize for Mixed-Integer Nonlinear Programming
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning problem formulation:
Penalty loss function reformulation:
We aim to predict the solution with machine learning model with inputs and weights

## Slide 44: Learning to Optimize for Mixed-Integer Nonlinear Programming
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning problem formulation:
Penalty loss function reformulation:
Until now this is standard self-supervised L2O for continuous problems.

## Slide 45: Learning to Optimize for Mixed-Integer Nonlinear Programming
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning problem formulation:
Penalty loss function reformulation:
Main innovation of the paper: Integer correction layers and integer feasibility projection

## Slide 46: Differentiable Integer Correction Layers
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learnable end-to-end extension of the Relaxation Enforced Neighborhood Search (RENS).

## Slide 47: Differentiable Integer Correction Layers: RC Example
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 48: Integer Feasibility Projection
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning-based alternative to Feasibility Pump which also alternates between rounding and projection.

## Slide 49: Approximate Feasibility Guarantees for Integer Projection
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 50: L2O for MINLP: Comparison with SOTA Solvers
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Exact solvers such as Gurobi and SCIP can find better solutions over time but are slow. In contrast, our methods achieve high-quality feasible solutions within milliseconds. Our methods provide up to 5 orders of magnitude speedup.
https://github.com/pnnl/L2O-pMINLP

## Slide 51: Effect of Penalty Weights and Integer Projections on Feasibility
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Our approach achieves comparable or better feasible solutions compared to exact solvers.
https://github.com/pnnl/L2O-pMINLP

## Slide 52: Co-Authors of Learning to Optimize for Mixed-Integer Non-Linear Programming
Ján Drgoňa
Associate Professor
Department of Civil and Systems
Johns Hopkins University
Bo Tang
PhD Candidate
Department of Mechanical & Industrial Engineering
University of Toronto
Elias B. Khalil
Assistant Professor
Department of Mechanical & Industrial Engineering
University of Toronto

## Slide 53
Ján Boldocký, Shahriar Dadras Javan, Martin Gulan, Martin Mönnigmann, Ján Drgoňa, "Learning to Solve Parametric Mixed-Integer Optimal Control Problems via Differentiable Predictive Control," arXiv:2506.19646, 2025
Mixed-Integer Differentiable Predictive Control

## Slide 54: Co-Authors of Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators
Ján Drgoňa
Martin Mönnigmann
Martin Gulan
Shahriar Dadras Javan
Ján Boldocký

## Slide 55: Summary
Scientific machine learning (SciML) methods integrating deep learning, constrained optimization, physics-based modeling, and control
  Learning to solve (L2S)
  Learning to optimize (L2O)
  Learning to model (L2M)
  Learning to control (L2C)
Challenges
  Mixed-integer equality constraints
  Gradients ill conditioning for deep graphs
  Offline pre-training vs online adaptation
  Computational cost of guarantees
Opportunities
  Large-scale systems
  PDE optimization and control
  Development of new software tools
SciML Course
  https://github.com/drgona/SciML-Course
drgona.github.io/
jdrgona1@jh.edu

## Slide 56: NeuroMANCER Scientific Machine Learning Library
github.com/pnnl/neuromancer
Open-source library in PyTorch
Physics-informed Neural Networks
Learning to optimize
Neural differential equations
Learning to control

## Slide 57: NeuroMANCER Team
Aaron Tuor
Draguna
Vrabie
James Koch
Madelyn Shapiro
Rahul
Birmiwal
Bruno
Jacob
Ján Drgoňa

## Slide 58: NeuroMANCER Scientific Machine Learning Library
import neuromancer as nm
p = nm.variable(‘p’)
x = nm.variable(‘x’)
y = nm.variable('y’)
obj = ((1-x)**2 + p*(y-x**2)**2).minimize(weight=1.0, name='obj’) c1 = (p/2)**2 <= x**2 + y**2
c2 = x**2 + y**2 <= p**2
c3 = x >= y net = nm.MLP(insize=2, outsize=2, hsizes=[80]*4) map = nm.Node(net, input_keys=['p’], output_keys=[‘x’,‘y’])
loss = nm.PenaltyLoss([obj], [c1, c2, c3]) problem = nm.Problem([map], loss)
optimizer = torch.optim.AdamW(problem.parameters()) trainer = nm.Trainer(problem,data,optimizer)
best_model = trainer.train()
2. Python code interface
1. Mathematical formulation
4. Results
3. Problem graph
map

## Slide 59: Learning to Control Building Energy System
  J. Drgona, et al., Physics-constrained deep learning of multi-zone building thermal dynamics, Energy and Buildings, 2021
  J. Drgona, et al., Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, IFAC NMPC 2021
Benefits of Scientific Machine Learning
Modeling and optimal control design is roughly 10-times faster and requires less expertise.
Real-time decisions are made orders of magnitude faster than traditional model-based approaches.

## Slide 60: Learning to Control Power System
Ethan King, et al., Koopman-based Differentiable Predictive Control for the Dynamics-Aware Economic Dispatch Problem, American Control Conference 2022
Benefits of Scientific Machine Learning
Fast prototyping by re-using code template from building control project.
Real-time decisions are made orders of magnitude faster than traditional model-based approaches.

## Slide 61: Asymptotic Guarantees of Integer Feasibility Projection
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 62: Non-Asymptotic Guarantees of Integer Feasibility Projection
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 63: Non-Asymptotic Guarantees of Integer Feasibility Projection
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 64: Effect of Penalty Weight
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Integer feasibility projection (RC-P and LT-P), improves feasibility even with smaller penalty weights. Without projection there is a trade-off between feasibility and objective values (RC and LT).

## Slide 65: Benchmark Methods
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Method | Description
EX (Exact Solver) | Solves problems exactly using traditional solver with 1000-sec time-limit as a benchmark.
N1 (Root Node Solution) | Finds the first feasible solution from the root node of the solver, combining various heuristics.
RC (Rounding Classification) | A neural network-based correction layer that learns a classification to determine how to round each integer variable.
LT (Learnable Thresholding) | A neural network-based correction layer that learns a threshold value to decide to round up or down for each integer variable.
RC-P (RC + Feasibility Projection) | RC combined with feasibility projection, which corrects infeasibilities while preserving integer constraints.
LT-P (LT + Feasibility Projection) | LT combined with feasibility projection, which corrects infeasibilities while preserving integer constraints.

## Slide 66: L2O for MINLP: Empirical Evaluation
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Method | RC |  |  |  | RC-P |  |  |  | LT |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
100×100 | -13.54 | -13.6 | 96% | 0.0022 | -13.54 | -13.57 | 100% | 0.005 | -13.65 | -13.77 | 93% | 0.0023
200×200 | -31.62 | -31.71 | 97% | 0.0021 | -31.62 | -31.71 | 100% | 0.005 | -31.34 | -31.61 | 95% | 0.0022
500×500 | -73.31 | -73.38 | 86% | 0.0025 | -73.31 | -73.38 | 100% | 0.0065 | -72.36 | -72.48 | 94% | 0.0026
1000×1000 | -142.7 | -142.7 | 82% | 0.0042 | -142.7 | -142.7 | 100% | 0.009 | -142.6 | -142.6 | 100% | 0.0047
Method | LT-P |  |  |  | EX |  |  |  | N1 |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
100×100 | -13.65 | -13.77 | 100% | 0.01 | -20.79 | -20.78 | 100% | 1237 | 1.5E+18 | 1.4E+18 | 100% | 104.2
200×200 | -31.34 | -31.61 | 100% | 0.0064 | - | - | - | - | - | - | - | -
500×500 | -72.36 | -72.48 | 100% | 0.0063 | - | - | - | - | - | - | - | -
1000×1000 | -142.6 | -142.6 | 100% | 0.0086 | - | - | - | - | - | - | - | -
Integer Quadratic Problems (IQPs). Each problem size is evaluated on a test set of 100 instance.

## Slide 67: L2O for MINLP: Empirical Evaluation
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Integer Non-convex Problems (INPs). Each problem size is evaluated on a test set of 100 instance.
Method | RC |  |  |  | RC-P |  |  |  | LT |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
100×100 | 1.664 | 1.594 | 100% | 0.0022 | 1.664 | 1.594 | 100% | 0.0060 | 0.669 | 0.649 | 96% | 0.0021
200×200 | 1.472 | 1.436 | 99% | 0.0022 | 1.471 | 1.436 | 100% | 0.0054 | -0.356 | -0.373 | 100% | 0.0023
500×500 | 0.526 | 0.526 | 96% | 0.0029 | 0.524 | 0.526 | 100% | 0.0061 | -1.374 | -1.594 | 98% | 0.0029
1000×1000 | 1.423 | 0.809 | 97% | 0.0040 | 1.423 | 0.809 | 100% | 0.0115 | -3.744 | -3.716 | 99% | 0.0050
Method | LT-P |  |  |  | EX |  |  |  | N1 |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
100×100 | 0.669 | 0.649 | 100% | 0.0058 | 256.93 | 134.62 | 14% | 1001 | 4411 | 155.2 | 14% | 940.4
200×200 | -0.356 | -0.373 | 100% | 0.0056 | - | - | - | - | - | - | - | -
500×500 | -1.374 | -1.594 | 100% | 0.0072 | - | - | - | - | - | - | - | -
1000×1000 | -3.744 | -3.716 | 100% | 0.0117 | - | - | - | - | - | - | - | -

## Slide 68: L2O for MINLP: Empirical Evaluation
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Mixed-integer Rosenbrock Problems (MIRBs). Each problem size is evaluated on a test set of 100 instance.
Method | RC |  |  |  | RC-P |  |  |  | LT |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
20×4 | 59.39 | 48.86 | 100% | 0.0019 | 59.39 | 48.86 | 100% | 0.0048 | 62.51 | 63.40 | 100% | 0.0020
200×4 | 503.5 | 461.7 | 99% | 0.0021 | 504.2 | 461.7 | 100% | 0.0052 | 622.8 | 626.0 | 100% | 0.0026
50×4 | 5938 | 5792 | 99% | 0.0033 | 5942 | 5792 | 100% | 0.0070 | 5612 | 5558 | 97% | 0.0030
1000×4 | 6.7E+4 | 6.7E+4 | 76% | 0.0121 | 9.8E+4 | 7.3E+4 | 100% | 0.0824 | 4.8E+4 | 3.5E+4 | 66% | 0.0127
Method | LT-P |  |  |  | EX |  |  |  | N1 |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
20×4 | 62.51 | 63.40 | 100% | 0.0055 | 64.67 | 59.16 | 100% | 1005 | 87.83 | 77.34 | 100% | 0.0813
200×4 | 622.8 | 626.0 | 100% | 0.0062 | 8.4E+5 | 908.8 | 100% | 1002 | 3.7E+8 | 957.4 | 100% | 0.2608
2000×4 | 5615 | 5558 | 100% | 0.0071 | 4.7E+10 | 9262 | 96% | 1002 | 8.3E+12 | 9379 | 95% | 71.91
20000×4 | 8.0E+4 | 4.5E+4 | 100% | 0.0639 | 1.1E+15 | 1.0E5 | 78% | 1040 | 1.2E+15 | 1.0E5 | 78% | 782.1

## Slide 69: Metric Learning to Accelerate Convergence of Operator Splitting Methods
Douglas-Rachford splitting (DR) algorithm:
Parametric programming setting:
Ethan King, James Kotary, Ferdinando Fioretto, Jan Drgona, Metric Learning to Accelerate Convergence of Operator Splitting Methods for Differentiable Parametric Programming, Under review for CDC 2024.
Idea: Train neural network to optimize the metric as a function of problem parameters:
We can accelerate convergence of DR and ADMM algorithms via end-to-end metric learning.

## Slide 70: Metric Learning is a Form of Active Set Prediction
Ethan King, James Kotary, Ferdinando Fioretto, Jan Drgona, Metric Learning to Accelerate Convergence of Operator Splitting Methods for Differentiable Parametric Programming, Under review for CDC 2024.

## Slide 71: TODO: change this slide to be motivating and more flashy
J. Koch, M. Shapiro, H. Sharma, D. Vrabie, J. Drgona, Learning Neural Differential Algebraic Equations via Operator Splitting, arXiv:2403.12938, 2024.
DAE parameter estimation problem:
The Picard–Lindelöf theorem (also called the Cauchy–Lipschitz theorem) gives sufficient conditions under which an initial value problem (IVP) for an ordinary differential equation (ODE) has a unique solution.
Assumptions:
𝑓 is continuous in both 𝑡 and 𝑥
𝑓 is Lipschitz continuous in 𝑥 on some neighborhood of initial conditions
[30] K. E. Brenan, S. L. Campbell, and L. R. Petzold, Numerical Solution of Initial-Value Problems in Differential-Algebraic Equations. SIAM, 1996.
https://github.com/pnnl/NeuralDAEs

## Slide 72: Networked Dynamical Systems via Universal Differential Equations (UDEs)
Network of unknown oscillators
Coupling adjacency
Ground truth Kuramoto system:
Generalization of learned dynamics on never-seen network topology.
  James Koch, et al., Structural Inference of Networked Dynamical Systems with Universal Differential Equations, Chaos: An interdisciplinary Journal of Nonlinear Science, doi.org/10.1063/5.0109093, 2023