## Slide 1: Scientific Machine Learning for Modeling and Control of Data Centers
Ján Drgoňa
Associate Professor Civil and Systems Engineering Department The Ralph O'Connor Sustainable Energy Institute (ROSEI)
Data Science and AI Institute (DSAI)

## Slide 2: Optimizing Complex Energy Systems is Hard
Simulations are crucial for optimal decision-making in complex energy systems
Need: Improve computational efficiency and scalability of digital twins and optimization-based decision-making
Challenges:
  Modeling and simulation of complex systems is hard
  Closed-loop control of complex systems is hard-er
  Scientific computing and machine learning tools are fragmented and not easily composable

## Slide 3: Example: Optimal Control of Building Energy Systems
Drgona J., et al., Cloud-based implementation of white-box model predictive control for a GEOTABS office building: a field test demonstration. Journal of Process Control, 2020.
Motivation
Buildings today contribute to approximately 40% of the global energy use.
Existing control solutions governing building energy systems are very inefficient.

## Slide 4: Example: Optimal Control of Building Energy Systems
Upside
Heat pump energy savings up to 53%.
Improvement of thermal comfort up to 37%.
Drgona J., et al., Cloud-based implementation of white-box model predictive control for a GEOTABS office building: a field test demonstration. Journal of Process Control, 2020.

## Slide 5: Example: Optimal Control of Building Energy Systems
Upside
Heat pump energy savings up to 53%.
Improvement of thermal comfort up to 37%.
Drgona J., et al., Cloud-based implementation of white-box model predictive control for a GEOTABS office building: a field test demonstration. Journal of Process Control, 2020.
Downside
Project duration: 1 year.
Expertise required: 6 staff with advanced engineering degree.

## Slide 6: Challenge 1: Heterogenous Modeling Methods
Data-driven
Physics-based
More domain knowledge
Less domain knowledge
White-box models
Gray-box models
Black-box models

## Slide 7: Challenge 2: Heterogenous Solution Methods
Constrained Optimization
Differential Equations
Supervised Learning
Requires prior knowledge of objective function and constraints
Requires prior knowledge of the physics to be modeled
Requires large labeled datasets
Reinforcement Learning
Requires environment model to sample
Less domain knowledge
More domain knowledge

## Slide 8: Challenge 3: Heterogenous Solution Tools
Constrained Optimization
Differential Equations
Supervised Learning
Reinforcement Learning
More domain knowledge
Less domain knowledge

## Slide 9: Automatic Differentiation (AD) in Machine Learning
Baydin, Atilim Gunes et al. Automatic differentiation in machine learning: a survey. Journal of Machine Learning Research, 2015
Animation source: wikipedia
Gradient Descent Algorithm
Backpropagation Algorithm
AD enables efficient and accurate gradient computation, which is fundamental for training complex ML models using GPUs.
SW and HW Innovations

## Slide 10
What?
SciML systematically integrates ML methods with mathematical models and algorithms developed in various scientific and engineering domains
Why?
Scientific applications are governed by fundamental principles and physical constraints
Purely data-driven “black box” ML methods cannot satisfy underlying physics
How?
Leverage automatic differentiation used in learning for modeling, optimization, and control
Image source: https://sciml.wur.nl/reviews/sciml/sciml.html
Karniadakis, G.E., Kevrekidis, I.G., Lu, L. et al. Physics-informed machine learning. Nat Rev Phys 3, 422–440, 2021.
Scientific Machine Learning (SciML)

## Slide 11: Components of Scientific Machine Learning
Karniadakis, G.E., Kevrekidis, I.G., Lu, L. et al. Physics-informed machine learning. Nat Rev Phys 3, 2021.
Thiyagalingam, J., Shankar, M., Fox, G. et al. Scientific machine learning benchmarks. Nature Reviews Physics 4, 413–420, 2022.
Nghiem T., Drgona J., et al. Physics-Informed Machine Learning for Modeling and Control of Dynamical Systems, ACC, 2023.

## Slide 12: Learning to Solve Differential Equations with Physics-Informed Neural Networks (PINNs)
Training neural networks as PDE solutions
Application: Parameter estimation from data
  M. Raissi, et al., Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations, Journal of Computational Physics, 2019
  Images: NVIDIA Modulus

## Slide 13: Learning to Solve Differential Equations with Physics-Informed Neural Networks (PINNs)
  M. Raissi, et al., Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations, Journal of Computational Physics, 2019
Dataset: collocation points in the spatio-temporal coordinates.
https://github.com/pnnl/neuromancer/blob/master/examples/PDEs/Part_2_PINN_BurgersEquation.ipynb
Architecture: PDE equations solved with neural network via automatic differentiation.
Loss function: minimizing PDE equation, initial and boundary condition residuals.

## Slide 14: Learning to Optimize (L2O) with Constraints
Training neural networks as optimization solutions
Application: solving optimal power flow
  James Kotary, et al., End-to-End Constrained Optimization Learning: A Survey, IJCAI, 2021

## Slide 15: Learning to Optimize (L2O) with Constraints
  A. Agrawal, et al., Differentiable Convex Optimization Layers, 2019
  P. Donti, et al., DC3: A learning method for optimization with hard constraints, 2021
Dataset: collocation points in the parametric space.
https://github.com/pnnl/neuromancer/blob/master/examples/parametric_programming/Part_1_basics.ipynb
Loss function: minimizing objective function and constraints penalties.
Architecture: differentiable optimization solver with neural network surrogate.

## Slide 16: Learning to Model (L2M) Dynamical Systems
Nonlinear system identification
  R. T. Q. Chen, et al., Neural ordinary differential equations. NeurIPS, 2018
  C. Rackauckas, et al., Universal Differential Equations for Scientific Machine Learning, 2021
  James Koch, et al., Learning Neural Differential Algebraic Equations via Operator Splitting, CDC, 2025
Applications: modeling process dynamics

## Slide 17: Learning to Model (L2M) Dynamical Systems
  R. T. Q. Chen, et al., Neural Ordinary Differential Equations, 2019
  B. Lusch, et al., Deep learning for universal linear embeddings of nonlinear dynamics, 2018
Dataset: time-series of states, inputs, and disturbances tuples.
Loss function: trajectory matching, regularizations, and constraints penalties.
Architecture: differentiable ODE solver with neural network model.
https://github.com/pnnl/neuromancer/blob/master/examples/ODEs/Part_1_NODE.ipynb
Architecture: Koopman operator with neural network basis functions.

## Slide 18: Learning to Control (L2C) via Differentiable Predictive Control (DPC)
Application: autonomous systems
Trajectory optimization for dynamical systems
J. Drgoňa, A. Tuor and D. Vrabie, "Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees," in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024

## Slide 19: Learning to Control (L2C) via Differentiable Predictive Control (DPC)
J. Drgoňa, A. Tuor and D. Vrabie, "Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees," in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024
Dataset: collocation points in the control parametric space.
Loss function: reference tracking, constraints and terminal penalties.
Architecture: differentiable model with neural network control policy.
https://github.com/pnnl/neuromancer/blob/master/examples/control/Part_3_ref_tracking_ODE.ipynb

## Slide 20: NeuroMANCER Scientific Machine Learning Library
github.com/pnnl/neuromancer
Open-source library in PyTorch
Physics-informed Neural Networks
Learning to optimize
Neural differential equations
Learning to control

## Slide 21: NeuroMANCER Scientific Machine Learning Library
import neuromancer as nm
p = nm.variable(‘p’)
x = nm.variable(‘x’)
y = nm.variable('y’)
obj = ((1-x)**2 + p*(y-x**2)**2).minimize(weight=1.0, name='obj’) c1 = (p/2)**2 <= x**2 + y**2
c2 = x**2 + y**2 <= p**2
c3 = x >= y net = nm.MLP(insize=2, outsize=2, hsizes=[80]*4) map = nm.Node(net, input_keys=['p’], output_keys=[‘x’,‘y’])
loss = nm.PenaltyLoss([obj], [c1, c2, c3]) problem = nm.Problem([map], loss)
optimizer = torch.optim.AdamW(problem.parameters()) trainer = nm.Trainer(problem,data,optimizer)
best_model = trainer.train()
2. Python code interface
1. Mathematical formulation
4. Results
3. Problem graph
map

## Slide 22: Learning to Control Heating Ventilation and Air Conditioning (HVAC) Systems
  J. Drgona, et al., Physics-constrained deep learning of multi-zone building thermal dynamics, Energy and Buildings, 2021
  J. Drgona, et al., Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, IFAC NMPC 2021
Benefits of Scientific Machine Learning
Modeling and optimal control design is roughly 10-times faster and requires less expertise.
Real-time decisions are made orders of magnitude faster than traditional model-based approaches.

## Slide 23: Remaining Challenges in Data Center Modeling and Control
  Image from: https://www.csemag.com/using-fluid-technology-to-address-cooling-limitations-in-data-centers/
High-fidelity digital twins of data centers require:
Scalable control-oriented surrogates to partial differential equations (PDEs)
Multi-physics and multi-scale modeling
Adaptive data-driven modeling
Handling energy and mass conservation laws
Optimal control of data centers require:
Handling of multi-objective tradeoffs such as grid-responsive and compute-aware objectives
Constraints satisfaction for safety and performance guarantees
Handling uncertainty and operational variability
Mixed-integer action spaces

## Slide 24: Summary
Scientific machine learning (SciML) methods integrating deep learning, constrained optimization, physics-based modeling, and control
  Learning to solve (L2S)
  Learning to optimize (L2O)
  Learning to model (L2M)
  Learning to control (L2C)
Challenges
  Mixed-integer equality constraints
  Gradients ill conditioning for deep graphs
  Offline pre-training vs online adaptation
  Computational cost of guarantees
Opportunities
  Large-scale modeling, design, and control of data center operations
  PDE optimization and control
  Development of new software tools
drgona.github.io/
jdrgona1@jh.edu