## Slide 1: Scientific Machine Learning for Modeling, Optimization, and Control
Ján Drgoňa
Associate Professor @ CaSE & ROSEI

## Slide 2: Optimizing Complex Energy Systems is Hard
Simulations are crucial for optimal decision-making in complex energy systems
Need: Improve computational efficiency and scalability of digital twins
Challenges:
  Modeling and simulation of complex systems is hard
  Optimal control and closed-loop decision-making for complex systems is hard-er
  Scientific computing and machine learning tools are fragmented and not easily composable

## Slide 3: Existing Decision-Making Approaches
Model-based Optimal Control
Learning-based Optimal Control
Drgona J., et al. "All You Need to Know About Model Predictive Control for Buildings." Annual Reviews in Control, September 29, 2020
G. Dulac-Arnold, D. J. Mankowitz, and T. Hester, “Challenges of real-world reinforcement learning,”, 2019.
More domain knowledge
Less domain knowledge

## Slide 4: Example: Model-based Optimal Control of Building Energy Systems
Drgona J., et al., Cloud-based implementation of white-box model predictive control for a GEOTABS office building: a field test demonstration. Journal of Process Control, 2020.
Motivation
Buildings today contribute to approximately 40% of the global energy use.
Existing control solutions governing building energy systems are very inefficient.

## Slide 5: Example: Model-based Optimal Control of Building Energy Systems
Upside
Heat pump energy savings up to 53%.
Improvement of thermal comfort up to 37%.
Drgona J., et al., Cloud-based implementation of white-box model predictive control for a GEOTABS office building: a field test demonstration. Journal of Process Control, 2020.

## Slide 6: Example: Model-based Optimal Control of Building Energy Systems
Upside
Heat pump energy savings up to 53%.
Improvement of thermal comfort up to 37%.
Drgona J., et al., Cloud-based implementation of white-box model predictive control for a GEOTABS office building: a field test demonstration. Journal of Process Control, 2020.
Downside
Project duration: 1 year.
Expertise required: 6 staff with advanced engineering degree.

## Slide 7: Challenge 1: Heterogenous Modeling Methods
Data-driven
Physics-based
More domain knowledge
Less domain knowledge
White-box models
Gray-box models
Black-box models

## Slide 8: Challenge 2: Heterogenous Solution Methods
Constrained Optimization
Differential Equations
Supervised Learning
Requires prior knowledge of objective function and constraints
Requires prior knowledge of the physics to be modeled
Requires large labeled datasets
Reinforcement Learning
Requires environment model to sample
More domain knowledge
Less domain knowledge

## Slide 9: Challenge 3: Heterogenous Solution Tools
Constrained Optimization
Differential Equations
Supervised Learning
Reinforcement Learning
More domain knowledge
Less domain knowledge

## Slide 10: Scientific Machine Learning (SciML)
What?
SciML systematically integrates ML methods with mathematical models and algorithms developed in various scientific and engineering domains
Why?
Scientific applications are governed by fundamental principles and physical constraints
Purely data-driven “black box” ML methods cannot satisfy underlying physics
How?
Leverage automatic differentiation used in learning for modeling, optimization, and control
Image source: https://sciml.wur.nl/reviews/sciml/sciml.html
Karniadakis, G.E., Kevrekidis, I.G., Lu, L. et al. Physics-informed machine learning. Nat Rev Phys 3, 422–440, 2021.

## Slide 11: Automatic Differentiation in Machine Learning
Baydin, Atilim Gunes et al. Automatic differentiation in machine learning: a survey. Journal of Machine Learning Research, 2015
Animation source: wikipedia
Gradient descent
algorithm
Forward and Backward propagation
through computational graph

## Slide 12: Selected Scientific Machine Learning Literature
Differentiable Programming
  M. Innes, et al., A Differentiable Programming System to Bridge Machine Learning and Scientific Computing, 2019
Learning to Solve (L2S)
  M. Raissi, et al., Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations, 2019
Learning to Optimize (L2O)
  A. Agrawal, et al., Differentiable Convex Optimization Layers, 2019
  P. Donti, et al., DC3: A learning method for optimization with hard constraints, 2021
  J. Kotary, et al., End-to-End Constrained Optimization Learning: A Survey, 2021
Learning to Model (L2M)
  B. Lusch, et al., Deep learning for universal linear embeddings of nonlinear dynamics, 2018
  R. T. Q. Chen, et al., Neural Ordinary Differential Equations, 2019
  C. Rackauckas, et al., Universal Differential Equations for Scientific Machine Learning, 2021
Learning to Control (L2C)
  B. Amos, et al., Differentiable MPC for End-to-end Planning and Control, 2019
  S. East, et al., Infinite-Horizon Differentiable Model Predictive Control, 2020
  Y Qiao, et al., Scalable Differentiable Physics for Learning and Control, 2020

## Slide 13: Components of Scientific Machine Learning
Karniadakis, G.E., Kevrekidis, I.G., Lu, L. et al. Physics-informed machine learning. Nat Rev Phys 3, 2021.
Thiyagalingam, J., Shankar, M., Fox, G. et al. Scientific machine learning benchmarks. Nature Reviews Physics 4, 413–420, 2022.
Nghiem T., Drgona J., et al. Physics-Informed Machine Learning for Modeling and Control of Dynamical Systems, ACC, 2023.

## Slide 14: Learning to Solve Differential Equations with Physics-Informed Neural Networks (PINNs)
Training neural networks as PDE solutions
Application: Parameter estimation from data
  M. Raissi, et al., Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations, Journal of Computational Physics, 2019
  Images: NVIDIA Modulus

## Slide 15: Learning to Solve Differential Equations with Physics-Informed Neural Networks (PINNs)
  M. Raissi, et al., Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations, Journal of Computational Physics, 2019
Dataset: collocation points in the spatio-temporal coordinates.
https://github.com/pnnl/neuromancer/blob/master/examples/PDEs/Part_2_PINN_BurgersEquation.ipynb
Architecture: PDE equations solved with neural network via automatic differentiation.
Loss function: minimizing PDE equation, initial and boundary condition residuals.

## Slide 16: Learning to Optimize (L2O) with Constraints
Training neural networks as optimization solutions
Application: solving optimal power flow
  James Kotary, et al., End-to-End Constrained Optimization Learning: A Survey, IJCAI, 2021

## Slide 17: Learning to Optimize (L2O) with Constraints
  A. Agrawal, et al., Differentiable Convex Optimization Layers, 2019
  P. Donti, et al., DC3: A learning method for optimization with hard constraints, 2021
Dataset: collocation points in the parametric space.
https://github.com/pnnl/neuromancer/blob/master/examples/parametric_programming/Part_1_basics.ipynb
Loss function: minimizing objective function and constraints penalties.
Architecture: differentiable optimization solver with neural network surrogate.

## Slide 18: Learning to Model (L2M) Dynamical Systems
Neural models for nonlinear system identification
Application: climate modeling
  R. T. Q. Chen, et al., Neural ordinary differential equations. NeurIPS, 2018
  C. Rackauckas, et al., Universal Differential Equations for Scientific Machine Learning, 2021
  Image: NVIDIA FourCastNet

## Slide 19: Learning to Model (L2M) Dynamical Systems
  R. T. Q. Chen, et al., Neural Ordinary Differential Equations, 2019
  B. Lusch, et al., Deep learning for universal linear embeddings of nonlinear dynamics, 2018
Dataset: time-series of states, inputs, and disturbances tuples.
Loss function: trajectory matching, regularizations, and constraints penalties.
Architecture: differentiable ODE solver with neural network model.
https://github.com/pnnl/neuromancer/blob/master/examples/ODEs/Part_1_NODE.ipynb
Architecture: Koopman operator with neural network basis functions.

## Slide 20: Learning to Control (L2C) with Differentiable System Models
Trajectory optimization for dynamical systems
Application: autonomous systems
J. Drgoňa, A. Tuor and D. Vrabie, "Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees," in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024

## Slide 21: Learning to Control (L2C) with Differentiable System Models
Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022
Dataset: collocation points in the control parametric space.
Loss function: reference tracking, constraints and terminal penalties.
Architecture: differentiable model with neural network control policy.
https://github.com/pnnl/neuromancer/blob/master/examples/control/Part_3_ref_tracking_ODE.ipynb

## Slide 22: NeuroMANCER Scientific Machine Learning Library
github.com/pnnl/neuromancer
Open-source library in PyTorch
Physics-informed Neural Networks
Learning to optimize
Neural differential equations
Learning to control

## Slide 23: NeuroMANCER Scientific Machine Learning Library
import neuromancer as nm
p = nm.variable(‘p’)
x = nm.variable(‘x’)
y = nm.variable('y’)
obj = ((1-x)**2 + p*(y-x**2)**2).minimize(weight=1.0, name='obj’) c1 = (p/2)**2 <= x**2 + y**2
c2 = x**2 + y**2 <= p**2
c3 = x >= y net = nm.MLP(insize=2, outsize=2, hsizes=[80]*4) map = nm.Node(net, input_keys=['p’], output_keys=[‘x’,‘y’])
loss = nm.PenaltyLoss([obj], [c1, c2, c3]) problem = nm.Problem([map], loss)
optimizer = torch.optim.AdamW(problem.parameters()) trainer = nm.Trainer(problem,data,optimizer)
best_model = trainer.train()
2. Python code interface
1. Mathematical formulation
4. Results
3. Problem graph
map

## Slide 24: Learning to Control Building Energy System
  J. Drgona, et al., Physics-constrained deep learning of multi-zone building thermal dynamics, Energy and Buildings, 2021
  J. Drgona, et al., Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, IFAC NMPC 2021
Benefits of Scientific Machine Learning-based Digital Twins
Modeling and optimal control design is roughly 10-times faster and requires less expertise.
Real-time decisions are made orders of magnitude faster than traditional model-based approaches.

## Slide 25: Learning to Control Power System
Ethan King, et al., Koopman-based Differentiable Predictive Control for the Dynamics-Aware Economic Dispatch Problem, American Control Conference 2022
Benefits of Scientific Machine Learning-based Digital Twins
Fast prototyping by re-using code template from building control project.
Real-time decisions are made orders of magnitude faster than traditional model-based approaches.

## Slide 26: Summary
Scientific machine learning (SciML) methods integrating deep learning, constrained optimization, physics-based modeling, and control
  Learning to optimize (L2O)
  Learning to control (L2C)
  Learning to model (L2M)
  Learning to solve (L2S)
Energy systems applications
  Buildings
  Power systems
  Wind farms
  Energy storage
  Transportation networks
drgona.github.io
jdrgona1@jh.edu

## Slide 27: Acknowledgements
James Koch
Bruno Jacob
Draguna Vrabie
Aaron Tuor
Ethan King
Rahul Birmiwal
Soumya Vasisht
Wenceslao Shaw Cortez
Sayak Mukherjee
Mahantesh Halappanavar
Shrirang Abhyankar
Madelyn Shapiro
Panos Stinis
Sonja Glavaski

## Slide 28: Metric Learning to Accelerate Convergence of Operator Splitting Methods
Douglas-Rachford splitting (DR) algorithm:
Parametric programming setting:
Ethan King, James Kotary, Ferdinando Fioretto, Jan Drgona, Metric Learning to Accelerate Convergence of Operator Splitting Methods for Differentiable Parametric Programming, Under review for CDC 2024.
Idea: Train neural network to optimize the metric as a function of problem parameters:
We can accelerate convergence of DR and ADMM algorithms via end-to-end metric learning.

## Slide 29: Metric Learning is a Form of Active Set Prediction
Ethan King, James Kotary, Ferdinando Fioretto, Jan Drgona, Metric Learning to Accelerate Convergence of Operator Splitting Methods for Differentiable Parametric Programming, Under review for CDC 2024.

## Slide 30: Neural Differential Algebraic Equations
Time stepper architecture is inspired by Lie-Trotter operator splitting method:
Trained with physics-informed loss function:
J. Koch, M. Shapiro, H. Sharma, D. Vrabie, J. Drgona, Neural Differential Algebraic Equations, arXiv:2403.12938, 2024.
Inverse modeling, robustness to noise and, out of distribution generalization.

## Slide 31: Networked Dynamical Systems via Universal Differential Equations (UDEs)
Network of unknown oscillators
Coupling adjacency
Ground truth Kuramoto system:
Generalization of learned dynamics on never-seen network topology.
  James Koch, et al., Structural Inference of Networked Dynamical Systems with Universal Differential Equations, Chaos: An interdisciplinary Journal of Nonlinear Science, doi.org/10.1063/5.0109093, 2023

## Slide 32: Learning Stable Policies with Neural Lyapunov Functions
Sayak Mukherjee, Ján Drgoňa, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Neural Lyapunov Differentiable Predictive Control, Conference on Decision and Control (CDC), 2022

## Slide 33: Learning Safe Policies with Control Barrier Functions
Wenceslao Shaw Cortez, et al., Differentiable Predictive Control with Safety Guarantees: A Control Barrier Function Approach, Conference on Decision and Control (CDC), 2022

## Slide 34: Differentiable Parametric Programming: Generalization of Physics-informed Neural Networks
Problem formulation:

## Slide 35: Differentiable Parametric Programming: Generalization of Physics-informed Neural Networks
Objective function
Constraints
Scenarios
Parameters
Solution map
Primal optimizers
Problem formulation:

## Slide 36: Differentiable Parametric Programming: Generalization of Physics-informed Neural Networks
Objective function
Constraints
Scenarios
Parameters
Solution map
Primal optimizers
Problem formulation:
Lagrangian form:
Constraints penalties
Gradient-based optimization