## Slide 1: Scientific Machine Learning for Modeling, Optimization, and Control
Ján Drgoňa
Associate Professor Civil and Systems Engineering Department Electrical and Computer Engineering Department (secondary) The Ralph O'Connor Sustainable Energy Institute (ROSEI)
Data Science and AI Institute (DSAI)

## Slide 2: Optimizing Complex Systems is Hard
Simulations are crucial for optimal decision-making in complex energy systems
Need: Improve computational efficiency and scalability of digital twins and optimization-based decision-making
Challenges:
  Modeling and simulation of complex systems is hard
  Closed-loop decision-making for complex systems is hard-er
  Scientific computing and machine learning tools are fragmented and not easily composable
  Safety guarantees are critical

## Slide 3: Challenge: Heterogenous Software Tools
Constrained Optimization
Differential Equations
Supervised Learning
Reinforcement Learning
More domain knowledge
Less domain knowledge

## Slide 4: Automatic Differentiation (AD) in Machine Learning
Baydin, Atilim Gunes et al. Automatic differentiation in machine learning: a survey. Journal of Machine Learning Research, 2015
Animation source: wikipedia
Gradient Descent Algorithm
Backpropagation Algorithm
AD enables efficient computation of derivatives for differentiable programs, which is fundamental for training complex ML models using GPUs.
SW and HW Innovations

## Slide 5
What?
SciML systematically integrates ML methods with mathematical models and algorithms developed in various scientific and engineering domains
Why?
Scientific applications are governed by fundamental principles and physical constraints
Purely data-driven “black box” ML methods cannot satisfy underlying physics
How?
Leverage automatic differentiation used in learning for modeling, optimization, and control
Image source: https://sciml.wur.nl/reviews/sciml/sciml.html
Karniadakis, G.E., Kevrekidis, I.G., Lu, L. et al. Physics-informed machine learning. Nat Rev Phys 3, 422–440, 2021.
Scientific Machine Learning (SciML)

## Slide 6: Components of Scientific Machine Learning
Karniadakis, G.E., Kevrekidis, I.G., Lu, L. et al. Physics-informed machine learning. Nat Rev Phys 3, 2021.
Thiyagalingam, J., Shankar, M., Fox, G. et al. Scientific machine learning benchmarks. Nature Reviews Physics 4, 413–420, 2022.
Nghiem T., Drgona J., et al. Physics-Informed Machine Learning for Modeling and Control of Dynamical Systems, ACC, 2023.

## Slide 7: Learning to Solve Differential Equations with Physics-Informed Neural Networks (PINNs)
Training neural networks as PDE solutions
Application: Parameter estimation from data
  M. Raissi, et al., Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations, Journal of Computational Physics, 2019
  Images: NVIDIA Modulus

## Slide 8: Learning to Solve Differential Equations with Physics-Informed Neural Networks (PINNs)
  M. Raissi, et al., Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations, Journal of Computational Physics, 2019
Dataset: collocation points in the spatio-temporal coordinates.
https://github.com/pnnl/neuromancer/blob/master/examples/PDEs/Part_2_PINN_BurgersEquation.ipynb
Architecture: PDE equations solved with neural network via automatic differentiation.
Loss function: minimizing PDE equation, initial and boundary condition residuals.

## Slide 9: Learning to Optimize (L2O) with Constraints
Training neural networks as optimization solutions
Application: solving optimal power flow
  James Kotary, et al., End-to-End Constrained Optimization Learning: A Survey, IJCAI, 2021

## Slide 10: Learning to Optimize (L2O) with Constraints
  A. Agrawal, et al., Differentiable Convex Optimization Layers, 2019
  P. Donti, et al., DC3: A learning method for optimization with hard constraints, 2021
Dataset: collocation points in the parametric space.
https://github.com/pnnl/neuromancer/blob/master/examples/parametric_programming/Part_1_basics.ipynb
Loss function: minimizing objective function and constraints penalties.
Architecture: differentiable optimization solver with neural network surrogate.

## Slide 11
Nonlinear system identification
  R. T. Q. Chen, et al., Neural ordinary differential equations. NeurIPS, 2018
  C. Rackauckas, et al., Universal Differential Equations for Scientific Machine Learning, 2021
  James Koch, et al., Learning Neural Differential Algebraic Equations via Operator Splitting, CDC, 2025
Applications: modeling process dynamics
Learning to Model (L2M) Dynamical Systems

## Slide 12
  R. T. Q. Chen, et al., Neural Ordinary Differential Equations, 2019
  Milan Korda, Igor Mezić, Linear predictors for nonlinear dynamical systems: Koopman operator meets model predictive control, Automatica, 2018
Dataset: time-series of states, inputs, and disturbances tuples.
Loss function: trajectory matching, regularizations, and constraints penalties.
Architecture: differentiable ODE solver with neural network model.
https://github.com/pnnl/neuromancer/blob/master/examples/ODEs/Part_1_NODE.ipynb
Architecture: Koopman operator with learned basis functions.
Learning to Model (L2M) Dynamical Systems

## Slide 13: Learning to Control (L2C) Methodologies
Supervised L2C: Approximate Model Predictive Control
Self-Supervised L2C: Differentiable Predictive Control (DPC)
J. Drgoňa, A. Tuor and D. Vrabie, "Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees," in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024
Ján Drgoňa, et al, Differentiable predictive control: Deep learning alternative to explicit model predictive control for unknown nonlinear systems, Journal of Process Control, 2022
M. Hertneck, et al., "Learning an Approximate Model Predictive Controller With Guarantees," in IEEE Control Systems Letters, 2018
B. Karg and S. Lucia, "Efficient Representation and Approximation of Model Predictive Control Laws via Deep Learning," in IEEE Transactions on Cybernetics, 2020

## Slide 14: Self-Supervised L2C: Differentiable Predictive Control (DPC)
J. Drgoňa, A. Tuor and D. Vrabie, "Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees," in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024
Dataset: collocation points in the control parametric space.
Loss function: reference tracking, constraints and terminal penalties.
Architecture: differentiable model with neural network control policy.
https://github.com/pnnl/neuromancer/blob/master/examples/control/Part_3_ref_tracking_ODE.ipynb

## Slide 15: Differentiable Closed-Loop System

## Slide 16: Differentiable Closed-Loop System

## Slide 17: DPC Policy Optimization Algorithm

## Slide 18: DPC vs Model-based Reinforcement Learning
J. Drgoňa, A. Tuor and D. Vrabie, Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees, in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024
J. Drgoňa, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022
DPC is closely related to MBRL in that both leverage model of dynamics, but DPC utilizes differentiable closed-loop models and cost functions, allowing direct policy gradients without requiring a learned critic.
Empirical risk minimization problem:
Policy gradient via automatic differentiation:
Critic parametrized by differentiable MPC loss function:

## Slide 19: DPC vs Model Predictive Control
J. Drgoňa, A. Tuor and D. Vrabie, Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees, in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024
J. Drgoňa, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022
DPC is also related to explicit MPC, as it solves a parametric optimal control problem via gradient-based policy optimization.
There is a structural equivalence between single shooting formulation of MPC problem and the unrolled closed-loop system dynamics in DPC.
DPC is also closely related to MPC, but instead of single instance online optimization, the DPC learns parametric explicit policy offline, over distribution of parametric instances in batched setting.

## Slide 20: NeuroMANCER Scientific Machine Learning Library
github.com/pnnl/neuromancer
Open-source library in PyTorch
Physics-informed Neural Networks
Learning to optimize
Neural differential equations
Learning to control

## Slide 21: NeuroMANCER Team
Aaron Tuor
Draguna
Vrabie
James Koch
Madelyn Shapiro
Rahul
Birmiwal
Bruno
Jacob
Ján Drgoňa

## Slide 22: Some Open Challenges
Mixed-Integer Decision Space
Modeling of Differential
Algebraic Equations (DAEs)
Control of Partial Differential Equations (PDEs)
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," under review, 2025
J. Koch, M. Shapiro, H. Sharma, D. Vrabie, J. Drgoňa, Learning Neural Differential Algebraic Equations via Operator Splitting, CDC, 2025.
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 23: Some Open Challenges
Mixed-Integer Decision Space
Modeling of Differential
Algebraic Equations (DAEs)
Control of Partial Differential Equations (PDEs)
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," under review, 2025
J. Koch, M. Shapiro, H. Sharma, D. Vrabie, J. Drgoňa, Learning Neural Differential Algebraic Equations via Operator Splitting, CDC, 2025.
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 24: Neural Differential Algebraic Equations (NDAEs) Problem Formulation
DAE parameter estimation problem
The Picard–Lindelöf theorem (also called the Cauchy–Lipschitz theorem) gives sufficient conditions under which an initial value problem (IVP) for an ordinary differential equation (ODE) has a unique solution.
Assumptions:
𝑓 is continuous in its arguments
𝑓 is Lipschitz continuous in 𝑥 on some neighborhood of initial conditions
constraints g are nonsingular
[30] K. E. Brenan, S. L. Campbell, and L. R. Petzold, Numerical Solution of Initial-Value Problems in Differential-Algebraic Equations. SIAM, 1996.

## Slide 25: Learning Neural Differential Algebraic Equations via Operator Splitting
Our neural DAE time stepper architecture is inspired by operator splitting methods for ODEs:
J. Koch, M. Shapiro, H. Sharma, D. Vrabie, J. Drgona, Learning Neural Differential Algebraic Equations via Operator Splitting, arXiv:2403.12938, 2024.
Lie-Trotter splitting scheme for ODEs:
Operator splitting for DAEs:
Neural DAE learning problem:
Picard-Lindelof Theorem for index-1 DAEs.

## Slide 26: Tank-Manifold Pump Modeling Problem
J. Koch, M. Shapiro, H. Sharma, D. Vrabie, J. Drgona, Learning Neural Differential Algebraic Equations via Operator Splitting, arXiv:2403.12938, 2024.
DAE inverse modeling, with satisfied conservation laws.
Tank-manifold pump schematics
DAE with unknown components:
Neural DAE:
drgona.github.io/NeuralDAEs/

## Slide 27: Co-Authors of Learning Neural Differential Algebraic Equations via Operator Splitting
Draguna
Vrabie
James Koch
Madelyn Shapiro
Himanshu
Sharma
Ján Drgoňa

## Slide 28: Some Open Challenges
Mixed-Integer Decision Space
Modeling of Differential
Algebraic Equations (DAEs)
Control of Partial Differential Equations (PDEs)
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," under review, 2025
J. Koch, M. Shapiro, H. Sharma, D. Vrabie, J. Drgoňa, Learning Neural Differential Algebraic Equations via Operator Splitting, CDC, 2025.
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 29
P. Zanotta, H. Zheng, D. R. Sharkar, S. Goswami, J. Drgoňa, Cardinality-Invariant Neural Operator Policies for Scalable PDE Control, under review, 2026, https://github.com/SOLARIS-JHU/Multi-Agent-DPC
Cardinality-Invariant Neural Operator Policies for Multi-Agent PDE Control

## Slide 30
P. Zanotta, H. Zheng, D. R. Sharkar, S. Goswami, J. Drgoňa, Cardinality-Invariant Neural Operator Policies for Scalable PDE Control, under review, 2026, https://github.com/SOLARIS-JHU/Multi-Agent-DPC
Multi-agent PDE Control Problem
Time-dependent PDE operator
Actuator ODE dynamics
Sensor operator
Parametric control functional
Shared neural operator policy
Constraints

## Slide 31
P. Zanotta, H. Zheng, D. R. Sharkar, S. Goswami, J. Drgoňa, Cardinality-Invariant Neural Operator Policies for Scalable PDE Control, under review, 2026, https://github.com/SOLARIS-JHU/Multi-Agent-DPC
PDE Control as Self-Supervised Neural Operator Learning
We learn the multi-agent policy operator using differentiable predictive control algorithm with differentiable PDE solvers.

## Slide 32
P. Zanotta, H. Zheng, D. R. Sharkar, S. Goswami, J. Drgoňa, Cardinality-Invariant Neural Operator Policies for Scalable PDE Control, under review, 2026, https://github.com/SOLARIS-JHU/Multi-Agent-DPC
Empirical Results: Stabilization of 2D Kuramoto-Sivashinsky Chaos

## Slide 33
P. Zanotta, H. Zheng, D. R. Sharkar, S. Goswami, J. Drgoňa, Cardinality-Invariant Neural Operator Policies for Scalable PDE Control, under review, 2026, https://github.com/SOLARIS-JHU/Multi-Agent-DPC
Empirical Results: Multi-agent Heat Control with Spatial Constraints

## Slide 34
P. Zanotta, H. Zheng, D. R. Sharkar, S. Goswami, J. Drgoňa, Cardinality-Invariant Neural Operator Policies for Scalable PDE Control, under review, 2026, https://github.com/SOLARIS-JHU/Multi-Agent-DPC
Empirical Results: Density Transport in Advection-Diffusion

## Slide 35
P. Zanotta, H. Zheng, D. R. Sharkar, S. Goswami, J. Drgoňa, Cardinality-Invariant Neural Operator Policies for Scalable PDE Control, under review, 2026, https://github.com/SOLARIS-JHU/Multi-Agent-DPC
Empirical Results: Solver Fidelity Robustness
The policy, trained on a coarse discretization of 64 × 64 (Top), is deployed zero-shot on a high-fidelity solver with 512 × 512 grid points (Bottom).

## Slide 36
P. Zanotta, H. Zheng, D. R. Sharkar, S. Goswami, J. Drgoňa, Cardinality-Invariant Neural Operator Policies for Scalable PDE Control, under review, 2026, https://github.com/SOLARIS-JHU/Multi-Agent-DPC
Cardinality Invariance Across Diverse PDE Benchmarks

## Slide 37
P. Zanotta, H. Zheng, D. R. Sharkar, S. Goswami, J. Drgoňa, Cardinality-Invariant Neural Operator Policies for Scalable PDE Control, under review, 2026, https://github.com/SOLARIS-JHU/Multi-Agent-DPC
Mean-Field Gradient Consistency
We train a shared neural operator policy on a finite swarm of size ,
but deploy it zero-shot on different swarm sizes. Key questions:
Does finite- training optimize the true continuous control problem?
Why does the policy transfer across cardinalities without knowing ?
We observe that training on a finite swarm asymptotically optimizes the continuous PDE control operator, not a particular agent configuration. Hence cardinality becomes a resolution parameter.
Our primary theoretical result establishes that the gradients computed during our discrete multi-agent training are consistent estimators of the gradients for this continuous limit.

## Slide 38
P. Zanotta, H. Zheng, D. R. Sharkar, S. Goswami, J. Drgoňa, Cardinality-Invariant Neural Operator Policies for Scalable PDE Control, under review, 2026, https://github.com/SOLARIS-JHU/Multi-Agent-DPC
Mean-Field Gradient Consistency
Proof sketch: Proof relies on the discrete physics uniformly approximates the mean-field physics.
Uniform bounds: PDE states and adjoints remain uniformly bounded in suitable function space regardless of M, preventing blow-ups as agents are added.
Compactness and convergence: Using the Aubin-Lions lemma, we extract strongly convergent subsequences of the state trajectories, showing that the discrete dynamics converge to a unique mean-field limit.
Gradient Identification: We decompose the gradient error into a state-dependent term and a measure dependent term. We show both vanish in the limit, proving that optimizing the swarm is asymptotically equivalent to optimizing the continuous operator.

## Slide 39: Co-Authors of Cardinality-Invariant Neural Operator Policies for Scalable PDE Control
Dibakar Roy
Sharkar
Somdatta
Goswami
Ján Drgoňa
Honghui
Zheng
Pietro
Zanotta

## Slide 40: Some Open Challenges
Mixed-Integer Decision Space
Modeling of Differential
Algebraic Equations (DAEs)
Control of Partial Differential Equations (PDEs)
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," under review, 2025
J. Koch, M. Shapiro, H. Sharma, D. Vrabie, J. Drgoňa, Learning Neural Differential Algebraic Equations via Operator Splitting, CDC, 2025.
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 41: Challenges of Existing Learning to Optimize Methods
1. Collecting Solutions as Training Labels for Supervised Learning is Very Expensive
2. Neural Networks Cannot Directly Output Integer Values
Our Solution: Self-Supervised Learning Approach without requiring solutions for training.
Our Solution: Differentiable Integer Correction Layers to ensure integer feasibility.
Our Solution: Gradient-based Feasibility Projection to guarantee feasible integer solutions.
3. It is Difficult to Ensure Feasibility, Especially in Integers
  Selected Existing L2O methods Ferdinando Fioretto, et al., Predicting ac optimal power flows: Combining deep learning and lagrangian dual methods. AAAI conference on AI, 2020.
  Priya Donti, et al., DC3: A learning method for optimization with hard constraints, ICLR, 2021
  James Kotary, et al., End-to-end constrained optimization learning: A survey. arXiv preprint arXiv:2103.16378, 2021.
  He He, et al., Learning to search in branch and bound algorithms. NeurIPS, 2014.
  Elias Khalil, et al., Learning to branch in mixed integer programming. AAAI Conference on AI, 2016.
  Maxime Gasse, et al., Exact combinatorial optimization with graph convolutional neural networks. NeruIPS, 2019.
  Timo Berthold , et al., Learning to scale mixed-integer programs. AAAI Conference on AI, 2021.
  Yoshua Bengio, et al., Machine learning for combinatorial optimization: a methodological tour d’horizon. European Journal of Operational Research, 2021.
  Dimitris Bertsimas and Bartolomeo Stellato. Online mixed-integer optimization in milliseconds. INFORMS Journal on Computing, 2022.

## Slide 42: Learning to Optimize for Mixed-Integer Nonlinear Programming
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning problem formulation:
Penalty loss function reformulation:
Amortized optimization allows scaling to some of the largest MINLPs.
Could also be used as primal heuristics.

## Slide 43: Learning to Optimize for Mixed-Integer Nonlinear Programming
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning problem formulation:
Penalty loss function reformulation:
Parameters influence the objective and constraints of the optimization problem. We sample a set of problems from a distribution.

## Slide 44: Learning to Optimize for Mixed-Integer Nonlinear Programming
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning problem formulation:
Penalty loss function reformulation:
We aim to predict the solution with machine learning model with inputs and weights

## Slide 45: Learning to Optimize for Mixed-Integer Nonlinear Programming
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning problem formulation:
Penalty loss function reformulation:
Until now this is standard self-supervised L2O for continuous problems.

## Slide 46: Learning to Optimize for Mixed-Integer Nonlinear Programming
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning problem formulation:
Penalty loss function reformulation:
Main innovation of the paper: Integer correction layers and integer feasibility projection

## Slide 47: Differentiable Integer Correction Layers
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learnable end-to-end extension of the Relaxation Enforced Neighborhood Search (RENS).

## Slide 48: Differentiable Integer Correction Layers: RC Example
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 49: Integer Feasibility Projection
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Learning-based alternative to Feasibility Pump which also alternates between rounding and projection.

## Slide 50: Approximate Feasibility Guarantees for Integer Projection
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 51: L2O for MINLP: Comparison with SOTA Solvers
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Exact solvers such as Gurobi and SCIP can find better solutions over time but are slow. In contrast, our methods achieve high-quality feasible solutions within milliseconds. Our methods provide up to 5 orders of magnitude speedup.
https://github.com/pnnl/L2O-pMINLP

## Slide 52: Effect of Penalty Weights and Integer Projections on Feasibility
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Our approach achieves comparable or better feasible solutions compared to exact solvers.
https://github.com/pnnl/L2O-pMINLP

## Slide 53: Co-Authors of Learning to Optimize for Mixed-Integer Non-Linear Programming
Ján Drgoňa
Associate Professor
Department of Civil and Systems
Johns Hopkins University
Bo Tang
PhD Candidate
Department of Mechanical & Industrial Engineering
University of Toronto
Elias B. Khalil
Assistant Professor
Department of Mechanical & Industrial Engineering
University of Toronto

## Slide 54
Fast MPC algorithms:
[*] L. Wu, et. al., “πMPC: A Parallel-in-horizon and Construction-free NMPC Solver”, under review by IEEE TAC.
[2] L. Wu, et. al., “Koopman-BoxQP: solving large-scale NMPC problems at kHZ Rate”, accepted by L4DC 2026.
[3] L. Wu and A. Bemporad, “A Simple and Fast Coordinate-Descent Augmented-Lagrangian Solver for Model Predictive Control” IEEE TAC, 2023.
Address the open challenge in MPC: Execution time certificate
[4] L. Wu and R.D. Braatz, “A Direct Optimization Algorithm for Input-Constrained MPC”, in IEEE TAC, 2025.
[5] L. Wu and R.D. Braatz, “A Quadratic Programming Algorithm with Time Complexity”, in IEEE TAC (in press).
[6] L. Wu, et. al., “EIQP: Execution-time-certified and Infeasibility-detecting QP Solver", in IEEE TAC, 2025
[7] L. Wu, et. al., “A Time-certified Predictor-corrector IPM Algorithm for Box-QP”, in IEEE Control Systems Letters, 2025.
Control
[8] L. Wu, et. al., “Arbitrarily Small Execution-Time Certificate: what was missed in Analog Optimization”, in IEEE TAC, 2025.
[*] L. Wu, “XCo: A Factorization-free ADMM Solver for Extreme-scale Conic Optimization”, ongoing.
[*] L. Wu, “CCQP: An Efficient Complementarity Constrained Optimization Program Solver for Mixed-Integer MPC”, ongoing.
Optimization
Analog physical system
Learning
[*] L. Wu et al., “A Least-Squares Multi-Step Koopman Operator for Model Predictive Control”, submitted to Automatica.
Learning to Model
Learning to Optimize
[*] L. Wu, “A Trustworthy and Self-supervised Online/Offline Neural Convex Optimization (and HJB) Solver”, ongoing.
[*] L. Wu, “Modern EKF Optimizer for Large-scale Deep Neural Networks”, ongoing.
Optimizer for DNN Training
Liang Wu
Education & experiences
2018-2023, PhD, IMT Lucca 2023-2025, Postdoc at MIT
2025-present, Postdoc at JHU

## Slide 55: Summary
Scientific machine learning (SciML) methods integrating deep learning, constrained optimization, physics-based modeling, and control
  Learning to solve (L2S)
  Learning to optimize (L2O)
  Learning to model (L2M)
  Learning to control (L2C)
Challenges
  Mixed-integer equality constraints
  Gradients ill conditioning for deep graphs
  Offline pre-training vs online adaptation
  Computational cost of guarantees
Opportunities
  PDE optimization and control via Geometric Neural Operators (GNO) and Koopman Operators (KO)
  Development of new software tools
SciML Course
  https://github.com/drgona/SciML-Course
drgona.github.io/
jdrgona1@jh.edu

## Slide 56
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," arXiv:2511.08992, 2025
Learning to Control PDEs with DPC and Neural Operators

## Slide 57
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," arXiv:2511.08992, 2025
Time-Integrated Neural Operator (TI-DeepOnet)
⊙ denotes element-wise multiplication
is a state branch net encoding the state field
is a control branch net encoding the control function
is a trunk net encoding the solution at the collocation points
TI-DeepOnet: PDE surrogate based on method-of-lines spatial discretization

## Slide 58
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," arXiv:2511.08992, 2025
Formulation of DPC with TI-DeepOnet
Discretize then optimize reformulation of the PDE control problem:

## Slide 59
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," arXiv:2511.08992, 2025
Training Algorithms for TI-DeepOnet and DPC
JAX implementation: https://github.com/Centrum-IntelliPhysics/PDEControl_DPC

## Slide 60
Learning to Control PDEs with DPC and Neural Operators
D. R. Sharkar, J. Drgoňa, S. Goswami, "Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators," arXiv:2511.08992, 2025
Heat equation tracking control
Fisher-KPP population density control

## Slide 61: Co-Authors of Learning to Control PDEs with Differentiable Predictive Control and Time-Integrated Neural Operators
Dibakar Roy Sharkar
Somdatta Goswami
Ján Drgoňa

## Slide 62
Ján Boldocký, Shahriar Dadras Javan, Martin Gulan, Martin Mönnigmann, Ján Drgoňa, "Learning to Solve Parametric Mixed-Integer Optimal Control Problems via Differentiable Predictive Control," arXiv:2506.19646, 2025
Mixed-Integer Differentiable Predictive Control

## Slide 63: Co-Authors of Mixed-Integer Differentiable Predictive Control
Ján Drgoňa
Martin Mönnigmann
Martin Gulan
Shahriar Dadras Javan
Ján Boldocký

## Slide 64: Learning to Control Building Energy System
  J. Drgona, et al., Physics-constrained deep learning of multi-zone building thermal dynamics, Energy and Buildings, 2021
  J. Drgona, et al., Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, IFAC NMPC 2021
Benefits of Scientific Machine Learning
Modeling and optimal control design is roughly 10-times faster and requires less expertise.
Real-time decisions are made orders of magnitude faster than traditional model-based approaches.

## Slide 65: Learning to Control Power System
Ethan King, et al., Koopman-based Differentiable Predictive Control for the Dynamics-Aware Economic Dispatch Problem, American Control Conference 2022
Benefits of Scientific Machine Learning
Fast prototyping by re-using code template from building control project.
Real-time decisions are made orders of magnitude faster than traditional model-based approaches.

## Slide 66: Asymptotic Guarantees of Integer Feasibility Projection
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 67: Non-Asymptotic Guarantees of Integer Feasibility Projection
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 68: Non-Asymptotic Guarantees of Integer Feasibility Projection
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024

## Slide 69: Effect of Penalty Weight
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Integer feasibility projection (RC-P and LT-P), improves feasibility even with smaller penalty weights. Without projection there is a trade-off between feasibility and objective values (RC and LT).

## Slide 70: Benchmark Methods
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Method | Description
EX (Exact Solver) | Solves problems exactly using traditional solver with 1000-sec time-limit as a benchmark.
N1 (Root Node Solution) | Finds the first feasible solution from the root node of the solver, combining various heuristics.
RC (Rounding Classification) | A neural network-based correction layer that learns a classification to determine how to round each integer variable.
LT (Learnable Thresholding) | A neural network-based correction layer that learns a threshold value to decide to round up or down for each integer variable.
RC-P (RC + Feasibility Projection) | RC combined with feasibility projection, which corrects infeasibilities while preserving integer constraints.
LT-P (LT + Feasibility Projection) | LT combined with feasibility projection, which corrects infeasibilities while preserving integer constraints.

## Slide 71: L2O for MINLP: Empirical Evaluation
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Method | RC |  |  |  | RC-P |  |  |  | LT |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
100×100 | -13.54 | -13.6 | 96% | 0.0022 | -13.54 | -13.57 | 100% | 0.005 | -13.65 | -13.77 | 93% | 0.0023
200×200 | -31.62 | -31.71 | 97% | 0.0021 | -31.62 | -31.71 | 100% | 0.005 | -31.34 | -31.61 | 95% | 0.0022
500×500 | -73.31 | -73.38 | 86% | 0.0025 | -73.31 | -73.38 | 100% | 0.0065 | -72.36 | -72.48 | 94% | 0.0026
1000×1000 | -142.7 | -142.7 | 82% | 0.0042 | -142.7 | -142.7 | 100% | 0.009 | -142.6 | -142.6 | 100% | 0.0047
Method | LT-P |  |  |  | EX |  |  |  | N1 |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
100×100 | -13.65 | -13.77 | 100% | 0.01 | -20.79 | -20.78 | 100% | 1237 | 1.5E+18 | 1.4E+18 | 100% | 104.2
200×200 | -31.34 | -31.61 | 100% | 0.0064 | - | - | - | - | - | - | - | -
500×500 | -72.36 | -72.48 | 100% | 0.0063 | - | - | - | - | - | - | - | -
1000×1000 | -142.6 | -142.6 | 100% | 0.0086 | - | - | - | - | - | - | - | -
Integer Quadratic Problems (IQPs). Each problem size is evaluated on a test set of 100 instance.

## Slide 72: L2O for MINLP: Empirical Evaluation
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Integer Non-convex Problems (INPs). Each problem size is evaluated on a test set of 100 instance.
Method | RC |  |  |  | RC-P |  |  |  | LT |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
100×100 | 1.664 | 1.594 | 100% | 0.0022 | 1.664 | 1.594 | 100% | 0.0060 | 0.669 | 0.649 | 96% | 0.0021
200×200 | 1.472 | 1.436 | 99% | 0.0022 | 1.471 | 1.436 | 100% | 0.0054 | -0.356 | -0.373 | 100% | 0.0023
500×500 | 0.526 | 0.526 | 96% | 0.0029 | 0.524 | 0.526 | 100% | 0.0061 | -1.374 | -1.594 | 98% | 0.0029
1000×1000 | 1.423 | 0.809 | 97% | 0.0040 | 1.423 | 0.809 | 100% | 0.0115 | -3.744 | -3.716 | 99% | 0.0050
Method | LT-P |  |  |  | EX |  |  |  | N1 |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
100×100 | 0.669 | 0.649 | 100% | 0.0058 | 256.93 | 134.62 | 14% | 1001 | 4411 | 155.2 | 14% | 940.4
200×200 | -0.356 | -0.373 | 100% | 0.0056 | - | - | - | - | - | - | - | -
500×500 | -1.374 | -1.594 | 100% | 0.0072 | - | - | - | - | - | - | - | -
1000×1000 | -3.744 | -3.716 | 100% | 0.0117 | - | - | - | - | - | - | - | -

## Slide 73: L2O for MINLP: Empirical Evaluation
Bo Tang, Elias B. Khalil, Ján Drgoňa, Learning to Optimize for Mixed-Integer Non-linear Programming, arXiv:2410.11061, 2024
Mixed-integer Rosenbrock Problems (MIRBs). Each problem size is evaluated on a test set of 100 instance.
Method | RC |  |  |  | RC-P |  |  |  | LT |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
20×4 | 59.39 | 48.86 | 100% | 0.0019 | 59.39 | 48.86 | 100% | 0.0048 | 62.51 | 63.40 | 100% | 0.0020
200×4 | 503.5 | 461.7 | 99% | 0.0021 | 504.2 | 461.7 | 100% | 0.0052 | 622.8 | 626.0 | 100% | 0.0026
50×4 | 5938 | 5792 | 99% | 0.0033 | 5942 | 5792 | 100% | 0.0070 | 5612 | 5558 | 97% | 0.0030
1000×4 | 6.7E+4 | 6.7E+4 | 76% | 0.0121 | 9.8E+4 | 7.3E+4 | 100% | 0.0824 | 4.8E+4 | 3.5E+4 | 66% | 0.0127
Method | LT-P |  |  |  | EX |  |  |  | N1 |  |  | 
Metric | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec) | Obj Mean | Obj Median | % Feasible | Time (Sec)
20×4 | 62.51 | 63.40 | 100% | 0.0055 | 64.67 | 59.16 | 100% | 1005 | 87.83 | 77.34 | 100% | 0.0813
200×4 | 622.8 | 626.0 | 100% | 0.0062 | 8.4E+5 | 908.8 | 100% | 1002 | 3.7E+8 | 957.4 | 100% | 0.2608
2000×4 | 5615 | 5558 | 100% | 0.0071 | 4.7E+10 | 9262 | 96% | 1002 | 8.3E+12 | 9379 | 95% | 71.91
20000×4 | 8.0E+4 | 4.5E+4 | 100% | 0.0639 | 1.1E+15 | 1.0E5 | 78% | 1040 | 1.2E+15 | 1.0E5 | 78% | 782.1

## Slide 74: Metric Learning to Accelerate Convergence of Operator Splitting Methods
Douglas-Rachford splitting (DR) algorithm:
Parametric programming setting:
Ethan King, James Kotary, Ferdinando Fioretto, Jan Drgona, Metric Learning to Accelerate Convergence of Operator Splitting Methods for Differentiable Parametric Programming, Under review for CDC 2024.
Idea: Train neural network to optimize the metric as a function of problem parameters:
We can accelerate convergence of DR and ADMM algorithms via end-to-end metric learning.

## Slide 75: Metric Learning is a Form of Active Set Prediction
Ethan King, James Kotary, Ferdinando Fioretto, Jan Drgona, Metric Learning to Accelerate Convergence of Operator Splitting Methods for Differentiable Parametric Programming, Under review for CDC 2024.

## Slide 76: TODO: change this slide to be motivating and more flashy
J. Koch, M. Shapiro, H. Sharma, D. Vrabie, J. Drgona, Learning Neural Differential Algebraic Equations via Operator Splitting, arXiv:2403.12938, 2024.
DAE parameter estimation problem:
The Picard–Lindelöf theorem (also called the Cauchy–Lipschitz theorem) gives sufficient conditions under which an initial value problem (IVP) for an ordinary differential equation (ODE) has a unique solution.
Assumptions:
𝑓 is continuous in both 𝑡 and 𝑥
𝑓 is Lipschitz continuous in 𝑥 on some neighborhood of initial conditions
[30] K. E. Brenan, S. L. Campbell, and L. R. Petzold, Numerical Solution of Initial-Value Problems in Differential-Algebraic Equations. SIAM, 1996.
https://github.com/pnnl/NeuralDAEs

## Slide 77: Networked Dynamical Systems via Universal Differential Equations (UDEs)
Network of unknown oscillators
Coupling adjacency
Ground truth Kuramoto system:
Generalization of learned dynamics on never-seen network topology.
  James Koch, et al., Structural Inference of Networked Dynamical Systems with Universal Differential Equations, Chaos: An interdisciplinary Journal of Nonlinear Science, doi.org/10.1063/5.0109093, 2023